## Slide 1: Bulk PM Use Case OSC Rel A Plugfest, December 5, 2019
Oskar Malm, Ericsson

## Slide 2: 3GPP Bulk PM Overview
Measurements are collected internally by the PM producer (PNF/VNF) during each granularity period according to configured measurement jobs
A result report is generated at the end of the period and stored locally
Bulk PM data for one or multiple granularity periods is transferred as file(s) to a management system
Granularity Period
Bulk Data Transfer
Time
Measurements
3GPP RAN measurements (defined in TS 28.552 for 5G)
Vendor-specific measurements
ORAN measurements being discussed

## Slide 3: Event-driven Bulk PM File Collection (ONAP/ORAN)
SMO (Service Management and Orchestration)
VES Collector
File Collector
PNF/VNF
File Consumer
fileReady notification
data file
2. File Collector uses protocol like FTP(ES) to retrieve the files (e g compressed XML) indicated in the notification
3. Collected files are made available to other management application and services
1. VES fileReady notification is sent with information about available files on the PNF/VNF
Processing of collected files is SMO and use case specific
As example, ONAP includes PM Mapper component that can extract measurement data from PM XML files and create internal VES events
Note: 3GPP has defined the notifyFileReady notification (28.532), mapping to VES is under discussion
O1

## Slide 4: fileReady VES Event Example
"event": {
“commonEventHeader”: { },
"notificationFields": {
"changeIdentifier": “PM_MEAS_FILES",
"changeType": “fileReady",
"arrayOfNamedHashMap": [
{ "name": "A20191129.1030+0000-1045+0000_gNB123.xml.gz", "hashMap": {
"location": "ftpes://192.168.0.101:22/rop/A20191129.1030+0000-1045+0000_gNB123.xml.gz",
"compression": "gzip",
"fileFormatType": “org.3GPP.32.435#measCollec",
"fileFormatVersion": “V10"
} },
{ "name": "A20191129.1045+0000-1100+0000_gNB123.xml.gz", "hashMap": {
"location": "ftpes://192.168.0.101:22/rop/A20191129.1045+0000-1100+0000_gNB123.xml.gz",
"compression": "gzip",
"fileFormatType": “org.3GPP.32.435#measCollec",
"fileFormatVersion": “V10"
} }
],
"notificationFieldsVersion": "2.0“
}
}
The fileReady event can include a list of available files
The PM producer can add existing files in list to improve reliability in case of lost events
The file collector will use the file name to ensure files are only collected once

## Slide 5: File Formats
3GPP has defined multiple XML file formats for bulk PM data
  TS 32.435 – previously used for e g LTE, can also be used for 5G
  TS 28.532 – new 5G format with minor changes to the XML schema
As mentioned in the O1 specification, event-driven file upload could be used in the future also for other types of data
  ONAP El Alto release already supports collection of any standard or vendor-specific file formats based on File Collector configuration