## Slide 1: OOF-PCI: Physical Cell ID (PCI) Optimization and centralized Automated Neighbor Relations (ANR) using ONAP Optimization Framework (OOF): ONAP Dublin Proof of Concept
July 24, 2019
PoC Collaborators: AT&T, Wipro, TechMahindra, highstreet technologies, Lumina Networks, Nokia, Reliance Jio, Rutgers Winlab Acknowledgments: Feedback and support from participants in ONAP OOF-PCI team calls

## Slide 2: OOF-PCI PoC Demo - Outline
OOF-SON Overview – N. K. Shankar (12)
Demo introduction - Swaminathan S, Saravanan A (5)
Demo – Krishna Moorthy (20)
Open Platform for Advanced Wireless Research East Coast – Tracy van Brakle / Ivan Seskar (3)
ONAP Component Enhancements – (10)
  DCAE / SON Handler Microservice – Swaminathan S
  RAN Simulator, Policy - Saravanan A
  SDN-R & ConfigDB – Sandeep Shah
  OOF enhancement for PCI – Vikas Varma / Carlos de Andrade
  Integration Testing – Krishna Moorthy
ONAP SON Frankfurt Plans – (5)
Conclusion – (5)

## Slide 3: ONAP-Based SON (Self Organizing Networks)
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SDN-R)
5G/4G Radio Network
SON  Control Loop (CL)
ONAP: Open-source platform, with basic open-source code
Companies can use framework to add proprietary SON solutions
OOF-PCI Casablanca –
  First ONAP SON PCI use case
  PoC Demo in Dec 2018
OOF-PCI Dublin
  Added SON function: ANR
  More SON data flows: FM, PM
  More ONAP code integration
Config status
Data, FM, PM

## Slide 4: ONAP-Based SON & ORAN interfaces
RIC (non-RT)
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SDN-R)
OOF-PCI use case has built a foundation for ONAP/ORAN integration
Radio network uses common netconf/yang model
Data flows:
SDN-R to RAN: netconf-based configuration
RAN to DCAE: VES format for FM alarms and PM KPI
RAN to SDN-R: netconf notifications for configuration changes within RAN
Config status
Data, FM, PM
A-1/O-1
A-1/O-1
RIC (near RT)
ORAN Radio Network

## Slide 5: ONAP SON Release planning
ONAP Casablanca - focus on Minimum Viable Product and PoC
Focus on data flow and interfaces for: OOF, new PCI-Handler-MS, Policy, SDN-R, new RAN-Sim
ONAP Dublin – add functionality, integrate into ONAP codebase
Fully compliant DCAE implementation
Add centralized ANR functionality to PCI, including joint optimization
Add SON flows for FM/PM data (e.g. PCI Confusion alarm, Handover KPI)
Focus on integration testing, and inclusion in ONAP Dublin release
PoC in newly upgraded Rutgers Winlab OWL
ONAP Frankfurt – deployment readiness
Alignment with ORAN/3GPP common model
PoC with SDN-R and DCAE interacting with real gNodeBs
Include other ONAP modules: A&AI, SO, SDC, CLAMP

## Slide 6: Contributors
Organization | Contributor(s) | Topic(s)/Area(s)
AT&T | N. K. Shankaranarayanan, Sarat Puthenpura, P. N. Shankaranarayanan, Carlos de Andrade, Vikas Varma, George Clapp, Tracy van Brakle, Marco Platania Pam Dragosh, Dan Timoney, Brian Freeman, Vijay Venkatesh | Use case lead & conceptualization, OOF, SDN-R, ONAP setup at Winlab; Policy, DCAE, SDN-C/SDN-R and Integration Test support
Wipro | Swaminathan S, Saravanan A, Krishna Moorthy, Reshmasree C, Ramya R, Phunith Kumar | Use case enhancements, DCAE (new SON-Handler MS), Policy, RAN-Sim, RAN-Sim GUI, Honeycomb enhancements, Integration Test Lead
Tech Mahindra | Sandeep Shah, Vineeth Agarwal, Devendra Chauhan | SDN-R, Config DB
highstreet technologies | Martin Skorupski, Herbert Eiselt, Hanif Kukkalli | ONAP setup at Winlab, SDN-R and RAN-Sim
Lumina Networks | Jeff Hartley | SDN-R support
Nokia | Ben Cheung, Ferri Tafreshi | Use case guidance and conceptualization
Reliance Jio | Dilip Krishnaswamy | Use case conceptualization
Rutgers University | Ivan Seskar, Michael Sherman, Mohit Sheth, Aayush Shah | ONAP setup at Winlab

## Slide 7: PCI and ANR optimization – 4G/5G SON functionality
Cell: C3
PCI: 2
Cell: C4
PCI: 1
Cell: C5
PCI: 4
Cell: C1
PCI: 3
Cell: C2
PCI: 8
Cell: C7
PCI: 7
Cell: C8
PCI: 6
Cell: C11
PCI: 2
Cell: C9
PCI: 5
Cell: C10
PCI: 10
Cell: C12
PCI: 1
Physical cell ID (PCI) is a locally unique integer ID in 4G/5G
  Used for handoff and physical layer design
  PCI ranges: (LTE: 0-503, 5G: 0-1007)
PCI optimization: Assign PCI values to avoid PCI collision and minimize PCI confusion
Automated Neighbor Relations (ANR) builds & maintains neighbor relation tables in eNodeB and gNodeB
  Distributed ANR in eNodeB, gNodeB
  Centralized ANR optimizes neighbor tables based on global information
PCI needs to be re-optimized if neighbor relationship changes, (e.g. during distributed ANR function in RAN)
Centralized ONAP ANR optimization is best done jointly with PCI - blacklisting neighbors from HO based on HO metrics over a period of time
PCI confusion
Cell C9 has two neighbors with PCI = 1
PCI collision
Cell C3 has a neighbor
with the same PCI=2
Graph Coloring
Problem
X
ANR action
Cell C11 is blacklisted from HO from Cell C9.

## Slide 8: ONAP Dublin PoC: PCI & ANR Optimization using OOF
DCAE
SON Handler MS
OOF
SDN-C* (SDN-R)
Policy
Simulated RAN
~2000 Cells
Nbr_list, PCI values
2
5
6
1b
1c
Config Value
Change Notifn
(Netconf/Yang)
9
1d
1a
8
10
4b
4a
Config Value
Changes
11
DMaaP Message
REST API
3a
7
ConfigDB
FM/PM KPIs
4c
DCAE Collector
(VES)
FM/PM Database
1e
4d
PCI enhancements
Add ANR function
FM/PM Collector and Database
FM/PM
Data
SDC & CL setup
3b
(*Note: Team has renamed Casablanca PCI-Handler MS as SON-Handler-MS to reflect broader role of MS)
12
13

## Slide 9: OOF-PCI Dublin Use Case / PoC Highlights
New SON optimization triggers: FM data / alarms, PM KPIs
New SON functionality - joint PCI-ANR optimization by OOF, handoff blacklist in Cell Neighbor table
New data flows - Receiving and handling FM/PM data using VES Collector in DCAE
SON-Handler MS on-boarded on DCAE and is part of ONAP Dublin distribution
SDN-R implementation integrated with CCSDK and DG requirements – includes netconf notification handling, part of ONAP El Alto distribution
SDN-R, RAN-Sim, ConfigDB designed around common netconf/yang model
New control loop for ANR in Policy, and model alignment with Dublin Policy architecture
RAN-Sim enhancements – generate/send PM/FM data, handle ANR updates, 60+ netconf servers controlling 1000 cells realized successfully
Completed Integration Tests as per ONAP process
Use case is a catalyst for, and early adopter of, upgraded Rutgers Winlab OWL – new ONAP Test lab, focused on Mobile networks, OOM-based ONAP Dublin installation

## Slide 10
Demo

## Slide 11: ONAP Dublin OOF-SON Demo : PCI & ANR Optimization
DCAE
SON Handler MS
OOF
SDN-C* (SDN-R)
Policy
Simulated RAN (GUI)
~1000 Cells
Nbr_list, PCI values
FM alarms for PCI confusion/collisions
HO KPIs
2
5
6
1b
1c
Config Value
Change Notifn
(Netconf/Yang)
9
1d
1a
8
10
4b
4a
Config Value
Changes
11
DMaaP Message
REST API
3a
7
ConfigDB
FM/PM KPIs
4c
DCAE Collector
(VES)
FM/PM Database
1e
4d
PCI enhancements
Add ANR function
FM/PM Collector and Database
SDC & CL setup
3b
(*Note: Team has renamed Casablanca PCI-Handler MS as SON-Handler-MS to reflect broader role of MS)
12
13
= DEMO Highlights

## Slide 12: Demo Sequence: Joint PCI-ANR optimization
1. Show RAN topology in UI
2. Add neighbors to a cell and show collision/confusion in UI, FM data sent from RAN-Sim
1. Show SON-Handler MS receiving info from RAN (FM->VES and netconf->SDN-R)
2. Show OOF triggered by SON-Handler MS & OOF response with optimization results
1. Show Control Loop in Policy getting activated
2. Show message flowing from Policy to SDN-R
1. Show karaf and DG logs in SDN-R
2. Show refreshed RAN-Sim GUI with problems solved.
1. Trigger PM data generation, specifying for which source cells, HO success should be bad/poor to ‘some’ of its neighbors
Step 2: RAN-Sim UI (Neighbors)
Step 3: SON-Handler MS Logs
Step 4: Policy Logs
Step 5: SDN-R and RAN-Sim UI
Step 1: RAN-Sim UI (PM)

## Slide 13: Trigger PM Generation
Specify HO from which cells should be bad/poor.
Click “Start” to open the window shown on the left
Relevant for Centralized ANR update
Relevant for joint PCI-ANR optimization

## Slide 14: Modify Neighbors - Illustration

## Slide 15: Demo Steps – Add neighbors to Cell with PCI = 5
Collision
Confusion
Original neighbors
After addition of 3 neighbors

## Slide 16: SON-Handler MS Logs (OOF trigger and acknowledgement)
Request to OOF
Ack from OOF

## Slide 17: OOF Enhancements for PCI and ANR
Enhancements in SON Optimization Solver and API:
PCI Optimization (optimizer = pci)
  Input: Set of cells, PCI values, neighbor relations
  Output: pciSolutions: Optimized PCI assignment without PCI Collision and Confusion
Joint PCI/ANR Optimization (optimizer = pci_anr)
  Input: Set of cells, PCI values, neighbor relations, removeable neighbors (neighbor links with bad handover KPI)
  Output response: pciSolutions: Optimized assignment of PCI anrSolutions: List of links to be blacklisted for handover
Code changes in SON Optimizer to adapt to new ConfigDB API

## Slide 18: OOF Log – PCI optimization results

## Slide 19: Policy Logs

## Slide 20
20
SDNR/Karaf and DG Logs (Config Phy Cell ID)

## Slide 21: YANG Model Tree for OOF PCI/ANR POC1
The platform ready to support any YANG Model
1 https://gerrit.onap.org/r/gitweb?p=ccsdk/features.git;a=tree;f=sdnr/northbound/oofpcipoc/model/src/main/yang;h=5b3ef2c03cf516ba716f69076a780a95e96fadc2;hb=refs/heads/dublin
RPC
RPC
Number & List of Cells
PCI and PNF-NAME for a Cell
List of Neigbors
Netconf Notification

## Slide 22: Demo Steps – PCI optimization completed
Before optimization
After optimization

## Slide 23: Demo Sequence: Centralized ANR Actions
1. Show RAN topology in UI
2. Initiate PM data generation, and specify which neighbors are ‘bad’
1. Show SON-Handler MS receiving PM data from RAN (via VES-Collector)
2. Show SON-Handler triggering ANR update to Policy
1. Show Control Loop in Policy getting activated
2. Show message flowing from Policy to SDN-R
1. Show netconf message from SDN-R to RAN-Sim with ANR updates
2. Show refreshed RAN-Sim GUI with problems solved.
Step 1: RAN-Sim UI
Step 2: SON-Handler MS Logs
Step 3: Policy Logs
Step 4: SDN-R, RAN-Sim UI

## Slide 24: Trigger PM Generation
Specify HO from which cells should be bad/poor.
Relevant for Centralized ANR update
(already shown earlier)

## Slide 25: SON-Handler MS Logs

## Slide 26: Policy Logs

## Slide 27
27
SDNR/Karaf and DG Logs (Neighbor Config)

## Slide 28: Centralized ANR update completed
Original list of neighbors
HO blacklisted to 2 neighbors after ANR update
HO blacklisted
to chn0001 &
Chn0000 after
centralized
ANR update

## Slide 29
ONAP Wireless Lab Installation

## Slide 30: WINLAB at Rutgers University
WINLAB Tech Center Facility
WINLAB founded in 1989 as a collaborative
industry-university research center with
specialized focus on wireless networking
~25 faculty/staff, most from the ECE and CS departments at Rutgers
~40-50 grad students (80% PhD, 20% MS)
Low Power IoT Device
ORBIT Radio Grid Testbed
CloudLab Rack
SDN
Massive MIMO
SDR
GENI Rack
Center’s research portfolio spans information theory, radio technology, wireless systems, mobile networks and computing
Extensive experimental research infrastructure including ORBIT & GENI testbeds, SDR, SDN, …
Selected as an ONAP integration and testing laboratory for North America

## Slide 31: WINLAB Designated by NSF as NJ/NYC PAWR Testbed

## Slide 32: Open Wireless Lab (OWL) at WINLAB/COSMOS
Environment
  Entry point at console located at console.sb10.orbit-lab.org
  10 Ubuntu servers, all managed by OpenStack
  Control Node: Node 1-1
  Compute Nodes: Node 2-1 through 2-9
Access Methods
  One can gain access by requesting an account at WINLAB
  https://wiki.onap.org/pages/viewpage.action?pageId=45298557

## Slide 33: Open Wireless Lab (OWL)
OpenStack Pike installation
ONAP Dublin Installation
  Three Rancher servers
  Twelve Kubernetes nodes
  One NFS server
  Two VMs hosting 10,000 NETCONF simulators

## Slide 34: OpenStack Environment
Configuration database
VMs for Rancher/Kubernetes installation of ONAP
NETCONF server simulators

## Slide 35: High Availability Rancher-Kubernetes Setup
Open source software Rancher, Helm, Kubernetes and docker are deployed in the VMs to create high-availability Rancher and Kubernetes Cluster environment.
The deployment of the ONAP components is done using ONAP helm charts from the “oom” git repository
  https://onap.readthedocs.io/en/latest/submodules/oom.git/docs/oom_setup_kubernetes_rancher.html#onap-on-kubernetes-with-rancher
High Availability Rancher/Kubernetes environment setup
  Documented at: https://wiki.onap.org/display/DW/SDN-R+on+Rancher+Kubernetes+at+WINLAB

## Slide 36: Deployed ONAP modules at WINLAB
  Currently deployed ONAP components at OWL:
    aaf
    aai
    consul
    dcaegen2
    dmaap
    log
    msb
    oof
    policy
    portal
    robot
    sdnc
    SNIRO Emulator
    so

## Slide 37: Future Considerations and References
  Goal: Three ONAP Installations
    Stable
    Developer
    Sandbox
      Short experiments, wiped and refreshed every day
    Only stable instance is currently installed
  WINLAB: http://www.winlab.rutgers.edu/
  ORBIT Lab: https://www.orbit-lab.org/
  COSMOS: https://www.cosmos-lab.org/

## Slide 38
ONAP Component Enhancements

## Slide 39: OOF-PCI Dublin Use Case: Impacts
OOF
Solver enhanced with PCI and ANR joint optimization
DCAE
(SON-Handler MS)
MS on-boarded to DCAE
Policy
New control loop for ANR updates
Config DB and SDN-R/SDN-C
RAN-Sim and GUI
Interface with SON-Handler MS enhanced to obtain ANR inputs, and provide ANR actions after optimization
PM data reception and processing for initiating autonomous ANR updates, and/or invoke OOF for joint PCI-ANR optimization
FM data reception, correlation with neighbor-list-update notification from SDN-R, and initiating PCI optimization actions
Control loop extension to wait for response from SDN-R, and forward it to SON-Handler MS
Yang model extensions to communicate ANR updates to RAN
Update Config DB on reception of neighbor-list-change notification from RAN, PCI/ANR update from Policy
OOF interface enhanced, new interface to VES-Collector, receive response from Policy
Enhancements to generate FM data on collision/confusion detection
Generation and sending of PM data periodically with GUI-based trigger
Handle ANR updates and display in GUI
Enhancements to Honeycomb agent to send PM/FM data over REST interface to VES-Collector
Config DB enhanced with HO flag, and additional APIs
New DB for FM/PM
Honeycomb footprint reduction
RPC’s/DG’s to send Netconf message to RAN simulator upon reception of DMaaP message from Policy
RPC’s/DGs to handle netconf notification from RAN, update ConfigDB, and send DMaaP message

## Slide 40
DCAE: SON-Handler MS
New MS fully on-boarded to DCAE
Functional updates for FM/PM handling and centralized ANR

## Slide 41: DCAE (with SON-Handler MS on-boarded)
DCAE Services
xNF (RAN node)
DCAE Platform
SON Handler MS
MS - n
HV-VES Collector
Datafile Collector
VES Collector
SNMP Trap Coll.
MS - 1
CBS
Deployment Handler
Service Change Handler
Policy Handler
Inventory API
Cloudify Manager
CLAMP
SDC
Policy
Consul Cluster
Consul Cluster
PG DB
OOF
Policy
SDN-R

## Slide 42: SON-Handler MS Architecture
Spring boot application
Database
Core Logic
Main thread
Child thread(s) for FM data/SDN-R notification processing
Child thread for PM data processing
DMaaP client
SDN-R
OOF
Policy
Other ONAP components
RAN nodes
REST Interface
RAN nodes
Could be a CU/DU or a traditional BS.
DB contents
Config information
Processed notifications & alarms (until OOF response is received)
Buffered notifications & alarms
State information
FM/PM processed data
Database
PostgreSQL DB
CBS
VES-C
Implementation details are available at https://wiki.onap.org/pages/viewpage.action?pageId=56131985.

## Slide 43
RAN-Simulator (RAN-Sim)
More functionality
Improved efficiency

## Slide 44: Approach for RAN Simulator (RANSim) – Dublin - FM
GUI
  Provide Control to User in UI to select a cell and modify neighbor list to simulate collision/confusion
Controller
  Send message to corresponding Netconf Server about the collision/confusion
Netconf Server
  Send configChangeNotification to SDNR
  Send FM/alarm message to VES Collector for collision/confusion. Thus the control loop starts
ONAP
VES Collector
Config DB
(MariaDB)
DCAE
SON Handler
RANSim
Controller
Web GUI
Simulated
Network
Netconf server 1
Honeycomb
Extension
Yang Model
Netconf server n
Honeycomb
Extension
Yang Models
Netconf
OOF
SDNR
Policy
REST
Websocket
REST
GUI
  Show the modified PCI values
Controller
  When the modified RAN configuration received, same is updated into DB and informed to UI
Netconf Server
  When the SDNR provides the modified RAN configuration, same is forwarded to Controller

## Slide 45: Approach for RAN Simulator (RANSim) – Dublin - PM
GUI
  Provide Control to User in UI to select a cell and generate PM data
Controller
  Send PM message to corresponding Netconf Server with KPI values. Initially send good values and after few minutes send bad values for selected cell.
Netconf Server
  Send PM message to VES Collector with given KPI values. Thus the control loop starts.
ONAP
VES Collector
Config DB
(MariaDB)
DCAE
SON Handler
RANSim
Controller
Web GUI
Simulated
Network
Netconf server 1
Honeycomb
Extension
Yang Model
Netconf server n
Honeycomb
Extension
Yang Models
Netconf
OOF
SDNR
Policy
REST
Websocket
REST
GUI
  Show the ANR updates as dotted lines.
Controller
  When the modified RAN configuration received, same is updated into DB and informed to UI
Netconf Server
  When the SDNR provides the modified RAN configuration, same is forwarded to Controller

## Slide 46
Policy
New control loop for ANR
Control loop extension

## Slide 47: Policy
RAN/
PNFs
SDN-R
DCAE (SON HandlerMS)
OOF
Policy (Drools)
Neighbor-list-change notification
Call Recipes of SDN-R
Drools controller
PCIAction:
{
controlLoopName: ControlLoop-vANR-fb41f388-a5f2-11e8-98d0-529269fb1459
timeout: 1200
abatement: false
policies:
name: modify PCI config
description:
actor: SDNR
recipe: ModifyConfig
}
PolicyConfig :
{
policyType: Config,
policyConfigType: Base,
Param1: Value1,
Param2, Value2
}
Policy GUI
Fetching of config policy
Note: DMaaP is not shown here.
Changed PCI values/ ANR updates (DMaaP notification)
Receive feedback from SDN-R
Response sent to SON-Handler MS
DCAE (VES-Collector)
FM/PM data

## Slide 48
SDN-R
ODL controller for RAN using Netconf/YANG
Control loop action
CC-SDK and DG integration

## Slide 49: SDNR Development in Support of OOF/PCI/ANR POC
YANG Model (ver1.1) - (Tree, RPC, Notification)
Create a Karaf Feature “oofpcipoc” (SDNC Docker)
Repo: CCSDK/features; Folder: features/sdnr/northbound
sdnr is a component-meta feature
Create SLI RPC’s/DG’s to support:
  Notification from RAN simulator and generate DMAAP event (3 and 4a)
  DMAAP event from Policy to initiate NETCONF based configuration towards mounted RAN simulator (10 and 11)
  Required update of JAVA provider/client classes
SDN-C Docker Build (based on CCSDK docker image)
DMAAP-Listener Docker Build
Update DMAAP-Listener Docker
Support new SDNR DMAAP topics for consumption/publishing
Netconf Mount of RAN simulator onto SDN-C platform
Leveraged existing ONAP components – CCSDK/SDN-C and DMAAP-Listener
Modified and Integrated Oofpcipoc YANG model
Leveraged DG Builder and JSON configuration templates to implement logic for Restconf transactions
Code fix for Restconf PATCH support thru DG (RFC 8072)
Open Items: Consumer/Listener code for Netconf Notification already merged; however, working to address SDNR docker stability issues
YANG Tree
DG

## Slide 50: YANG Model Tree for OOF PCI/ANR POC1
The platform ready to support any YANG Model
1 https://gerrit.onap.org/r/gitweb?p=ccsdk/features.git;a=tree;f=sdnr/northbound/oofpcipoc/model/src/main/yang;h=5b3ef2c03cf516ba716f69076a780a95e96fadc2;hb=refs/heads/dublin
RPC
RPC
Number & List of Cells
PCI and PNF-NAME for a Cell
List of Neigbors
Netconf Notification

## Slide 51
ConfigDB
New APIs
HO Blacklisted flag

## Slide 52: ConfigDB System Architecture
N
REST Interface for READ and BULK UPLOAD
(Java, Spring, Hibernate)
ONAP Components
Maria DB
Web Server
Swagger API JSON spec (Dublin)
GET /api/sdnc-config-db/v3/getCell/{cellId}
GET /api/sdnc-config-db/v3/getCellList/{networkId}/{ts}
GET /api/sdnc-config-db/v3/getNbrCellsNetwork/{networkId}
GET /api/sdnc-config-db/v3/getNbrList/{cellId}/{ts}
GET /api/sdnc-config-db/v3/getPCI/{cellId}/{ts}
GET /api/sdnc-config-db/v3/getPnfId/{cellId}/{ts}
PUT /api/sdnc-config-db/v3/createNbr/{cellId}
PATCH /api/sdnc-config-db/v3/modifyNbrHO/{cellId}/{targetCellId}
PATCH /api/sdnc-config-db/v3/modifyPci/{cellId}
PATCH /api/sdnc-config-db/v3/modifyPnfId/{cellId}
DELETE /api/sdnc-config-db/v3/deleteNbr/{cellId}/{targetCellId}
Bulk Upload API
PUT /api/sdnc-config-db/v3/insertData
Implemented to maintain configuration information of objects (e.g. cell) associated with the RAN network
CRUD operations supported for the POC (for updating ConfigDB)

## Slide 53: Config-DB Data Model and APIs
  Config DB (MariaDB) used by PCI-H-MS (step 4b) and OOF (step 7)
  Query API (swagger JSON spec) exposed to other ONAP modules
  cellId needs to be globally unique (assumed eCGI) and align with ONAP YANG model, ORAN, 3GPP
  pnf-name/pnf-id indicates netconf server to be used for interactions regarding cells
  ‘ho’ property added to support ANR use case
Attribute | Format
networkId | string
cellId | string
pciValue | uint64
nbrList | list of cellId
lastModifiedTS | timestamp
pnf-id | string
Attribute | Format
cellId | String
target_cell_id | String
ho | BIT(1)
Cell (Object)
Cell_Nbr_Info (Object)

## Slide 54
OOF
Joint PCI/ANR Optimization
Code changes for the new ConfigDB API

## Slide 55: ONAP Optimization Framework (R4)
ONAP Optimization Framework (OOF) provides a declarative, policy-driven approach for creating and running a wide variety of optimization applications like Homing/Placement, PCI optimization, etc.
API
OSDF
Policy
Dependencies on other ONAP Projects
CMSO Optimizer
CM Portal simulator
Actual policies
OOF
Policy Models
CMSO
HAS
PCI
PCI
PCI Handler MS
SON Optimizer
SDNC(R)
Route
SDNC
Route Optimizer
HAS
SO, VFC
(Homing + TD)
Homing/Placement Optimizer (HAS)
A&AI
Multi Cloud
MUSIC
FGPS
FGPS

## Slide 56: OOF Enhancements for PCI and ANR
Enhancements in SON Optimization Solver and API:
PCI Optimization (optimizer = pci)
  Input: Set of cells, PCI values, neighbor relations
  Output: pciSolutions: Optimized PCI assignment without PCI Collision and Confusion
Joint PCI/ANR Optimization (optimizer = pci_anr)
  Input: Set of cells, PCI values, neighbor relations, removeable neighbors (neighbor links with bad handover KPI)
  Output response: pciSolutions: Optimized assignment of PCI anrSolutions: List of links to be blacklisted for handover
Code changes in SON Optimizer to adapt to new ConfigDB API

## Slide 57
Integration Testing

## Slide 58: Integration Testing
TC # | Component(s) | Testcase | Status
IT#001 | DCAE (SON Handler MS) | SON Handler Micro-service successfully on-boarded on to DCAE | Completed
IT#002 | DCAE (SON Handler MS) | SON Handler Micro-service's DB is up and the Micro-service is able to read/write data. | Completed
IT#003 | DCAE (SON Handler MS) | SON Handler Micro-service is able to successfully fetch config policies from Consul. | Completed
IT#004 | OOF and Policy | OOF is able to successfully fetch config policy from Policy | Not applicable
IT#005 | DCAE (SON Handler MS) | SON Handler Micro-service is able to successfully receive a message over DMaaP containing PM/FM data (from VES Collector) | Completed
IT#006 | DCAE (SON Handler MS) and DMaaP | SON Handler Micro-service is able to successfully receive a message over DMaaP containing neighbor list update | Completed
IT#007 | DCAE (SON Handler MS) REST interface | SON Handler Micro-service is able to successfully fetch neighbor list details using REST interface (Config DB APIs) | Completed
IT#008 | DCAE (SON Handler MS) and OOF | SON Handler Micro-service invokes REST API of OOF for PCI optimization | Completed
IT#009 | OOF and Config DB (REST API) | OOF is able to obtain relevant neighbor list information for optimization algorithm from ConfigDB (REST API) | Completed
Integration Testing was done at Windriver lab.

## Slide 59: Integration Testing (continued)
TC # | Component(s) | Testcase | Status
IT#010 | DCAE (SON Handler MS) and OOF | SON Handler Micro-service receives optimization result from OOF (via callback URL) and sends response | Completed
IT#011 | DCAE (SON Handler MS) and Config DB (REST API) | SON Handler Micro-service is able to successfully fetch PNF details from Config DB (using REST API call) | Completed
IT#012 | DCAE (SON Handler MS) and Policy | SON Handler Micro-service is able to send PCI/ANR updates via DMaaP to Policy | Completed
IT#013 | Policy and DMaaP | Policy is able to successfully send a DMaaP message (to SDN-R) with PCI/neighbor list updates. | Completed
IT#014 | Policy and DMaaP | Policy is able to successfully receive a DMaaP message with PCI/neighbor list update response | Completed
IT#015 | DCAE (SON Handler MS) and Policy | SON Handler Micro-service is able to receive PCI/neighbor list update response via DMaaP from Policy, process it and logs the results. | Completed
IT#016 | DCAE (SON Handler MS) | SON Handler Micro-service is able to process PM KPI data, store as needed, and apply rules to recommend removal of a neighbor relationship. | Completed
IT#017 | SDN-R | Upon receiving message from Policy, SDN-R sends netconf message to RAN-Sim. | Not applicable
IT#018 | DCAE (VES Collector) | VES Collector receives VES messages from RAN-Simulator | Completed

## Slide 60
El Alto/Frankfurt

## Slide 61: OOF-SON El Alto/Frankfurt Plans
El Alto (Maintenance Release)
SDN-R/CC-SDK JIRA items: Complete carryover work and merge into El Alto/Frankfurt
SON-Handler MS: Handle non-functional updates (e.g., periodic config updates from Consul, container image minimization)
Frankfurt – More enhancements towards deployment readiness for ONAP SON
Include other ONAP modules: A&AI, SO, SDC, CLAMP
Alignment with ORAN/3GPP common model for SDN-R
Integrate with real systems – e.g. SDN-R controlling real gNodeB
Demonstrate alignment with Policy Control Loop Co-ordination
Establish ConfigDB role in ONAP – align with A&AI and any new models
PCI/ANR & SON Enhancements
  New cell addition, optimization features
  Incorporate support for ML-based solutions
  Additional SON functions

## Slide 62: Links for More Information
Description | Link
OOF-PCI Main Wiki Page | https://wiki.onap.org/display/DW/5G+-+OOF+%28ONAP+Optimization+Framework%29+and+PCI+%28Physical+Cell+ID%29+Optimization
OOF-PCI Dublin Release (Requirements and Test Cases) | https://wiki.onap.org/display/DW/OOF-PCI+Use+Case+-+Dublin+Release+-+ONAP+based+SON+for+PCI+and+ANR (See the child wiki pages for functional & implementation details)
OOF-PCI Dublin Release Plan | 5G - OOF and PCI (Casablanca carry-over items)
OOF SON in R5 El Alto and R6 Frankfurt | https://wiki.onap.org/display/DW/PCI+%28SON%29+in+R5+El+Alto%2C+PCI+%28SON%29+in+R6+Frankfurt
SON-Handler MS Demo | https://wiki.onap.org/download/attachments/53249727/DCAE_Weekly_04252019_Demo-Session1.mp4?version=1&modificationDate=1556202975000&api=v2 (Latter part)
OOF-PCI Dublin PoC Demo | <Link to be added>

## Slide 63
Thank You!