## Slide 1: E2E Network Slicing: Architecture Review for Guilin
Participants: CMCC, Wipro, Huawei, AT&T, Deutsche Telecom, TIM, QCT, Amdocs, Tech Mahindra, Reliance Jio, Tencent, China Telecom
Authors: Lin Meng (CMCC), Swaminathan S (Wipro), Henry Yu (Huawei), Shankar P N (AT&T), Lu Kai (CMCC), Yaoguang Wang (Huawei), Milind Jalwadi (Tech Mahindra)
May 26, 2020
Reporters: Lin Meng (CMCC), Swaminathan S (Wipro)

## Slide 2: Overall concept

## Slide 3: 3GPP Slice Management Functions (3GPP-defined)
Management Function | Key tasks | Remarks
Communication Service Management Function (CSMF) | Responsible for translating the communication service related requirement to network slice related requirements. Communicate with Network Slice Management Function (NSMF). | 
Network Slice Management Function (NSMF) | Responsible for management and orchestration of NSI. Derive network slice subnet related requirements from network slice related requirements. Communicate with the Network Slice Subnet Management Function (NSSMF) and Communication Service Management Function. | 
Network Slice Sub-net Management Function (NSSMF) | Responsible for management and orchestration of NSSI. Communicate with the NSMF. | 

## Slide 4: Network Slicing: 3GPP Context
3GPP TS 28.530 v15.2.0
This has some implications w.r.to realization of NSSMF functionality, and is not considered for Guilin release as there is no clarity yet on the real purpose and background.
3GPP TS 28.530 v15.1.0

## Slide 5: ONAP-based Slice Management Overall Architecture Choices
NSMF (ONAP)
CSMF (ONAP)
Standard APIs
NSSMF(s)1
(ONAP)
xNFs
NSMF (ONAP)
CSMF
NSSMF(s)1
(ONAP)
xNFs
NSMF (ONAP)
CSMF
NSSMF(s)1
xNFs
NSMF (ONAP)
CSMF (ONAP)
NSSMF(s)1
xNFs
NSMF
CSMF
NSSMF(s)1
(ONAP)
xNFs
3rd party component
1
2
3
4
5
Standard APIs
Standard APIs
Standard APIs
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
Standard APIs

G release
In F release, only Scenario 4 for Core is implemented. Scenario 1 (all 3 sub-nets) & Scenario 4 for RAN and Core will be supported in G release.
Standard APIs
Standard APIs

1 Top-most NSSMF/domain-specific NSSMF – under discussion
F & G release

## Slide 6: Functional Scope for Frankfurt - Recap
CSMF
NSMF
NSSMF
U-UI, SO, OOF, EXT-API, A&AI*
CSMF Portal & workflows
5G Service create/delete
On-demand Service activate/deactivate
ONAP Northbound interface to CSMF
Support interface to external CSMF
NSMF Portal & workflows
Slice instantiate
Slice activate/deactivate
Manual NSI/NSSI selection
Manual Service Profile decomposition
3rd party NSSMF (outside ONAP)
Interface between ONAP and 3rd party (core network) NSSMF
U-UI, EXT-API, SO, OOF, A&AI*
SO, A&AI*, SO Adaptor to connect to external NSSMF
* A&AI schema changes only foreseen. There is also impact to config policies (no code changes expected in Policy component).

## Slide 7: ONAP-based Slice Management - NSI Life Cycle view
Scope for Frankfurt
(with enhancements)
Ref.: 3GPP TS 28.530
Design and pre-provision: Creation of necessary slice/slice sub-net templates.
Creation, activation, deactivation and termination of NSI, including its constituent slice sub-nets (RAN, Core and Transport).
Objective for Guilin: Demonstrate e2e slice design, creation, activation, deactivation and termination - including RAN, Core and Transport slice sub-nets. Demonstrate KPI monitoring, simple Closed Loop Control & Intelligent Slicing.
Additional scope for Guilin
Initial steps in Guilin

## Slide 8: Summary of Guilin Requirements
Category | Requirement | Content | Priority
Functional requirements | Provide a full E2E Slicing solution involving RAN, Transport and Core NSSMF, and connecting to external Core/RAN NSSMF | Support e2e slice allocation, activation, deallocation and termination in ONAP with RAN, Transport and Core slice subnets. Implement RAN and Core NSSMF within ONAP Align with CCVPN use case team & implement Transport NSSMF Interact with external Core and RAN NSSMF. Implement improvements on top of Frankfurt content for e2e network slicing | HIGH
 | KPI monitoring, Closed Loop Control and Intelligent Slicing | Service/slice KPI Monitoring by tenant/operator Simple closed loop actions for slice resource optimization based on KPI monitoring & analysis Use of AI/ML for slice KPI Guarantee | HIGH
 | Standardized interfaces | Integration with ETSI/3GPP/TMF-based APIs Make working assumptions for missing details | MEDIUM
Modeling | Model enhancements, AAI schema updates 1:1 mapping between NSI & NSSI | Model enhancements for e2e, RAN and Transport slicing 1:1 mapping between NSI and NSSI in 3GPP - We’re open to considering it. | MEDIUM
*Details of Transport NSSMF implementation and Arc review material will be reported by another requirement team “CCVPN-Transport Slicing”
* Will also start collaboration with Intent Based Network Team from this release

## Slide 9: Architecture & Functional Scope for Guilin
Notes: Improvements
EXT-API
RAN, Core, Transport
KPI monitoring, Closed Loop, Intelligent Slicing
Modeling

## Slide 10: Slice Management Functions: Supported Interfaces
CSMF
NSMF
RAN NSSMF
Transport NSSMF
Core NSSMF
TMF APIs
3GPP APIs
TSCi
3GPP APIs
3GPP APIs
O1/A1*
RAN
Transport
Core
TSCi
The interfaces shown in the picture shall apply irrespective of whether NSSMF is within ONAP or external to ONAP.
TMF APIs – TMF 641 (Service creation, activation, …), TMF 628 (Performance Monitoring)
3GPP APIs – Based on 3GPP TS 28.531 Rel. 16
TSCi – Based on IETF draft.
O1/O2/A1 – O-RAN interfaces, exact details of what shall be supported in Guilin release is covered in later slides.
Information models shall be based on 3GPP NRM (TS 28.541 Rel. 16), and relevant O-RAN specs if available.
L0/L1/L2 itf
Standard itf
* May be supported beyond Guilin release

## Slide 11: Slice Management Functions - Realization in Guilin
Notes
CSMF and NSMF shall be realized within ONAP (enhancement of Frankfurt functionality), and the NB interfaces shall be standardized using ExtAPI.
All 3 NSSMFs shall be realized within ONAP (new for Guilin).
NSSMF mapping to ONAP components:
ONAP acting as NSMF shall also interact with external RAN and Transport NSSMF using 3GPP APIs.
SO
UUI
ExtAPI
CSMF
NSMF
OOF
AAI
ONAP
SDC
Policy
SDN-C
(SDN-R)
SDN-C
CDS
C&PS
NSSMF
RAN
O1/A1*
Transport
Core
Ext. RAN NSSMF
Ext. Core NSSMF
Sub-net | ONAP components
RAN | SO, OOF, SDN-C (R)
Transport | SO, OOF, SDN-C
Core | SO, OOF, CDS
NFVO

## Slide 12: NSSMF in ONAP– Functions & Classification
Function | Description | Classification | Proposed ONAP Component(s)
NSSI Allocation | Determine if an existing NSSI can be used, or a new one is needed | Optimization | OOF (triggered by SO)
 | Determine resources to be allocated to the NSSI (for a new NSSI) (Some parts such as PCE may be part of Domain Controllers) | Optimization | OOF (triggered by SO)
 | Instantiate/scale up necessary (virtual) resources (using NFVO) | Orchestration | SO
 | Perform necessary (re) configuration (incl. NSSI stitching configs) | Configuration | Domain controllers (Note 2)
NSSI (De)Activation | (De) Activate the NSSI resources | Configuration | Domain controllers
NSSI Modification | Determination of modifications to be done | Optimization | OOF
 | Resource modification (re-allocation, scaling) | Orchestration | SO, Domain controllers
 | (Re) Configuration of resources | Configuration | Domain controllers
NSSI details exposure | Provide details of NSSI to NSMF, inventory (resources, capabilities) | Orchestration | SO, Domain controllers
NSSI Closed Loop | Perform closed loop control actions such as scaling | Orchestration | SO, Domain controllers (Note 3)
NSSI De-Allocation | Tear down the NSSI and reclaim resources used | Orchestration | SO
 | Update configurations | Configuration | Domain controllers
Notes
SO triggers the NFVO (ref. 3GPP) to perform all virtual resource allocation & orchestration actions related to an NSSI. NFVO may be slice unaware.
Domain Controllers – include SDN-C (R), VF-C, CDS (CDS may be used for the configuration of VNFs).
Some closed loop actions may be performed by SO, while some by SDN-C.
Blue Partly in Guilin scope

## Slide 13: Frankfurt Improvements
Complete UUI Integration with ExtAPI for Network Slice instantiation
Extend NB interface based on TMF 641 to cover service (de)activation, termination.
Introduce standard interface (TMF 628) for PM reporting
Implement NSI termination (and also cover NSSI termination trigger)
Implement improvements in OOF and SO  OOF interactions, for example:
  Implement call back API in SO for NST and NSI/NSSI selection
  NST selection improvements
  NSST of NST to be provided by requestor
  Fully automated NSI selection, i.e., no manual intervention (stretch goal)

## Slide 14: RAN & Transport Subnet: Interaction Scenario 1
CSMF
NSMF
RAN NSSMF
Transport NSSMF
Core NSSMF
Fronthaul subnet
Mid haul subnet
Backhaul subnet
RAN NFs Subnet
Core subnet
1a
2
1
3
1b-i
1b-ii
1b-iii
2a
3a
TS_1 is backhaul transport slice; TS_3, fronthaul; TS_4, midhaul.
TN MD (T-NSSMF) receives TS_1 from NSMF (step 2), and TS_3 and TS_4 from RAN NSSMF (step 1b-i).
TN MD then configures backhaul (2a), fronthaul (1b-ii), and midhaul (1b-iii), respectively.
TS_1
TS_3
TS_4
RAN NSSMF shall be responsible for determination of Slice Profile of FH, MH and RAN NFs.
RAN NSSMF shall be responsible for entire RAN subnet comprising FH and MH (including stitching together, CL actions, etc.)
Preferred option by O-RAN
& ONAP internal RAN NSSMF

## Slide 15: RAN & Transport Subnet: Interaction Scenario 2
CSMF
NSMF
RAN NSSMF
Transport NSSMF
Core NSSMF
Fronthaul subnet
Mid haul subnet
Backhaul subnet
RAN NFs Subnet
Core subnet
1a
2
1
3
2a-ii
2a-iii
2a-i
3a
TS_1 is backhaul transport slice; TS_3, fronthaul; TS_4, midhaul.
TN MD (T-NSSMF) receives TS_1, TS_3 and TS_4 from NSMF (step 2).
TN MD then configures backhaul (2a-i), fronthaul (a2-ii), and midhaul (2a-iii), respectively.
TS_1
TS_3
TS_4
NSMF shall be responsible for determination of Slice Profile of FH, MH and RAN NFs.
NSMF shall be responsible for stitching together e2e slice including FH and MH.
Preferred option for external
RAN-NSSMF, E2E Slicing

## Slide 16: RAN Sub-net Slicing: Proposal for Guilin
ONAP shall:
Select RAN NSSI, determine RAN slice sub-net resources and then configure the RAN slice sub-net including:
  Association of xNFs to a Slice sub-net instance
  Allocation of ‘resources’ for a slice sub-net instance
  Configuration of RAN for a slice sub-net instance (including cell configuration such as bandwidth, etc.)
Consume necessary PM/FM info from RAN, for KPI monitoring/Closed Loop Actions/Intelligent Slicing (details to be worked out)
Re-configure/re-allocate RAN resources (under discussion).
Assumptions
All RAN xNFs are created and pre-configured (Preparation phase)
*** Configuration & Persistency Service is assumed to contain cell details including PNF mapping, etc.
Southbound interface from SDN-C (R) will be netconf for CM, and VES for FM/PM. We intend to align with O-RAN where feasible.
ONAP
RAN
CUs
DUs
O1/O2*
Details being worked out with O-RAN
Slice sub-net “configuration” – attributes, flows.
Configuration of Near-RT RIC
NRM for RAN elements
Role of Near-Real-time RIC & interactions in the context of RAN Slicing (A1 interface also)
PM/FM notifications and KPIs to be used
RAN slice inventory
List of cells, DUs, CUs with details of active slices
Capacity & Capability of RAN subnet
RUs
Near RT-RIC

## Slide 17: RAN sub-net slicing: Impact overview for Guilin
ONAP
SO CSMF
SO NSMF
SO RAN NSSMF
SDN-C (R)
SO
OOF
RAN NSSI selection
RAN Slice profile determination
RAN Resource allocation
A&AI
Configuration & Persistency Service
Cell details
RAN slice details
TA mapping details
SDC
NSSTs
KPIs
Policy
RAN sub-net config policies
CL Policy
Blue - Impacts
NSSMF functionality
(O) RAN
Slice profiles
NSST, NSSI
RAN VNF info
DCAE
S-NSSAI KPI monitoring
NSSI KPI monitoring
O1
SO NSSMF Adaptor
SO Transport NSSMF
SDN-C
External RAN NSSMF
NSI KPI monitoring
EXT-API
Note: The interaction between RAN & Transport subnets for FH and MH are not shown here.
Transport (FH, MH)

## Slide 18: External RAN NSSMF
Impacts for External RAN NSSMF interaction
Enhancements in SO NSSMF adapter to support RAN slicing, with standard 3GPP APIs) Enhance allocateNSSI and modifyNSSI, etc 3rd-party RAN NSSMF simulator for integration test automation (support standard 3GPP APIs) allocateNSSI deallocateNSSI modifyNSSI getNSSI Etc PM/FM data reporting from external RAN NSSMF to ONAP (NSMF) is still under discussion E2E slice stitching with Fronthaul, RAN NFs, Midhaul, Backhaul and Core shall be NSMF’s responsibility This requires Scenario 2 (see subsequent slides) to be supported, and requires interface between NSMF and External RAN NSSMF for informing the FH/BH configurations.
NSMF (ONAP)
CSMF (ONAP)
TMF APIs
External RAN NSSMF
RAN xNFs
OSS/BSS/Apps
Transport NSSMF
Core NSSMF
3GPP APIs
xhaul
Core
Adaptor

## Slide 19
Transport Subnet Slicing: Guilin scope
Transport Slice Definition Model
E2E NS controller, RAN Slice controller, CORE Slice controller
Optical Domain Controller
Optical Network
TSCi (draft-rokui-5G-transport-slice)
ACTN TE / L0/L1/L2 models
1. Implement TSCi (i.e., create TS definition model)
Transport Slice Implementation Models
2. L1 (OTN) and L2 (E-line) service slicing
NOTE: many existing CCVPN features can be reused.
NOTE: could also leverage MDONS L1 (OTN) using TAPI as implementation models.
Assumption
Transport slicing solution includes 2 level of abstraction models: Transport Slice Definition Model and Transport Slice Implementation Model.
Approach
We propose IETF-draft based approach for realizing Transport slicing.

## Slide 20
TSCi Information Model

## Slide 21
TSCi on ONAP: Used As Both Internal & External Interface
NSMF (ONAP)
CSMF (ONAP)
TN NSSMF
xNFs
OSS/BSS/Apps
TSCi Data Model (RESTCONF/YANG)
ONAP
TSCi Data Model is a YANG module
Augmentation of the ACTN VN model; still under development in IETF. Draft will be released this year.
RESTCONF/NETCONF interface
Definition Model
Implementation Model
NSMF (ONAP)
CSMF (ONAP)
TN NSSMF (ONAP)
xNFs
Internal call aligned with 3GPP
Internal call aligned with TSCi
OSS/BSS/Apps
SO
TN NSSMF
NSMF
Internal APIs (TSCi)
EXT-APIs
Standard Restconf APIs (TSCi)
AAI
TSCi model

## Slide 22: Core Subnet Slicing-Goals
Implement Core NSSMF for following features
  Network slice subnet instance creation
  Network slice subnet instance activation
  Network slice subnet instance deactivation
  Network slice subnet instance termination
Core NSSMF to implement sub-set of features as prescribed in 3GPP TS 28.531
Demonstrate 5G Core orchestration as part of slice ordering using containerized workloads (Dummy 5G Core NFs)
Demonstration of following scenarios for slicing requirements (ONAP SO acting as NFVO)
  Non-shared NSST resulting in NSSMF-NFVO interaction to orchestrate new CNFs (NFs) with day 0 configurations
  Shared NSST resulting in NSSMF->NFVO interaction to configure the specific NFs with the re-used S-NSSAI

## Slide 23: Core NSSI LCM
Slice Lifecycle Flows (Existing)
NSSMF – NFVO Flow (New)
UUI
ExtAPI
Core NSSMF
NSMF
CSMF
SO
CDS
Multicloud
serviceOrder API
with slicing
parameters
Call E2ESericeInstance
API with serviceType=CST
1
E2E workflow
8
OOF
AAI
Macro workflow
Call service Instance API
2
3
4
5
6
9
K8s Plug-in
K8s Cluster
7
10
11
NSSMF->NFVO Interaction
NFVO Orchestration Flow

## Slide 24: Core NSSMF -> NFVO, Day 1/n Configuration
Slice Lifecycle Flows (Existing)
NSSMF – NFVO Flow (New)
UUI
ExtAPI
Core NSSMF
NSMF
CSMF
SO
CDS
Multicloud
serviceOrder API
with slicing
parameters
Call E2ESericeInstance
API with serviceType=CST
1
E2E workflow
7
OOF
AAI
Macro workflow
2
3
4
5
6
8
K8s Plug-in
K8s Cluster
9
10
NSSMF->NFVO Interaction
NF Configuration Flow
The Slicing requirements would require in some cases to re-use the existing S-NSSAI. In such cases the NFVO would need to configure specific NFs

## Slide 25: Slice KPI Monitoring
Run Time
NSMF Portal
(Management Portal)
DCAE
Policy
Config Policies
UUI/Portal
CSMF Portal
(Tenant Portal)
Tenant
Service Provider
KPI Computation MS
ONAP
EXT-API
Analysis
MS***
5G NFs
FM/PM data collection
1. Tenant/Operator to monitor the KPI via the UI portal
2. Slice management system internal KPI supervision & analysis
To other ONAP MS (e.g., SO)
NST model incl. KPI
SDC
Impacts
DCAE – New KPI Compute MS, Analysis MS, Data Lake Data Exposure Service (DES)
SDC – Slice template enhancements
Policy – Config policies
EXT-API – External interface
UUI – KPI monitoring inputs, and display
VES Collector
DFC
Impacts
DataLake-DES
DataLake
Feeder
Big Data
DataBase
*** For Closed Loop
Control Loop Policies***
Also shows components relevant to Closed Loop in DCAE

## Slide 26: Details - KPI Computation MS
KPI Computation MS shall be a generic MS to compute KPIs, and shall be used for:
  KPI monitoring requested (via UUI) by operator/slice tenant
  KPI monitoring triggered from service profile
  KPI monitoring for Closed Loop Actions
  KPI monitoring for ML-based Intelligent Slicing
This MS shall get relevant inputs via config policies, thereby making it easily extendable
  KPI formula
  Data source(s) (PM data, another KPI, historical data – DB entry info, etc.)
  Default frequency of computation (can be modified by requestor)
  Default frequency of reporting (can be modified by requestor)

## Slide 27: Closed Loop Control for NSI resource optimization
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SO)
5G Network
Leverage the SON  Control Loop (CL) framework in ONAP
Based on PM/FM data, analyze NSI/NSSI traffic patterns and resource occupancy in NSI/NSSI resources
Based on analysis, trigger OOF for NSI resource optimization/re-allocation
Perform necessary resource adjustments via SO and Domain Controllers (modify NSI/NSSI)
FM, PM data
5G network
Domain
Controllers
Note: For Guilin release, a small set of KPIs from RAN and Core subnets shall be considered.

## Slide 28: Flow (NSSMFs within ONAP)
SO
CL-MS
VES
Policy
VIM
AAI
CPS
SDN-R
VF-C
RAN
Core
New NSI/NSSI/S-NSSAI creation
Slice details, KPIs
NSI/NSSIs are created/modified and AN/CN/TN are instructed to report PM data
PM data
PM data
KPI computations
KPI policies & thresholds
Optimize resources
Slice details
OOF
APPC
PM data
Provisioning CL using CLAMP is a stretch goal.
KPI-MS
KPI monitoring request (slice details)
KPI reporting
KPI analysis
DCAE
O1 interface
Notes: Tracking area list provided
AAI or CPS
Static mapping RU -> DU to start with

## Slide 29: Flow (NSSMFs within ONAP)
SO
CL-MS
VES
Policy
VIM
AAI
CPS
SDN-R
VF-C
RAN
Core
OOF
APPC
Provisioning CL using CLAMP is a stretch goal.
KPI-MS
DCAE
Res. updates
NSI-OPT CL Trigger: Actor SO
NSI-OPT CL DMaaP
RAN resource config update details
O1: RAN resource config update details
Core resource config update details
Core resource config update details
Scale Core VNFs
Scale Core VNF(s)
The acknowledgement/response for each update triggered by SO/VF-C/APP-C/SDN-R is not shown below.
NSI-OPT-CL Response
CL Response
Update RAN config
Update Core config
Notes: - NSSI – SO impacts

## Slide 30: Data Collection Mechanism
We propose to reuse the Bulk PM mechanism to collect data from the network.
Core and RAN NFs shall send a VES File Ready event to DCAE VES Collector.
The file will be fetched and provided to KPI Computation MS.
For Guilin release, we assume:
  KPI computation MS shall be able to read the PM file and do the processing.
  RAN and Core NFs shall report PM data in 3GPP aligned format (so no mapping/formatting is required).
  RAN and Core NFs shall be able to send a File Ready event to ONAP DCAE.
  To be checked: What is the limitation of VES/DCAE on number of files/events it can process? How can it be scaled up?
  Based on above, we may need a data aggregator component that consolidates data received from multiple NFs and sends as a file to ONAP.

## Slide 31: Intelligent Slicing: KPI Guarantee Function
Run Time
DCAE
Policy
Close-loop Policy
DataLake feeder (historic and current KPI)
Analysis MS from ML Model
ONAP
Slice ML Model
Big Data
Database
Real time KPI data
Trigger Event
Historic data for model training
KPI Computation MS
The goal of KPI Guarantee is to maximize/improve KPI adherence by NSIs to the supported services. This action will be triggered when the performance needs to be improved. By monitoring the KPI adherence, and analyzing the trends and correlating it with resource usage data, etc. (using ML models), perform necessary modifications to the NSI/NSSI to maximize KPI adherence.
TCA?
SO
Trigger slice modification
Acumos
Notes
Objective is to reuse existing frameworks & platforms – Acumos DCAE Adaptor, Acumos, DCAE capabilities
Output from Analysis MS from ML Model to create event to trigger policy need to be worked out
We will start with a simple model in Guilin Release.
Notes: Eg: toy model to start with
Eg throughput >10 send out event,
Situation，tendency,
VES, JSON from Analysis MS.
TCA only can read VES,
May need a json convert to ves

## Slide 32: Modeling Aspects
Resource sharing level (service request, NSI, NSSI, NSSI constituents)
Service Profile & Slice profile updates, mapping between service and slice profile
KPIs (for KPI monitoring)
RAN, Core and Transport NSSTs, NSSIs, data stored in AAI and CPS
Sub-net capabilities
Potential enhancements to CST, NST
Align with 3GPP Release 16 (TS 28.541), O-RAN (where applicable & available) and TSCi (IETF)

## Slide 33: Impact overview: Guilin
CSMF Portal
NSMF Portal
SDC
U-UI
NST
CSMF
NSMF
Slice Profile determination
NST Selection
NSI Selection
CSMF Policy
NSMF Policy
SO
OOF
Policy
Service instance
Service Profile
NSI
NST
NSSI
NSST
Slice Profile
A&AI
ONAP
EXT-API
CN NSSMF (3rd party)
NSSI Selection
NSST
CST
NSSMF (RAN, Transport, Core)
KPI Computation MS
Analysis MS
AI/ML MS
RAN-specific config
Transport specific config
SDN-C
Cell Configurations
RAN slice related configurations
C&PS
NSSMF Policy
KPI Policies
CL Policies
DCAE
Core NFs configuration
CDS
RAN NSSMF (3rd party)
Res. determination
RAN-Simulator
Core NFs simulator
Data Lake DES
Service LCM APIs
KPI Monitoring APIs
IBN
CSMF related impacts
NSMF related impacts
NSSMF related impacts
No code impact
External component (or) simulator

## Slide 34: Impact Summary
Track | UUI | SDC | ExtAPI | SO | OOF | SDN-C | SDN-R | CDS | DCAE | AAI | C&PS | Policy | Modeling
Frankfurt impr. |  |  |  |  |  |  |  |  |  |  |  |  | 
RAN Slicing |  |  |  |  |  |  |  |  |  |  |  |  | 
Transport Slicing |  |  |  |  |  |  |  |  |  |  |  |  | 
Core Slicing |  |  |  |  |  |  |  |  |  |  |  |  | 
KPI Monitoring & Closed Loop |  |  |  |  |  |  |  |  |  |  |  |  | 
Intelligent Slicing |  |  |  |  |  |  |  |  |  |  |  |  | 
Ext-RAN NSSMF |  |  |  |  |  |  |  |  |  |  |  |  | 
Note: In addition to above, Core NFs simulators would be required. Further, enhancements to RAN-Simulator is also foreseen.

## Slide 35: Demo scenarios
E2E Slice Service Creation resulting in:
(a) Creation of a new e2e slice with new RAN, Core, Transport slice subnets
(b) Creation of a new e2e slice with reuse of some sub-net(s) and creation of other(s)
(c) Reuse an existing e2e slice
E2E Slice Service activation
E2E Slice Service deactivation
E2E Slice Service termination, resulting in:
Removal of mapping of service to the e2e slice
Removal of NSI, and its associated configuration in constituent NSSIs
Removal of NSI, deallocation of constituent NSSIs
KPI monitoring via portal
Closed Loop Control for NSI resource re-allocation
Intelligent Slicing to ensure maximum KPI adherence
Stretch goal: (Simulated) traffic flow demo through NSI constituting of RAN, Core and Transport slice subnets created by ONAP preceded by NF configuration.

## Slide 36: Topics for discussion
Aggregation Function
RAN and Transport Slicing interaction
Intelligent Slicing

## Slide 37: Component Impacts
Note: This is a preliminary view that is under internal discussion, and not yet discussed with all PTLs.
ONAP Component | Impact(s)
SDC | Enhancements to CST and NST, design of RAN, Core and Transport NSSTs Enhancements for KPI monitoring and reporting
UUI | Support of standard interfaces to CSMF and NSMF KPI monitoring enhancements Time-based service activation
EXT-API | Support of standard interfaces for CSMF, NSMF and NSSMF (Northbound)
SO | Part of NSSMF functionality for RAN, Core and Transport subnets Enhancements to interface with external Core/RAN NSSMF (adaptor) Standardization of interfaces Closed Loop Control functionality (as actor) Improvements on top of Frankfurt implementation
OOF | Enhancements to NSI selection, NSSI selection Resource (re)allocation in RAN, Transport and Core subnets Improvements on top of Frankfurt implementation Taking PM data into consideration for NSI/NSSI selection (stretch goal)

## Slide 38: Component Impacts – cont’d
ONAP Component | Impact(s)
DCAE | New data lake for FM/PM and KPI data storage New micro-service for KPI analysis (and Closed Loop Trigger) New micro-service for Intelligent Slicing VES enhancements for FM/PM reporting for network slicing (NSSI/S-NSSAI level)
Policy | Enhancements for Control Loop New config policies for OOF, SO and DCAE
SDN-C | Part of NSSMF functionality for RAN and Transport Closed Loop Control functionality (as actor)
CDS | API mapping on SB interfaces
AAI | Schema updates for Network Slicing New nodes for NSI and NSSI, other modeling impacts RAN, transport and core slice inventory (at xNF and connection level)
Configuration & Persistency Service | RAN configuration data (cell level – initial as well as network slicing related)
Note: This is a preliminary view that is under internal discussion, and not yet discussed with all PTLs.

## Slide 39
Thank You!