## Slide 1: KPI Monitoring, Closed Loop and Intelligent Slicing (Part of the E2E Network Slicing Use Case)
Participants: CMCC, Wipro, Huawei, AT&T, QCT, Amdocs, Fujitsu, Verizon, Reliance Jio, Tencent, China Telecom
Authors: Lin Meng (CMCC), Swaminathan S (Wipro), Guobiao Mo (CMCC),
Lu Kai (CMCC)
May 28, 2020

## Slide 2: Introduction
KPI Monitoring
Tenant/Operator to monitor the KPI via the UI portal
Slice management system has internal KPI supervision
Closed Loop Control and Intelligent Slicing
Slice related Data analysis and prediction, generate optimal decision and execute in a closed loop way. Control loop need to be considered for intelligent slicing use.
3 cases for ONAP E2E Network Slicing implementation by introducing new SON functions:
(Cross)Slice resource optimization
(Guilin: simple closed loop for single NSI scenario; Beyond Guilin: Cross- Slice Scenario)
2. KPI adherence optimization (KPI Guarantee)
(Guilin: simple closed loop by introducing AI model. Beyond Guilin: cross-interaction with (1) also)
3. Service experience optimization (SLA Guarantee, QoE based) (Beyond Guilin)
Blue – Guilin scope
Pre-requisites
Support for data collection (FM/PM) and analysis
Collection and analysis of non-OAM and additional NF data (e.g., mobility, QoS flows)
Support for slice modification (in Guilin, only limited support)
Blue Guilin scope
Note: Reference 3GPP TS 28.861.

## Slide 3: KPI Monitoring - Considerations
ONAP as NSMF/NSSMF shall monitor certain KPIs for Closed Loop or Intelligent Slicing (details of supported KPIs to be defined)
2 additional inputs on what KPIs to be monitored:
  Operator/slice consumer through service profile, and
  Operator/tenant through KPI monitoring facility in UUI
For the 2 additional inputs above, we can also monitor a completely “new” KPI. We only need the formula and variables. Assumption: We are already collecting the required data from the network (to apply in the formula). Then we apply this formula on the collected data to compute the KPI.
NF-level monitoring: NF capabilities to report data per S-NSSAI.
Under discussion for Modeling and External NSSMF interface
Should we extend Slice Profile definition to include list of KPIs to be monitored (based on Service Profile input)?
How will KPI monitoring be informed to external NSSMF (APIs to be defined)?
For Closed Loop actions, what data shall be exposed by external NSSMF? How should we configure it to report, or query certain KPIs?

## Slide 4: Slice KPI Monitoring
Run Time
NSMF Portal
(Management Portal)
DCAE
Policy
Config Policies
UUI/Portal
CSMF Portal
(Tenant Portal)
Tenant
Service Provider
KPI Computation MS
ONAP
EXT-API
5G NFs
FM/PM data collection
1. Tenant/Operator to monitor the KPI via the UI portal
2. Slice management system internal KPI supervision & analysis
NST model incl. KPI
SDC
Impacts
DCAE – New KPI Compute MS, Data Lake Data Exposure Service (DES)
SDC – Slice template enhancements
Policy – Config policies
EXT-API – External interface
UUI – KPI monitoring inputs, and display
VES Collector
DFC
Impacts
DataLake-DES
DataLake
Feeder
Big Data
DataBase
*** For Closed Loop
Also shows components relevant to Closed Loop in DCAE
New components

## Slide 5: DataLake Components
Data Lake Data Exposure Service provides a framework to expose data in Big Data databases via REST API
with just configurations.

## Slide 6: KPI Monitoring: DCAE impacts
OSS/BSS
Ext-API
DES
MongoDB
Presto
MongoDB Connector
Elasticsearch
Elasticsearch
Connector
ONAP Components (UUI or others)
REST API
SQL
DL Admin UI
Config
RDBMS
(MariaDB)
Data Lake
New DCAE MS
Notes: Discuss with EXT-API if DES can be part of EXT-API component.

## Slide 7: Details - KPI Computation MS
KPI Computation MS shall be a generic MS to compute KPIs, and shall be used for:
  KPI monitoring requested (via UUI) by operator/slice tenant
  KPI monitoring triggered from service profile
  KPI monitoring for Closed Loop Actions
  KPI monitoring for ML-based Intelligent Slicing
This MS shall get relevant inputs via config policies, thereby making it easily extendable
  KPI formula
  Data source(s) (PM data, another KPI, historical data – DB entry info, etc.)
  Default frequency of computation (can be modified by requestor)
  Default frequency of reporting (can be modified by requestor)

## Slide 8: Data Collection
We propose to reuse the Bulk PM mechanism to collect data from the network.
Core and RAN NFs shall send a VES File Ready event to DCAE VES Collector.
The file will be fetched and provided to KPI Computation MS.
For Guilin release, we assume:
  KPI computation MS shall be able to read the PM file and do the processing.
  RAN and Core NFs shall report PM data in 3GPP aligned format (so no mapping/formatting is required).
  RAN and Core NFs shall be able to send a File Ready event to ONAP DCAE.
  To be checked: What is the limitation of VES/DCAE on number of files/events it can process? How can it be scaled up?
  Based on above, we may need a data aggregator MS that consolidates data received from multiple NFs and sends as a file to ONAP.

## Slide 9: KPI Computation
KPI Computation MS
MongoDB
MongoDB Connector
Message router
NF2
NF3
NF1
……
Pub
Sub
Data router
DFC
VES collector
notify
download
New DCAE MS
Policy
KPI request from DES (for KPI monitoring)
KPI request from Analysis MS (Closed Loop)
KPI request from AI/ML MS (Intelligent Slicing)
KPI request from SO (Service/Slice Profile)
Config and KPI computation policies
Based on the 4 triggers, KPI computation MS computes KPIs and stores them in Data Lake.
Config policies for KPI computation are fetched from Policy (standard mechanism).
Historical data if required shall be fetched from Data Lake.
DL feeder
PM mapper

## Slide 10: Flow
NF
DFC
Computation service
UUI
Store in datalake
Query result
Publish VES event
Pm-mapper
publish notify event
DMaap
Pm Notify
DES
Return result
VES collector
Download PM files
Data router
Convert 3gpp to ves
message router
publish to dmaap;store in datalake
sub ves
calculate
pub kpi result
Data lake feeder
MongoDb
External component
ONAP component
DCAE component
DL component

## Slide 11: Closed Loop Control for NSI resource optimization
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SO)
5G Network
Leverage the SON  Control Loop (CL) framework in ONAP
Based on PM/FM data, analyze NSI/NSSI traffic patterns and resource occupancy in NSI/NSSI resources
Based on analysis, trigger OOF for NSI resource optimization/re-allocation
Perform necessary resource adjustments via SO and Domain Controllers (modify NSI/NSSI)
FM, PM data
5G network
SO
SO
Domain
Controllers

## Slide 12: Closed Loop Illustration – NSI resource optimization
KPIs to be collected - draft
Data | Source | Remarks
Number of PDU sessions | SMF | 
Resource occupancy of VNFs (CPU, RAM) | VIM? | Separately for RAN and Core
Upstream and downstream throughput | UPF | Summed across all UPFs of a NSI from the NG-RAN
Physical radio resource usage (DL Total PRB Usage per S-NSSAI) | RAN | 
Number of users in RRC connected mode (per S-NSSAI) | RAN | 
AMFReg. Number | AMF | Registered subscribers of network and network slice instance through AMF
Notes: Maximum number of sessions = x
Level of sessions reached = (n/x) * 100 (if it is < 75%, then my threshold is not reached)
Resource occupancy % = (Average CPU load/Total CPU allocated to the NSI)
Upstream throughput % = 100* w/(allocated BW)
Scenario 1 = ONAP is Core NSSMF (KPI computation at NSSI level is done by ONAP)
Scenario 2 = Core NSSMF is outside ONAP (some of the NSSI KPIs will be given to ONAP)
In both scenarios, NSI KPIs are computed in ONAP.
KPI computation = DCAE MS.
New DCAE MS-1
Closed Loop KPI computation for NSI
For all the Service Profile listed KPIs, and KPI monitoring KPIs
KPI monitoring
Data collection from SB (VES standard) (Reuse Bulk PM for 3GPP specified data)
Request to report data from NF/NSSMF (reuse Bulk PM for NF data, for NSSMF – check 3GPP???)
O-RAN alignment (for RAN data reporting) (O1)
Modeling part
New DCAE MS-2
Closed Loop KPI computation for NSSI
For all the Slice Profile listed KPIs, and KPI monitoring KPIs provided by NSMF to be computed as NSSI level
Formula can be given via LuKai
Policy
KPI formulas for any new KPIs to be computed
Threshold policies, configuration (how often you will do KPI computation, KPI data aggregation, storage window – last ‘n’ samples)
Closed loop policy -> there may be some small code impact in Policy component

## Slide 13: Control Loop Illustration
Slice Analysis MS
KPI Computation MS
Data Lake
SO
OOF
Policy
5G Network
Domain Controllers
2a
1a
1b
2b
3
4
5
6
7
8
Step | Details
1a, 1b | Slice creation/reuse trigger with PM data reporting details
2a | Information about new NSI/NSSI creation with KPI details
2b | Request to compute KPIs
3 | Periodically (later on, based on events) analyze KPI data and trends
4 | Trigger OOF for resource optimization and obtain optimization results
5 | Trigger Policy for Control Loop action
6 | Trigger SO for NSI/NSSI resource (re) configuration
7,8 | Reconfigure resources
New DCAE MS
Note: The data collection part is not shown here.
DCAE
Notes: PMSH can be extended to remove SO <-> SA-MS interaction (check if AAI notification can be reused?)

## Slide 14: Flow (NSSMFs within ONAP)
SO
CL-MS
VES
Policy
VIM
AAI
CPS
SDN-R
CDS
RAN
Core
New NSI/NSSI/S-NSSAI creation
Slice details, KPIs
NSI/NSSIs are created/modified and AN/CN/TN are instructed to report PM data
PM data
PM data
KPI computations
KPI policies & thresholds
Optimize resources
Slice details
OOF
APPC
PM data
Provisioning CL using CLAMP is a stretch goal.
KPI-MS
KPI monitoring request (slice details)
KPI reporting
KPI analysis
DCAE
O1 interface
Notes: Tracking area list provided
AAI or CPS
Static mapping RU -> DU to start with

## Slide 15: Flow (NSSMFs within ONAP)
SO
CL-MS
VES
Policy
VIM
AAI
CPS
SDN-R
CDS
RAN
Core
OOF
APPC
Provisioning CL using CLAMP is a stretch goal.
KPI-MS
DCAE
Res. updates
NSI-OPT CL Trigger: Actor SO
NSI-OPT CL
RAN resource config update details
O1: RAN resource config update details
Core resource config update details
Core resource config update details
Scale Core VNFs
Scale Core VNF(s)
The acknowledgement/response for each update triggered by SO/VF-C/APP-C/SDN-R is not shown below.
NSI-OPT-CL Response
CL Response
Update RAN config
Update Core config
Notes: Tracking area list provided
AAI or CPS
Static mapping RU -> DU to start with

## Slide 16: Intelligent Slicing: KPI Guarantee Function
Run Time
DCAE
Policy
Close-loop Policy
DataLake feeder (historic and current KPI)
Analysis MS from ML Model
ONAP
Slice ML Model
Big Data
Database
Real time KPI data
Trigger Event
Historic data for model training
KPI Computation MS
The goal of KPI Guarantee is to maximize/improve KPI adherence by NSIs to the supported services. This action will be triggered when the performance needs to be improved. By monitoring the KPI adherence, and analyzing the trends and correlating it with resource usage data, etc. (using ML models), perform necessary modifications to the NSI/NSSI to maximize KPI adherence.
TCA?
SO
Trigger slice modification
Acumos
Notes
Objective is to reuse existing frameworks & platforms – Acumos DCAE Adaptor, Acumos, DCAE capabilities
Output from Analysis MS from ML Model to create event to trigger policy need to be worked out
We will start with a simple model in Guilin Release.
Notes: Eg: toy model to start with
Eg throughput >10 send out event,
Situation，tendency,
VES, JSON from Analysis MS.
TCA only can read VES,
May need a json convert to ves

## Slide 17: KPI Adherence Optimization – Sample KPIs
Draft list
QoS flow retainability-related KPI: RAN
DRB accessibility-related KPI: RAN
End-to-end latency measurements: Compute from all subnets latency (sum of NSSI latencies)
Service experience, etc. (TS 28.552)
Notes: Draw simple drawings

## Slide 18: Summary of DCAE Impacts
Category | Component | Impact
KPI Monitoring | DES | New MS
KPI Monitoring, Closed Loop, Intelligent Slicing | KPI Computation MS | New MS
Closed Loop | Slice Analysis MS | New MS
Intelligent Slicing |  | <No impact foreseen, to be confirmed>

## Slide 19: Other Component Impacts
Component | Category | Impact(s)
UUI | KPI Monitoring | TMF 628 based interface to EXT-API for KPI monitoring trigger TMF 628 based interface to EXT-API for fetching KPIs
EXT-API | KPI Monitoring | Support of TMF 628 APIs on NBI Interface to DES on SB
SO | KPI Monitoring, Closed Loop, Intelligent Slicing | Information to DCAE MS on NSI/NSSI creation with KPI details
 | Closed Loop, Intelligent Slicing | Upon reception of trigger from Policy, trigger domain controllers (RAN, Core) for reconfiguration
OOF | Closed Loop | Determine reconfiguration to be done for NSI optimization
Domain Controllers (SDN-R, CDS) | Closed Loop, Intelligent Slicing | Perform NF reconfigurations in RAN and Core sub-nets
Policy | Closed Loop, Intelligent Slicing | Potential minor impacts for new Control Loops

## Slide 20: Closed Loop Control/Intelligent Network Slicing
Use data (e.g., QoE data, network data, etc. ) from various sources as input, analysis such slice related data and make prediction by using AI algorithms, generate optimal decision and execute in a closed loop way.
3 cases for ONAP E2E Network Slicing implementation by introducing new SON functions:
(Cross) Slice Resource Optimization
KPI Adherence Optimization（KPI Guarantee）
The goal of maximizing KPI adherence is to maximize/improve KPI adherence by NSIs to the supported services. This action will be triggered when the performance needs to be improved. By monitoring the KPI adherence, and analyzing the trends and correlating it with resource usage data, etc. (using ML models), perform necessary modifications to the NSI/NSSI to maximize KPI adherence.
Service Experience Optimization (SLA Guarantee)
Considering the limited resource and changing condition like the Signal to Noise Ratio and users on the slice, the initial resource configuration may not be able to satisfy the slice SLA during the lifecycle of the slice. ONAP can update the resource configuration of the slice in a closed loop way triggered by the analysis of SLA fulfillment.
SLA fulfillment is evaluated based on the analysis of QoE info and KPIs.
1
2
3
Guilin Scope: simple control loop by introducing ML model
Guilin Scope: simple control loop for
single slice scenario
Beyond Guilin
The goal of resource optimization is to optimize the resource allocation within the total available physical and virtual resources, while adhering to the KPI levels.
So the trigger for resource optimization determination would be the changes in the network resources usage, and traffic patterns.
Later, ‘over-fulfillment of KPIs’ could also lead to resource optimization.

## Slide 21
Config Data
PM/FM Data
KPI Data
(NSI/NSSI/S-NSSAI level)
Network Data
(5GC NF level)
E.g.: QoS flow data, UE location, etc.
KPI/SLA Fulfillment Monitoring
(limited functionality in Guilin)
OAM Data
Non OAM Data
Application Data
QoE Data
(AF level)
Closed loop control
Intelligent analysis assists Slice KPI/SLA Guarantee
Determine changes, & Update Slice Resources and Configuration
(Limited updates for Guilin)
Data Collection
Data Analysis
Input
Input
Input
Input
Input
Input
refers to Guilin Scope




AI/ML Model:
KPI/SLA prediction
(Beyond Guilin: QoE prediction)


Trigger


## Slide 22: Thank You