## Slide 1: PM Dictionary Proposal Common Schema for ONAP Nokia Proposal August 13, 2018 v1

## Slide 2
Agenda
Topics Covered:
Overview of Bulk PM File Upload and Performance Event Generation
Overview of Real Time PM
PM Dictionary Usage in ONAP
PM Dictionary Requirements for ONAP
PM Dictionary Content
Common PM Dictionary Schema for ONAP

## Slide 3: Bulk PM File Upload and Performance Event Generation

## Slide 4
Bulk PM File Upload and Performance Event Generation
Network Function (NF) establishes a HTTP/TLS connection to the DCAE VES Collector. DCAE authenticates the certificate for TLS.
NF sends FileReady notification Event to DCAE VES Collector. Event is encoded in JSON and sent via HTTP/TLS. HTTP/TLS connection is set up and torn down every time a FileReady notification event is sent.
DCAE VES Collector publishes the event to appropriate topic in DMaaP Message Router (MR).
DCAE File Collector retrieves the FileReady notification event from DMaaP MR.
File Collector uploads PM File from NF using a secure file transfer protocol; SFTP or FTPeS supported in Casablanca. NF authenticates the connection.
File Collector publishes PM File to DMaaP Data Router (DR).
PM Mapper retrieves PM file from DR and generates Performance events as configured by PM Mapper File.
PM Mapper publishes Performance events to MR.
Analytics Applications (AA) retrieve the Performance events of interest from MR. AA analyze the data to produce statistics and KPIs and optimization recommendations.
Bulk PM File Upload and Performance Event Generation
PM
Mapper
Data
Router
VES
Collector
Authenticate connection
HTTP/TLS
Upload PM file
Publish Event
HTTP/TLS
Send FileReady event
7
SFTP or FTPeS
Retrieve PM File
File
Collector
Retrieve Event
Publish File
Message
Router
VES
Collector
VNF
PNF
6
5
4
3
2
1
Analytics
Application
Publish Performance Event
Retrieve Performance Event
8
9
1
7
6
2
3
4
5
8
9

## Slide 5
Performance Event Generation by PM Mapper
Proposal
Provide the ONAP Operator with the ability to define flexible, customizable Performance events.
Events are generated from PM XML File and targeted for analytics applications in ONAP.
Define Performance Events
ONAP displays list of available measurements for a NF Type.
ONAP Operator selects the desired measurements from the list of measurements.
A PM Mapping File is generated so the PM Mapper knows how to create the events.
Create Performance Events
NF notifies DCAE that a PM file is available for upload.
File Collector uploads PM Files from NF and stores them in Data Router.
PM Mapper creates custom Performance events from the PM File data according to PM Mapping File.
Analytics Applications use these performance events for targeted analysis of network operations.
PM Dictionary is needed to display the list of available measurements for this NF Type (future goal).
PM Dictionary may be needed by AA to understand the measurements it receives so that it can automatically and dynamically process them (future goal).

## Slide 6: Real Time Performance Measurements (RTPM)

## Slide 7
Real Time PM High Volume Measurement Events
Real Time PM Flow
Real Time PM High Volume Event Scenario
Network Function (NF) establishes a TCP connection to the DCAE High Volume (HV) VES Collector. If TLS is used, DCAE authenticates the certificate. Connection is persistent as long as Real Time PM (RTPM) is enabled so this is only done once.
For each event:
NF sends hvMeas Event containing RTPM data to DCAE HV VES collector. Event is binary encoded with Google Protocol Buffer (GPB). Some string fields (measType) may be converted to numeric values (iMeasType) for efficiency.
DCAE validates the hvMeas Event using the VES_Event.proto (which contains the schema for the Common Header and hvMeas Event fields). DCAE publishes the event to DMaaP.
Analytics Application retrieves data. To decode and process the data, AA uses the VES_Event.proto, HvMeasFields.proto (which contains the schema for the RTPM measurements themselves), and the PM Dictionary.
DMaaP
DCAE HV
VES
Collector
Analytics
Application
PNF
VNF
4
Authenticate connection
1
AA retrieves data
Publish hvMeas Event
NF sends RTPM hvMeas event
TLS(optional)/TCP
Repeat for each event
2
3
TLS(optional)/TCP
PM Dictionary may be needed by AA to map the numeric IDs to measurement names and also to understand how to process the measurements (future goal) .

## Slide 8: PM Dictionary Usage and Requirements

## Slide 9
PM Dictionary Usage for Analytics Applications
PM Dictionary is used by Analytics Applications to retrieve information about the measurements in the Performance events and RTPM hvMeas events and in the Bulk PM XML File.
PM Dictionary provides detailed information about each Measurement that a NF produces, including Measurement Name, Measurement Family, Measured Object Class, Description, Collection Method, Value Ranges, Unit of Measure, Triggering Conditions and other information.
A very important value of the PM dictionary is to separate the meta data from the actual data so that new measurements can be defined/deleted/updated anytime without requiring any change to the transport framework, since all the data is sent using the same format/structure. As such, use of the data requires the dictionary so that the data can be properly interpreted.
Initially,
  PM Dictionary is used by the Analytics Application developers to update the Analytics Application code as needed to process the measurements.
  PM Dictionary may be used by the Analytics Applications to translate a numeric measurement identifier (iMeasType) in a RTPM event into a measurement name (measType). Alternately, AA may use the numeric values directly. This depends on how the AA code is written.
Ultimately,
  Goal is for the Analytics Applications to use the PM Dictionary directly to be able to dynamically process new measurements based on the information in the PM Dictionary.

## Slide 10
PM Dictionary Usage for Measurement Change Management
The set of PM Measurements produced by a NF changes with each new NF SW Release.
PM Dictionary is used by ONAP operators to determine the PM changes associated with a new NF SW release so they can update performance events, associated PM Mapper Files and impacted Analytics Applications if needed.
PM Dictionary contains a Last Change indicator for each measurement.
    Identifies the PM Dictionary version for the last time each measurement changed. For example, measLastChange=“5G18A_1807_003” or measLastChange=“5G19_1906_002”.
    Makes it possible to easily identify events and applications that are candidates for update due to a changed measurement in the new SW release.
At onboarding, ONAP Operator filters the PM Dictionary for the current version.
  Cross check against PM Mapper event definitions.
  Events that use measurements that were modified or deleted in the current version of the PM Dictionary need to be analyzed to see if they are still applicable and if the event definition and/or the Analytics Application needs to be updated.
  Measurements that were added in the current version need to be analyzed to see if they should be included in a new or existing PM Mapper event definition and if an Analytics Application needs to be updated to process them.

## Slide 11
PM Dictionary Usage for Event Specification
PM Dictionary is used by ONAP components (for example, SDC, CLAMP, Policy) to display the set of measurements supported by a particular NF.
ONAP Operator can:
  select the desired measurements for PM Mapper Performance events (future goal)
  configure the NF to generate RTPM hvMeas events (future goal).
For Performance events, ONAP creates:
  a PM Mapping File so the PM Mapper knows how to create the events. Format and content of PM Mapping File is TDB (future goal).
PM Dictionary is versioned. For example, pmDefVsn=“5G19_1906_002”.
  Allows ONAP components to associate the PM Mapper Performance events, RTPM hvMeas events and Bulk PM XML Files with the appropriate PM Dictionary version based on the NF instance that emitted the event.
  Each NF package has one PM Dictionary version onboarded with it.
  ONAP must keep track of the association between PM Dictionary version and NF Package version and NF Instance.

## Slide 12
PM Dictionary Requirements for ONAP
PM Dictionary requirements:
  Provides detailed information about each Measurement that a NF produces.
  Delivered as part of the NF package at onboarding.
  Updated whenever a PM is added, deleted or modified.
  Delivered in a machine-readable format.
  Formatted according to a common PM Dictionary schema.
  Contains “last change” indicators for each measurement to make it easy for an Operator to know what has changed.
  Aligns with a NF package version. There is a PM Dictionary version (pmDefVsn) that describes the set of PM measurements supported by the NF in that NF package version.
  Is the same artifact for Bulk PM and Real Time PM.
  Nokia is proposing a common PM Dictionary schema for ONAP.

## Slide 13: PM Dictionary Content

## Slide 14
PM Dictionary Contents for ONAP
Field | Description | Example
pmDefVsn | Version of the PM Dictionary. Version is vendor defined. | 5G19_1906_002
nfType | NF type to whom this PM Dictionary applies. 3GPP NF Types are 3GPP defined. Approved 5G terms are gNB, gNB-CU, gNB-DU, gNB-CU-CP and gNB-CU-UP. Convert these to camel format for ONAP; gnb, gnbCu, gnbDu, gnbCuCp or gnbCuUp. Should match the string used in eventName. | gnb
vendor | Vendor of the NF type to whom this PM Dictionary applies. | Nokia

## Slide 15
PM Dictionary Contents for ONAP
Field | Description | Example
measType | Measurement name used in PM file. Name is in 3GPP format. Vendor specific names are preceded with VS. | VS.NINFC.IntraFrPscelChFailTdcExp
iMeasType | Vendor defined integer identifier for the measType; used in GPB for efficiency. Must be combined with measInfoId to identify a specific measurement. | 2
measInfoId | Name for a group of related measurements, in 3GPP format where specified, else vendor defined. | NR Intra Frequency PSCell Change
measFamily | Abbreviation for a family of measurements, in 3GPP format where specified, else vendor defined. | NINFC
measDescription | Text description of the purpose of the measurement, what information does the measurement provide. | This measurement is the number of intra gNB intra frequency PSCell change failures due to TDCoverall timer expiry.
measCondition | Text description of the condition that causes the measurement to be updated. | This measurement is updated when the TDCoverall timer has elapsed before gNB receives the X2AP: SgNB Modification Confirm message.
measLastChange | PM Dictionary version for the last time this measurement was changed, added or deleted. | 5G18A_1807_003

## Slide 16
PM Dictionary Contents for ONAP
Field | Description | Example
measResultType | Data type of the measurement result. Valid values are integer or float. | integer
measResultRange | Range for the measurement result. | 0..2^32-1
measResultUnits | Unit of measure for the result; e.g. milliseconds, bytes, kilobytes, packets, integer number. | integer number
measObjClass | Measurement Object Class | CELL
measCollectionMethod | 3GPP Collection Method for measurement; e.g. CC, SI, DER, Gauge. | CC
measAggregationLevels | Vendor recommendation for the levels at which measurements are aggregated | BTS CELL

## Slide 17: Common PM Dictionary Schema

## Slide 18
PM Dictionary Schema Format
There are two logical choices for PM Dictionary Schema:
  YAML
    This is the preferred schema for the PM Dictionary because all other ONAP artifacts are in YAML format.
    See PM Dictionary YANG Schema Definition and PM Dictionary YANG Example below.
  XML
    3GPP PM files are in XML format so Analytics Applications can more easily handle a XML schema for the PM Dictionary.
    See PM Dictionary XML Schema Definition and PM Dictionary XML Example below.