## Slide 1
5G Service Modeling & 5G Service Creation
R6 Frankfurt Use Cases
July 20, 2020 version 2
Benjamin Cheung, PhD

## Slide 2
5G Basics & 5G RAN
Benjamin Cheung, PhD

## Slide 3
3GPP Release 15, IMT-2020 = 5G
Virtual and Augmented Reality
Smart City
Geographically spread devices
Smart Automated Vehicle Control
Remote Surgery and Examination
Factory Automation
Remote Device Control
Internet of Things (IoT)
Smart Infrastructure
Broadband Experience Everywhere Anytime
Media Anywhere
eMBB (enhanced Mobile Broadband)
URLLC (Ultra Reliable Low Latency Communications)
mMTC (massive Machine Type Communications)
Smart
Connected
Collaborate
Access
Interactive
Aware

## Slide 4
5G RAN Wireless Network
5G
Application
Ecosystem
UE
RU
DU
CU
Internet
Edge
Cloud
Antenna
DU
RAU
External Content
RU – Remote Radio Unit
DU – Distributed Unit (5G Base Unit)
CU – Centralized Unit
CPRI – Common Public Radio Interface
CPRI
Mid Haul
Back Haul
Centralized
Cloud
Disaggregated Core
UPF
SMF
UDM
AUSF
UPF – User Plane Function
SMF – Session Management Function
UDM – Unified Data Management Function
AUSF – Authentication Service Function
AMF – Access Management Function
RAN Network Elements
Core Network Elements
ONAP Run Time Management
SO
SDN-C
DCAE
A&AI
OSS
BSS
APP-C
SO – Service Orchestrator
SDN-C – Service Design Network Controller
DCA&E – Data Collection Analytics & Events
A&AI – Available & Active Inventory
APP-C – Application Control
CU
RAP
RF
AMF
1
N
1
N

## Slide 5
Cell
Carrier-Sector
RU
DU
CU
Antenna
DU
RAU
CPRI
Mid Haul
CU
RAP
RF
1
N
1
N
Carrier-Sector
Carrier-Sector
Carrier-Sector
Carrier-Sector
Carrier-Sector
Carrier-Sector
Fred
RAN management – see it/ performing/ control
Performance, 28.541 as anchor
Model for gNB.
Look at other 3GPP documents to capture common for functions
Categorized to lifecycle management; instant. Rtconfig, …
Orchestration / Performance FCAPS. LCM
3GPP TS28.541
5G NRM
GROUPINGS
Kevin
What parameters are common to many functions
Super-class w/ common things and sub-class to particular functions
Configurations & groupings.
Different Domains
Are there common constructs we can use across domains.
Optical Fixed Wireless = same Information
Data Models domain focused?

## Slide 6
Fred F.
Bob Pape
Chris Skowronek
Chuyi Guo
Jacqueline Beaulac
Marek Kukulski
S. Ricci
Yaoguang Wang
Andy Mayer
Kevin Skaggs
f1
f1
f1
orthogonal

## Slide 7
5G Service Modeling & 5G Service Creation
Benjamin Cheung, PhD

## Slide 8
R7: Modeling a 5G Service
Virtual
Link
Connection
Point
HEAT
Templates
Informational
Artifacts
Deployment
Artifacts
Blueprints
Policies
Configuration
Files
Templates
5G SERVICE
Network
Function (VNF)
Network
Function PNF
Resources
User Designed
Vendor Provided
Foundational
P
Allotted NF
ANF

## Slide 9
R4: 5G Base Station (gNodeB)
DU
CU
(VNF)
DU
RAU
CU
N
1
UPF
(VNF)
AMF
(VNF)
RAN Network Elements
Core Network Elements
N
1
1
N
VNF/CU #1
Conn Pt #1
Conn Pt #3
Conn Pt #n
PNF/DU #n
PNF/DU #1
Virtual Link
5G SERVICE
Resources
…

## Slide 10
3GPP TS28.541/TS28.622 Model

## Slide 11
3GPP TS28.541/TS28.622 Model
ETSI Alignment R7+ U/C will introduce a CNF version of the gNB DU

## Slide 12
3GPP TS28.541 Model

## Slide 13
3GPP TS28.541 Model

## Slide 14
PNF Descriptor Model
NetworkServiceDescriptor
Pnfd
pnfdId – Identifier [1]
provider – String [1]
version – Version [1]
security – SecurityParameters [0..1]
functionDescription – String [1]
pnfdInvariantId – Identifier
name – String [1]
PnfExtCpd
cpdId – Identifier [1]
cpRole – String [0..1]
description – String [0..1]
cpProtocol – CpProtocolData [1..*]
trunkMode – Boolean [1]
allowedAddressData – AddressData [*]
NsdReferencesPnfd
*
*
PnfdHasPnfExtCpd
1
1..*
NetworkFunctionDesc
ResourceDesc
ExtCpd
Cpd
https://wiki.onap.org/display/DW/Agreed+PNFD+Model

## Slide 15
VNFD Model
https://wiki.onap.org/display/DW/Updated+V2.5.1+VNFD+Model

## Slide 16
PNF A&AI Model
https://wiki.onap.org/display/DW/Example%3A+PNF+in+AAI
PnfsType
Pnfd
pnfName – String [0..1]
pnfName2 – String [0..1]
selflink – String [0..1]
pnfName2Source – String [0..1]
pnfId – String [0..1]
equipType – String [0..1]
equipVendor – String [0..1]
equipModel – String [0..1]
managementOption – String [0..1]
orchestrationStatus – String [0..1]
ipaddressV4Oam – String [0..1]
swVersion – String [0..1]
inMaint – Boolean [0..1]
frameId – String [0..1]
serialNumber – String [0..1]
ipaddressV4Loopback0 – String [0..1]
ipaddressV6Loopback0 – String [0..1]
ipaddressV4Aim – String [0..1]
ipaddressV6Aim – String [0..1]
ipaddressV6Oam – String [0..1]
invStatus – String [0..1]
resourceVersion – String [0..1]
provStatus – String [0..1]
nfRole – String [0..1]
adminstatus – String [0..1]
opertionalStatus – String [0..1]
modelCustomizationId – String [0..1]
modelInvariantId – String [0..1]
modelVersionId – String [0..1]
pnfIpv4Address – String [0..1]
pnfIpv6Address – String [0..1]
1
5000

## Slide 17
SOL 001 Civic Address RFC 6225 Geolocation

## Slide 18
3GPP TS32.
Some IOC of TS 28.622 are derived from IOCs in TS 28.620 (Federation Umbrella Information Module)
BR,
Jing
From: Andrianov, Anatoly (Nokia - US/Naperville) Sent: Friday, November 22, 2019 8:29 AM To: Cheung, Ben (Nokia - US/Murray Hill) <ben.cheung@nokia.com> Cc: Ping, Jing (NSB - CN/Chengdu) <jing.ping@nokia-sbell.com>; Andrianov, Anatoly (Nokia - US/Naperville) <anatoly.andrianov@nokia.com> Subject: RE: 5G Configuration / Resource Model
Hi Ben,
Yes, 5G NRM is in TS 28.541. For complete 5G picture you also need to look at TS 28.622 (generic NRM) and TS 28.632 (inventory NRM). There are several NRMs for LTE… for 5G we tried to consolidate all necessary information in one place, but as you may see (28.622 and 28.632) it’s not the case now.
-Anatoly
P.S.: I’m CC-ing Jing – she is the rapporteur of 5G NRM

## Slide 19
Sources
3GPP TS28.501
TMF GB922
Location (Place)
RFC 6225
Geo Location
A&AI Schema
SDC AID
ONAP Platform
Information Model
Complex Object
Place object
ETSI SOL 001
Civic Address
ORAN WGx
3GPP
Inventory
ITUT X.731
Op/Admin
3GPP
Operational
3GPP TS32.106
3GPP TS28.540
5G NRM
3GPP TS28.541
5G NRM
3GPP TS28.620
FNIM UIM
3GPP TS28.622
Generic NRM

## Slide 20
3GPP TS28.622
Generic NRM
3GPP TS28.620
FNIM, UIM
* Federated Network Information Model (FNIM) , Umbrella Information Model (UIM)

## Slide 21
3GPP TS28.622
Generic NRM
3GPP TS28.620
FNIM, UIM

## Slide 22
3GPP DU Models from TS28.541, 620, 622

## Slide 23
Enhance Platform Information Model
DESIGN TIME
xNF Resource
5G NRM
Generic NRM
Platform
Information
Model ++
RUN TIME
Service CSAR
3GPP TS28.620 FNIM UIM
TS28.622 Generic NRM
3GPP TS28.540 5G NRM
3GPP TS28.541 5G NRM
Domain & Vendor specific
SDN-C (etc)
C&PS Database

## Slide 24
Generic Application Model
DESIGN TIME
xNF Resource
5G NRM
Generic NRM
Generic
Application
Model
Platform
Information
Model
RUN TIME
Service CSAR
3GPP TS28.620 FNIM UIM
TS28.622 Generic NRM
3GPP TS28.540 5G NRM
3GPP TS28.541 5G NRM
+ Domain & Vendor specific
SDN-C (etc)
C&PS Database

## Slide 25
(Zu) Use case driven, in current use cases, use SDN-C
For node configuration, C&PS stores the config data
Need to understand the application model, no other run-time component
Needs this model, so it would be nice to NOT significantly change the PlfrmInfoModel
The 3GPP model is well-defined, doesn’t make sense for ONAP to redefine it.
CNF/VNF (Fred) the generic APP-C using CDS as the modeling approach would fit this model well. Intended to
Encompass application model, and deal w/ configuration manipuatlion of application model > turn into
Specific implementations. CDS & APP-C . xNF consideration. General abstraction problem
Unification strategy to join SDN-C and APP-C into one entity. Yuriy for CDS.
CDS – GUI – define the (3GPP model) model that you can import; enable you to input the model and instance specific configuration to talk to each instance. Define models for manip application data. Define a model (importing the 3GPP model) and have the manipulation svc to implement the configuration associated w/ the xNF.
ACTION ITEM: PNF resource instantiated by ONAP. The issue of non-unification. Could interact w/ PNF. Yuriy.
(Andy) Maybe we introduce “core” sub-model to the Platform information that might accompany the G-A-M solution. Creating a “hybrid” solution, where the G-A-M serves the MAIN data model for xNFs, and this adjunct model maybe a way to SUPPLEMENT the P.I.M. w/ information that G-A-M solution falls short on, (1) isolates the changes thus there is not a big change to the P.I.M. (2) covers all the bases, “management level” that G-A-M 100% sufficient.

## Slide 27
PNFD Model
NsVL3
CU
1
CP6
5G RAN
CP4
NsVL2
DU:
1-N
CP1
CP3
CP7
Logical view
CP2
NsVL1
CP5
CP1
CP1 to CP6: Ext connection points (e.g. Control plane, data plane, management, etc
NsVL1
NsVirtual link for each type of connection types
Note: These VL may also can represent transport network technologies used.
ECP7
CP7: Ext connection point(s) for network core elements.
VNFD
PNFD
NSD

## Slide 28
Example: TOSCA Service Template
tosca_definitions_version: tosca_simple_yaml_1_2
description: 5G RAN simple example
imports:
- etsi_nfv_sol001_nsd_2_6_1_types.yaml
node_types:
tosca.5gexample_NS:
derived_from: tosca.nodes.nfv.NS
properties:
descriptor_id:
flavour_id:
topology_template:
substitution_mappings:
node_type: tosca.5gexample_NS
requirements:
virtual_link: [ CU, virtual_link_XYZ ] # the External connection point of CU
node_templates:
my_5gservice:
type: tosca.5gexample_NS
properties:
interfaces:
Nslcm:
CU:
type: tosca.nodes.nfv.5Gexample_VNF1 # this type is described in another service template
properties:
flavour_id: simple
vnf_profile:
requirements:
- virtual_link_1: NsVirtualLink_1
- virtual_link_2: NsVirtualLink_2
- virtual_link_3: NsVirtualLink_3
DU_1_to_N:
type: tosca.nodes.pnf.5gexample_DU # the description of this type is described in another service template
properties:
requirements:
- virtual_link_1: NsVirtualLink_1
- virtual_link_2: NsVirtualLink_2
- virtual_link_3: NsVirtualLink_3
- dependency: CU
NsVirtualLink_1: #
type: tosca.nodes.nfv.NsVirtualLink
properties:
connectivity_type:
vl_profile:
NsVirtualLink_2: #
type: tosca.nodes.nfv.NsVirtualLink
NsVirtualLink_3: #
type: tosca.nodes.nfv.NsVirtualLink
# omitted here for brevity

## Slide 29
Creating a 5G Service
Need to create a 5G service in R6
Currently individual services can be created using VNFs and PNFs
Modeling of 5G NFs is work ongoing in Platform (Internal) Info Modeling Committee
Architecture sub-committee needs to approve modeling committee proposal before requirements can go to SDC
SDC needs to receive requirements so service models can be created
Schedule in R6 M0 (Sept 5 2019).
5G Use Case Proposed for R6.
“Target” 5G Service. Multiple options. 3GPP options 2/7/8. Based on U/C.

## Slide 30
Creating a 5G Service
Attribute | Format
networkId | string
cellId | string
pciValue | uint64
nbrList | list of cellId
lastModifiedTS | timestamp
pnf-id | string
Attribute | Format
cellId | String
target_cell_id | String
ho | BIT(1)
Cell (Object)
Cell_Nbr_Info (Object)
  Config DB (MariaDB) used by PCI-H-MS (step 4b) and OOF (step 7)
  Query API (swagger JSON spec) exposed to other ONAP modules
  cellId needs to be globally unique (assumed eCGI) and align with ONAP YANG model, ORAN, 3GPP
  pnf-name/pnf-id indicates netconf server to be used for interactions regarding cells
  ‘ho’ property added to support ANR use case

## Slide 31
Cell Management, Cell object, Cell Configuration
Benjamin Cheung, PhD

## Slide 32
Cell Definition
DEFINITION: Cell in wireless communication technologies, the geographical region that is covered by a transmission facility. The term «cell» is most often used in reference to cellular phone technology, but it can also be used in reference to the coverage areas for transmission of cordless telephones, satellite transmissions, wireless local area networks (LANs), packet radio, and paging technologies.
https://networkencyclopedia.com/cell-in-wireless-communication/
Carrier-Sector
RU
DU
CU
Antenna
DU
RAU
CPRI
CU
RF
1
N
1
N
Carrier-Sector
Carrier-Sector
Carrier-Sector
5G Base Station
…
Logical Entity
that the RU services
1
N
CELL
ONAP doesn’t
Manage the RU
Per se except for
Front-haul

## Slide 33
Cell Management
VISIBILITY / EXISTENCE OF CELL
1 USE CASES –
1a E2E Network Slicing - Slicing – xNFs involved in a slice (TA/RA), where is the “slice” stored? NSI in A&AI. Alloted NF (ANF). Slice Service.
1b OOF/SON/PCI What use cases are Using it – OOF/SON/PCI which needs to store some cell info, KPI HO success rate. CellID. What Attributes to update. Key Identifiers. Neighbor Lists.
2 EXISTENCE - does ONAP need to know of existence of Cell? What does it need to know about a Cell?
MANAGEMENT OF CELL
1 LIFE CYCLE - Life Cycle of a Cell (FCAPS); OA&M interface at ONAP (no interface) all the information related to a cell is reported/retrieved from the DU. -> ONAP command “xyz Cell” (add/del/ onboard). ONAP would not “manage” a cell at all; it would manage a DU -> rather information for a cell (adds/deletes) are covered by the C&PS database solution.
2 FUNCTION - What would it do with a Cell
3 ADD/DELETE - For add/delete Cell case -> the corresponding activity in ONAP is to add/delete C&PS database entry. The DU informs ONAP that a Cell is added/deleted, then C&PS updates database accordingly. ONAP management level to add/delete would be a configuration update.
4 MODELING - How would it Model it? (Info Model). A DU is a MOC. A Cell is a Logical object. -> No modeling is needed.
INFORMATION ABOUT CELL
1 PERFORMANCE MANAGMENT - Cell specific KPIs, PM generated & reported from DU. COUNTERS collected & reported by the DU. KPI derived from counters. ONAP doesn’t need to interact with a RU/Cell w.r.t. PM (Counters & KPI).
2 CONFIGURATION MGMT - Cell configuration info - Cell related information stored in C&PS.; Cell – A cell is a logical object. CDS. Cell related information is use case specific (PCI and E2ENS). (1) define, (2) store, (3) loop back to the xNF.

## Slide 34
C&PS
Database
PNF #106
Cell #1 – Logical Object
Cell #2
Cell #3
RECORD ELEMENT
INDEX = PNF #106
Parameter #1
Parameter #2
Parameter #3
Logical object, Cell #1
Cell Parameter #1
Cell Parameter #2
Cell Parameter #3
RECORD ELEMENT
INDEX = Logical Object #111
Parameter #1
Parameter #2
Parameter #3
State Info
Associations
{ PNF #106 } List
Cardinality Rules
Linking Restrictions
RECORD ELEMENT
INDEX = PNF #106
Parameter #1
Parameter #2
Parameter #3
State Info X.733
Associations
{ Logical Object #111 Cell #2 }
Cardinality Rules
Linking Restrictions
C&PS Database (Run-Time View)

## Slide 35
Appendix
Benjamin Cheung, PhD

## Slide 36
PNF (Full) A&AI Model
https://wiki.onap.org/display/DW/Example%3A+PNF+in+AAI