## Slide 1: CIR Change Process Flow
Mehmet Toy, Ph.D
October, 2018

## Slide 2: CIR on Demand
Prior to an on-demand request, ENNI, UNIs and EVC between off-net and on-net locations of a SP is established for Access E-Line:
  Customer via user portal requests change within CIR bounds for CIR per bandwidth profile flow , <CIRlb , CIRub > for OVC End Point
    Immediately
      With no end time for new CIR , CIRelastic where CIRelastic = CIRlb +NxCIRincrement <List of available CIR rates>
      With end time for new CIR, CIRelastic where CIRelastic = CIRlb +NxCIRincrement
        After end time elapses, the rate becomes CIRlb
    At certain time and day in the future
      With no end time for new CIR , CIRelastic where CIRelastic = CIRlb +NxCIRincrement
      With end time for new CIR , CIRelastic where CIRelastic = CIRlb +NxCIRincrement
        After end time elapses, the rate becomes CIRlb
Note that CIRlb , CIRub , CIRincrement values of CIR have been established in SONATA as part of pre-negotiated contract. As CIR values are set by the user at user portal, these values need to be confirmed by SP. Once they are confirmed, billing entity must be informed.

## Slide 3: CIR Change Process Flow
Customer
SP ECM
PART SOF
SP Portal
SP SOF
SP ICM
PART ICM
PART ECM
Request CIR Change for Service (ALEGRO or CANTATA+LEGATO)
Validating User, Location, Service & if rate within bounds
Invalid Credentials or Invalid Request or Unavailable Resources &
Please try it later
Request CIR Change
for Service (INTERLUDE )
Validate service-interface map &
resource
availability
CIR Change at
Interfaces
(UNI,NNIs,ENNI) (PRESTO)
Invalid Request or
Unavailable Resources&
Please try it later
CIR Change at EPs
(ADAGIO)
Conf. or Deny CIR
Change at EPs
Confirm or Deny CIR Change for PART OVC
Test new CIR for SP OVC
Confirm or Deny CIR Change
for SP OVC
Test failed for new CIR for SP OVC
Unavailable Resources
Please try it later
CIR Change at
Interfaces (UNI,
NNIs, ENNI) (PRESTO)
Invalid Request
or Unavailable
Resources
Invalid Request or
Unavailable Resources&
Please try it later
CIR Change at
End Points
(ADAGIO)
Conf. or Deny
CIR Change at
End Points
Conf.or Deny
CIR Change
at Interfs.&EPs
Test new CIR for PART OVC
Confirm or Deny CIR Change
for PART OVC
Test failed for new CIR for PART OVC
Unavailable PART Resources
Unavailable Resources
Please try it later
1
2
4
3
5
6
Validate service-end point map &
resource
availability
4b
5
6
6
6
8
7a
8
8
8
8
9
9
9
9
10
10
10
10
12
4a
11
12
12
13
13
11
Represents messages crossing Interlude
Conf.or Deny CIR Change at interfs.&EPs
Confirm or Deny CIR Change for
PART OVC
10
CIR for Service
is Changed
CIR for Service is Changed
15
Test new CIR for EVC
14
Unavailable Resources&
Please try it later
7
OSS
(Billing)
(LEGATO)
16
17
CIR Change
is
Not Granted
CIR is Changed
from <x> to <y>
OSS
(Billing)
(LEGATO)
17
CIR Change
is
Not Granted
16
CIR is Changed
from <x> to <y>
7
7a
Validate service-
interface map &
resource availability
Validate service-end point map &
resource
availability
8a
CIR for Service is Changed
8b
Invalid Request or
Unavailable Resources&
Please try it later
Confirm CIR Change for EVC
Or Deny CIR Change for EVC
Validate service-
interface map &
resource availability
4c
4d
Invalid Request or Unavailable Resources
Invalid Request or Unavailable Resources&Please try it later
4e
Step 9, 10,12 and 14 could be optional