## Slide 1: OOF-SON: 5G Self-Organizing Network (SON) using ONAP Optimization Framework (OOF): Requirements Proposal for Guilin
Collaborators : AT&T, Wipro, IBM, highstreet technologies, TechMahindra, Lumina Networks, Nokia, Reliance Jio, Rutgers Winlab
Acknowledgments : Feedback and support from participants in ONAP OOF-SON team calls
Presenters : Shankaranayaranan N K, Swaminathan S
March 16, 2020

## Slide 2: Summary of Requirements (Under Discussion)
Category | Requirement | Content | Priority
Interoperability | O-RAN alignment (VES, O1 interface) | Receive Configuration Management (CM) notifications over VES (instead of netconf) | HIGH
Functional | RAN Database (Runtime Config DB), including any new RAN models | Data models/DB schema and APIs to be generated from yang models Details of cells to be stored with PNF reference in AAI Modeling of RAN functions and objects | HIGH
Platform | Control Loop Coordination (CLC) extensions | Collaborate on CLC extensions (queueing, priority, …) | HIGH
Functional | Integration of SON and PNF onboarding functions | New cell(s) addition – extension to PNF onboarding & registration scenario, addition of new cell later to a PNF Initial assignment of PCI to a cell | MEDIUM
Functional | New SON function to evolve ONAP platform | SON based on data/KPI analysis CLC interaction Machine Learning (ML) aspects in DCAE | MEDIUM
Functional | SON Lifecycle | Role of SO, SDC, CLAMP (for SON service/feature deployment) | LOW
Interoperability | Real gNB interaction | Interaction with real gNB in lab | LOW

## Slide 3: ONAP SON alignment with O-RAN
ONAP
Centralized SON (cSON) functions
Control Loop actions
Simulated RAN
~2000 Cells
Neighbor list, PCI
Cells/GNBs
RIC
Yang model
O1 - Netconf interface
O1 - VES
outputs
Config change
FM/PM KPIs
CM Notify
VES
DB schema &APIs generated from yang models



Guilin scope

Receive Config Management (CM) notification from RAN over (standardized) VES (Priority 1)
ONAP DB schema and APIs to be generated from associated ORAN network yang models (Priority 1)
Send Config change to RAN (to update neighbor list or PCI value) using O-RAN aligned yang models (Priority 2)
Note: Substantial work in RAN Simulator to develop/test/demo ONAP functionality
This has dependency on progress within O-RAN

## Slide 4: ONAP SON alignment with O-RAN

## Slide 5: ONAP RAN Database (Runtime Config DB)
Objectives
  Build upon 5G SON RAN Database started in Dublin & Frankfurt
  Collaborate with (new) Rel 7 Runtime Config DB project to make this a shared ONAP functionality
Dependencies
  Availability of O-RAN yang models and VES specification
  Runtime Config DB, DCAE
 | Frankfurt (Release 6) | Guilin (Release 7)
RAN database | ConfigDB (part of SDN-C CCSDK) | Runtime Config DB (RCDB) (New Rel 7 function)
Config (CM) notification | Pre-standard VES message | ORAN standard VES CM Notify message
CM Notify processing | RANSim –> DMaaP -> SDNR | RANSim -> DCAE -> DMaaP -> SDNR
CM update | SDNR -> ConfigDB | SDNR -> RCDB

## Slide 6: Control Loop Coordination
RIC (non-RT)
Co-ordination, Decisions (Policy)
Optimization (OOF)
Action
(SDN-R)
Data Collection, & Analysis
(DCAE)
Collaborate with Policy/Control Loop Team for extensions to Control Loop Coordination (CLC)
Build further on Frankfurt work to enhance Platform capabilities, for example:
  Queueing/de-queueing (illustrated in the figure)
  Discard outdated loop actions
  Prioritization/pre-emption
CLC has much wider implications to ONAP as a platform, and not just restricted in scope to SON use cases
FM, PM, CM
A-1/O-1
A-1/O-1
(Near RT) RIC
ORAN Radio Network
1a
1b
1c
1d
1e
1f
2a
2d
2e
CL2
Control Loop 1
Control Loop 2
Illustration of CLC with queuing
2b
2c

## Slide 7: SON Lifecycle – Cell addition/configuration
PNF
Contacts ONAP
PNF connects to ONAP via a Registration Event
PNF Registration Handler (PRH) processes the event
PNF
Activation
Connection points configured
Second part of PNF service instantiation
PNF configured and ready to provide service
PNF
Boot-strapping
PNF Powers up and Boot-straps
PNF performs a “Plug and Play” procedure
Equipment vendor proprietary steps
3
4
5
PNF Modeling
1
PNF Instance
Declaration
PNF Infrastructure Service Declaration
First part of PNF instantiation
DCAE & AAI Entry with PNF ID (e.g. MAC address)
2
Design
Resources Definition/Services Definition
SDC: PNF (physical element) Modeling
Distribution of types
Run-Time (Instances)
Cell Configuration
(for SON)
New cells configured & manageable from ONAP
Include PCI assignment to cells associated with PNF
and update NR info from cells
6
New cell addition by ONAP – extend PNF Plug-and-play use case
Assign initial PCI value (any other configuration?)
Points for further analysis and discussion
  Modeling of RAN “Cell” in ONAP
  ‘Discovery’ of a new cell (provided by PNF?) and subsequent configuration (by ONAP?) before it is active; removal of a cell (dis-associate from PNF)
  Handling of “shared”/”virtual” cells
  O-RAN alignment
    Cell discovery, initial configuration, new cell addition/removal later, initial PCI assignment
  Initial NR details update in ONAP (topology discovery?)
Notes: SDN-R impacts
Interactions with Runtime Config DB
SON-Handler MS and OOF interface updates (no existing PCI)? Or will SO trigger OOF directly?
32.501 REQ_SCRCD_CON_1 (Self configuration of eNodeB) (check similar aspect for 5G gNodeB)

## Slide 8: Other requirements (under investigation)
New SON use case to extend ONAP platform capabilities
Handle large volume of real-time data (HV-VES), and process it
Application of ML in ONAP (specifically in Control Loops)
CLC
SON Lifecycle
  Role of SDC, SO and AAI for “ONAP SON Service”
  Deployment of Control Loop via CLAMP
  Instantiation of SON-Handler MS when the first cell is activated
Interaction with real gNB and/or O-RAN software components

## Slide 9: Business Drivers
Executive Summary
SON (Self-Organizing Networks) functionality is an essential part of 4G networks, and will be even more critical for 5G. SON enables automation to improve network performance and efficiency, improve user experience, and reduce operational expenses and complexity. The objective of the OOF SON use cases is to develop an ONAP-based SON platform using the ONAP Optimization Framework (OOF). We have taken a phased approach since SON is complex, and SON for 5G is still evolving. We started with the Physical Cell Identity (PCI) optimization SON use case in Casablanca, and added centralized Automated Neighbor Relations (ANR) aspects in Dublin. In Frankfurt, we included adaptive SON functionality, took initial steps in O-RAN alignment and collaborated with Policy Control Loop Co-ordination (CLC). For Guilin, we will align with ORAN interfaces, be the early adopter of the new Runtime Config DB (e.g. generate DB schemas and APIs based on yang models), cover SON-related workflow for new cell addition, introduce another SON use case to add new platform capabilities, and collaborate on further extensions to CLC. We will also pursue alignment with industry trends for open interfaces & open models for RAN interactions, in particular with O-RAN.
Business Impact
SON is an essential feature in mobile networks, and relevant to every operator. Any ONAP-based network deployment for 5G will benefit from an ONAP-based SON solution, which provides a disaggregation of SON functions into modules aligned with the ONAP architecture. Operators and vendors will both benefit from the ability of vendors to bring best-in-class solutions to each module, while leveraging the benefits of a community-supported open platform. This will enable faster development of innovative solutions. The approach taken could very well be evolved to address SON use cases whose scope extends beyond just the RAN.

## Slide 10
Business Markets
SON for 5G is relevant to all 5G operators and markets.
Funding/Financial Impacts
SON functions reduce OPEX since the automated self-organizing functions are an efficient approach to continuously optimize network configurations to improve performance and respond to network conditions.
Organization Mgmt, Sales Strategies
There are no additional organizational management or sales strategies for this beyond whatever is required for ONAP deployment to support 5G.

## Slide 11
Thank You!