## Slide 1: Core NSSMF Implementation Options For ONAP G Release
Participants: CMCC, Wipro, Huawei, AT&T, Amdocs, Verizon, Reliance Jio, Tencent, China Telecom, Tech Mahindra, DT
Authors: Milind Jalwadi (Tech Mahindra)
May 22, 2020

## Slide 2: Goals
Implement Core NSSMF for following features
  Network slice subnet instance creation
  Network slice subnet instance activation
  Network slice subnet instance deactivation
  Network slice subnet instance termination
Core NSSMF to implement sub-set of features as prescribed in 3GPP TS 28.531
Demonstrate 5G Core orchestration as part of slice ordering using containerized workloads (Dummy 5G Core NFs)
Demonstration of following scenarios for slicing requirements (ONAP SO acting as NFVO)
  Non-shared NSST resulting in NSSMF-NFVO interaction to orchestrate new CNFs (NFs) with day 0 configurations
  Shared NSST resulting in NSSMF->NFVO interaction to configure the specific NFs with the re-used S-NSSAI

## Slide 3: Implementation Options
Functional Options
Implementation Options
Option 1:
NSSMF->ExtAPI (NBI)
Options 2:
NSSMF->SO WF
NSSMF->NFVO
ONAP SO Based
NSSMF->NFVO
ONAP VFC (ETSI) Based
Both Functional options can be supported by NSSMF without any custom / specific code
The NS to be associated with Network Slice sub-net to be designed with service category as “Network Service” and Instantiation Type as “macro” in SDC
Both Functional options can be supported by NSSMF without any custom specific / code
The NS to be associated with Network Slice sub-net to be designed with service category as “E2E Service” in SDC
Custom / Specific code only for this option needs to be developed in NSSMF
NSSMF to trigger the internal “macro” workflow as part of NFVO invocation
Custom / Specific code only for this option needs to be developed in NSSMF
NSSMF to trigger the internal “E2E” workflow as part of NFVO invocation
Recommended option

## Slide 4: NSSI / Slice KPI monitoring
It is suggested that the KPI / Slice monitoring function of core NSSMF shall be implemented as DCAE micro-service
The closed control loop actions and policy design should ensure that the KPI monitoring decisions ex. Scale-out, NF configurations, Slice configurations etc. are implemented using the existing ONAP features as part of closed control loop operations
Should we add NSSMF as actor in the policy configurations? This could be a desired feature and a cleaner design

## Slide 5: Architecture view – Option 1 (NSSMF Invokes ExtAPI)
Slice Lifecycle Flows (Existing)
NSSMF – NFVO Flow (New)
UUI
ExtAPI
VFC
Core NSSMF
NSMF
CSMF
SO
CDS
Multicloud
serviceOrder API
with slicing
parameters
Call E2ESericeInstance
API with serviceType=CST
1
E2E workflow
8a
OOF
AAI
Macro workflow
Call service Instance API
2
3
4
5
6
9
K8s Plug-in
K8s Cluster
7a
7b
8b
10
11
NSSMF->NFVO Interaction
NFVO Orchestration Flow

## Slide 6: Option 1 (NSSMF Invokes ExtAPI) : Solution Highlights
Slice Order operation invoked from UUI. The scenario assumes that the slice is non-shared and it would result NSSMF to call NFVO to orchestrate new NFs
NBAPI calls E2E Service Instance API on SO with service type to be CST so that CSMF workflow could be invoked
E2E Work flow invokes CSMF workflow
CSMF and NSMF workflow processing
NSMF invokes core NSSMF for further processing
NSSMF as required invokes ExtAPI Service Order API whenever the NFs need to be orchestrated
Based on the service category (E2E or Macro) the NBAPI will accordingly invoke SO APIs / Workflows
The Service orchestration either through the macro flow or E2E flow is then executed
9,10,11 – The containerized workload orchestration flow

## Slide 7: Option 1 – NF Configuration Requirements
The Slicing requirements would require in some cases to re-use the existing S-NSSAI. In such cases the NFVO would need to configure specific NFs
Need to check the below ONAP features in this regards
  The NSSMF should call SO Work Flow to configure the NFs as part of day 1/n configurations
  The day 1 configuration / LCM operations as supported by SO / CDS for VNFs and CNFs
  It should be possible model / design the configurations using CDS such that the slice parameters passed by NSSMF could be referred to by CDS and apply the configuration to desired NFs using Multi-Cloud / K8s plug-in
Next two slides detail the flow for NF configurations as part of slicing requirements

## Slide 8: Architecture view – Option 1 (NSSMF -> NFVO, Day 1/n Configuration)
Slice Lifecycle Flows (Existing)
NSSMF – NFVO Flow (New)
UUI
ExtAPI
VFC
Core NSSMF
NSMF
CSMF
SO
CDS
Multicloud
serviceOrder API
with slicing
parameters
Call E2ESericeInstance
API with serviceType=CST
1
E2E workflow
7
OOF
AAI
Macro workflow
2
3
4
5
6a
8
K8s Plug-in
K8s Cluster
6b
9
10
NSSMF->NFVO Interaction
NF Configuration Flow

## Slide 9: Option 1 (NSSMF -> NFVO, Day 1/n Configuration) : Solution Highlights
Slice Order operation invoked from UUI. The scenario assumes that the slice is shared and it would result NSSMF to call NFVO to “configure” existing NFs
NBAPI calls E2E Service Instance API on SO with service type to be CST so that CSMF workflow could be invoked
E2E Work flow invokes CSMF workflow
CSMF and NSMF workflow processing
NSMF invokes core NSSMF for further processing
Based on the Service Category, NSSMF shall invoke SO WF (If service category is Network Service) or VFC API (If service category is E2E service) for NF configurations.
7,8,9,10 – The existing ONAP workflows for day 1/n configurations for containerized NFs

## Slide 10: Option 2 (NSSMF Directly Invokes SO Work Flows)
Custom code needs to be written for both the approaches Viz SO and VFC based orchestration
Any other pros and cons needs to be discussed
Currently not recommended after internal discussions

## Slide 11: NSSMF Features – Network slice subnet instance creation
Use case stage | Evolution/Specification | Considered for implementation?
Step 1 (M) | Based on the network slice subnet related requirements received, the network slice subnet provisioning management service provider decides to create a new NSSI or use an existing NSSI. | Y
Step 2 (M) | If an existing network slice subnet instance is decided to be used, the network slice subnet provisioning management service provider may trigger to modify the existing network slice subnet instance to satisfy the network slice subnet related requirements. Go to “Step 8”. Otherwise, the network slice subnet provisioning management service provider triggers to create a new NSSI, the following steps are needed. | Y
Step 3 (O) | If the required NSSI contains constituent NSSI(s) managed by other network slice subnet provisioning management service provider (s), the first network slice subnet provisioning management service provider derives the requirements for the constituent NSSI(s) and sends those requirements to the corresponding network slice subnet provisioning management service provider (s) which manages the constituent NSSI(s). The first network slice subnet provisioning management service provider receives the constituent NSSI information from the other network slice subnet provisioning management service provider (s) and associates the constituent NSSI(s) with the required NSSI. | N
Step 4 (M) | Based on the network slice subnet related requirements received and SliceProfile [6], the network slice subnet provisioning management service provider decides that to satisfy the NSSI requirements, the part of the network controlled by certain NFVO should be involved. The network slice subnet provisioning management service provider determines the NS related requirements (i.e. information about the target NSD and additional parameterization for the specific NS to instantiate, see clause 7.3.3 in ETSI GS NFV-IFA013 [3]). | Y
Step 5 (M) | Based on the NS related requirements, the network slice subnet provisioning management service provider triggers corresponding NS instantiation request to NFVO via Os-Ma-nfvo interface as described in clause 6.4.3 in TS 28.525 [2], and the NFVO performs NS instantiation. (see note) | Y
Step 6 (M) | The network slice subnet provisioning management service provider associates the NS instance with corresponding network slice subnet instance (e.g. allocation of the management identifier of NSSI and mapping with the corresponding identifiers). | Y
Step 7 (M) | The network slice subnet provisioning management service provider is using the NF provisioning service to configure the NSSI constituents. In case of RAN NSSI, the configuration contains RRM policy information for individual Radio cells. In the cells shared by multiple NSSIs such policy includes guidance for split of Radio resources between the NSSIs. | Y
Step 8 (M) | The network slice subnet provisioning management service provider notifies the provisioning service consumer with the NSSI information (e.g. the management identifier of NSSI) and the NFVO identity when relevant. The network slice provisioning management service provider associates the NSSI with the NSI. | Y
Note: Highlighted text in RED not supported

## Slide 12: NSSMF Features – Network slice subnet instance activation
Use case stage | Evolution/Specification | Considered for implementation?
Step 1 (M) | The network slice subnet provisioning management service provider identifies inactive constituents (e.g. NSSI, NF) of the NSSI and decides to activate those constituents. | Y
Step 2 (M) | If the constituent of NSSI is managed directly by the the network slice subnet provisioning management service provider, the network slice subnet provisioning management service provider activates the NSSI constituent directly. | Y
Step 3 (M) | If an NSSI constituent is managed by other network slice subnet provisioning management service provider, the network slice subnet provisioning management service provider requests other network slice subnet provisioning management service provider to activate the constituent NSSI. | N
Step 4 (M) | If an NSSI constituent is an NF managed by NF related provisioning management service provider, the network slice subnet provisioning management service provider request the NF related provisioning management service provider to activate the NF (e.g., activate the NF in sleep mode, turn on the ports). | Y
Step 5 (M) | The network slice subnet provisioning management service provider receives response indicating that NSSI constituents are all activated. | Y
Step 6 (M) | The network slice subnet provisioning management service provider sets the state of the network slice subnet instance as active and sends response to its authorized consumer. | Y
Note: Highlighted text in RED not supported

## Slide 13: NSSMF Features – Network slice subnet instance deactivation
Use case stage | Evolution/Specification | Considered for implementation?
Step 1 (M) | The network slice subnet provisioning management service provider identifies the NSSI constituents that need to be deactivated. | Y
Step 2 (M) | If the constituent of NSSI is managed directly by the network slice subnet provisioning management service provider, the network slice subnet provisioning management service provider deactivates the NSSI constituent directly. | Y
Step 3 (M) | If an NSSI constituent is managed by other network slice subnet provisioning management service provider, the network slice subnet provisioning management service provider requests other network slice subnet provisioning management service provider to deactivate the constituent NSSI. | N
Step 4 (M) | If an NSSI constituent is managed by the NF related provisioning management service provider, the network slice subnet provisioning management service provider requests the NF related provisioning management service provider to deactivate the NF. | Y
Step 5 (M) | The network slice subnet provisioning management service provider receives response indicating that corresponding NSSI constituents are deactivated or not deactivated (e.g., shared constituents cannot be deactivated). | Y
Step 6 (M) | The network slice subnet provisioning management service provider sets the state of the network slice subnet instance as inactive and send response to its authorized consumer. | Y
Note: Highlighted text in RED not supported

## Slide 14: NSSMF Features – Network slice subnet instance termination
Use case stage | Evolution/Specification | Considered for implementation?
Step 1 (M) | Based on the request, the network slice subnet provisioning management service provider decides whether the NSSI should be terminated. If the decision is the NSSI should be terminated, go to the Step 2. If the decision is the NSSI is not terminated (e.g., the NSSI is shared or the network slice subnet provisioning management service provider decides to keep the NSSI for later use), the network slice subnet provisioning management service provider disassociates the NSSI from its consumer and provides feedback to the authorized consumer, maybe with removing its consumer’s configuration or not. Go to Step 5. | Y
Step 2 (M) | If the NSSI consists of constituent NSSIs that are not managed directly by the network slice subnet provisioning management service provider, the network slice subnet provisioning management service provider sends a request to other network slice subnet provisioning management service provider(s) indicating that the constituent NSSIs are no longer needed for the NSSI. | Y
Step 3 (M) | If the NSSI is associated with NSI, the network slice subnet provisioning management service provider disassociates the NSI with the NSSI to be terminated, and the network slice subnet provisioning management service provider may trigger corresponding NS instance related request to NFVO indicating that the NSI is no longer needed for the NSSI. | Y
Step 4 (M) | If there exists a transport network segment used by the NSSI, the network slice subnet provisioning management service provider may indicate that the transport network segment is no longer needed to support the NSSI. | N
Step 5 (M) | The network slice subnet provisioning management service provider sends response to its consumer. | Y
Note: Highlighted text in RED not supported

## Slide 15
Thank You!