## Slide 1: E2E Network Slicing: OOF Impacts & Design
Isaac Manuelraj
Swaminathan S
Jan 27th 2020

## Slide 2: OOF Impacts
A new interface OOFE-6 is introduced for E2E Network Slicing use case for Network Slice Template (NST) and Network Slice Instance (NSI selection.
When a new slice is requested to be created by operator, SO as CSMF needs to know the network slice template (NST) using which the slice needs to be created. So the CSMF workflow of SO will request OOF to suggest appropriate NST(s) for the requirement (Service Profile) which is provided by the operator to SO.
After obtaining the NST, NSMF workflow of SO requests OOF for appropriate NSI(s). At a high-level 2 scenarios are possible:
  If the operator request to SO indicates that an existing NSI cannot be shared , then SO has to launch the steps for creating a new NSI.
  If the operator request to SO indicates that an existing NSI can be shared, SO requests OOF for appropriate NSI(s). In this case, OOF can return existing NSI(s), and/or provide recommendation for creating a new NSI.
Notes: Inventory updates, interface
Long-term capability set
Policy and API definition

## Slide 3: Points to discuss – SO and OOF interactions, and SO updates for Frankfurt
API finalization
Layout of Service Profile and Slice Profile w.r.to mandatory and optional parameters
Code in SO to handle more than 1 option – NST as well as NSI response
Code in SO to decipher the recommendation from OOF for multiple sub-nets. For Frankfurt, we can assume 1 subnet only and keep it simple.
Callback URL to be implemented in SO
SO making a single call to OOF for NSI allocation and not separately for NSSI recommendation
Slice profile derivation from service profile/operator inputs – this functionality is to be moved to OOF
  Considering this, should SO call OOF even when an existing NSI cannot be shared (because operator does not want this)? Or shall we keep it simple by keeping it within SO itself for Frankfurt?

## Slide 4: Design Details

## Slide 5: Assumptions
We will create only 1 NST per sST (e.g., one NST for one type of eMBB, one NST for one type of mMTC, etc.) (wherein type refers to characteristics and not dimensions or specific KPI values)
We will define 3 “Cabability Sets” per NST.
The NST id and Capability Set will be stored in AAI for each NSI.
Updating AAI with NST, active NSI and NSSIs, and their capacity limits will be responsibility of SO or NSSMF.

## Slide 6: OOF Impacts – NST selection
Principle: We will not create separate NSTs for the same ‘slice type’ with different attribute values.
Steps
Upon reception of API call for NST selection
  Input: Service Profile parameters
  Extract performance requirements that are applicable (i.e., non-zero or non-null values).
  Determine all NST(s) that are a best match of the performance requirement attributes (not attribute values)
  Question: If service profile already contains sST, can we not directly choose ALL NST(s) with the same sST? In such a case, what additional filter to be applied to determine best match?

## Slide 7: OOF Impacts – NSI/NSSI selection (sharing allowed)
SO triggers OOF with Service Profile and Input_NST id.
Steps in OOF
For the Service Profile, determine a matching “Capability Set”.
Determine if there are any existing NSIs matching the input_NST id (Candidate NSI-List).
  Option 1: Fill input_NST with service profile input values.
  Option 2: Fill input_NST with Capability Set determined in Step 1.
  With the filled in input_NST, determine the best matching NSI(s) in the Candidate NSI-List. (Only those NSIs which are marked ‘shareable’ will be considered).
  How to determine best match – will it based on (capability set – existing service profile param values)? (We don’t have any occupancy or resource utilization data yet)

## Slide 8: Illustration
NST name | Capability Set 1 | Capability Set 2 | Capability Set 3
eMBB | Max UEs = 3000 | Max UEs = 5000 | Max UEs = 10000
mMTC | Device density = 100 | Device density = 200 | Device density = 500
URLLC | Reliability = 99.9 | Reliability = 99.99 | Reliability = 99.999
Q: NST shall contain blank attributes and filled by capability set, or NST shall contain range of parameter values?
Input | Chosen Capability Set | NSI Id | Spare “capacity” | Remarks
Service Profile 1 -> eMBB with Max UEs = 3000 | CS2 for eMBB | 1 | 2000 more UEs can be supported | Already instantiated
Service Profile 2 -> eMBB with Max UEs = 5000 | CS3 for eMBB | 2 | 5000 more UEs can be supported | Already instantiated
New request, Service Profile 3 -> eMBB with Max UEs = 2000. In case of Option 1, both NSI id 1 and 2 will match, and perhaps NSI id 2 will be the best match. In case of Option 2, no NSI will match.
Design Time
Run Time

## Slide 9: New NSI creation
For creating new NSI (will this always be considered or if num-solutions with existing NSIs < min-threshold-num-solns, and/or NST match with existing NSI is < max-threshold-match-level)
  Determine slice profile for each sub-net as follows:
  Option 1
    Based on capability of sub-net determine possible slice profile attribute values for each sub-net. Q: Where will sub-net capability be stored, or capability set corresponding to the NSST-id for that sub-net?
    List down all possible options for each sub-net.
    Shortlist valid e2e combinations which meet the service profile values.
    Choose the best combination(s), e.g., by associating cost for certain attributes per sub-net (e.g., lower latency for core may be higher cost, as it requires resources at the edge).
    Question: How to make sure that determined slice profile aligns/is consistent with the NSST ids within the NST?

## Slide 10: NSI creation
Option 2
Fetch all active (shareable) NSSIs that have ‘spare’ capacity with same NSST-id in each sub-net.
Form e2e NSI with all combinations of NSSIs determined above.
Filter e2E NSI combination which fulfil the Service Profile requirements.
Select the best combination by associating some cost.
Question: What to do when there is no matching/shareable NSSI for a sub-net? (shall we first shortlist feasible slice profile options for remaining sub-nets, and then identify slice profile options for the sub-net that requires a new NSSI to be instantiated?)

## Slide 11: NSSI selection
For each sub-net
  With slice profile determined in previous step, follow the same approach as for e2e slice, but for that sub-net.

## Slide 12: OOF Impacts – NSI/NSSI selection (sharing not allowed)
To be updated

## Slide 13: Following slides will be updated soon

## Slide 14: Logic
When “resourceSharingLevel” is set to “shared”, NSMF of SO will send request to OOF asking for suggested NSI and NSSI that can be shared by the current request. (selectnsi and selectnssi REST API will be used respectively)
When “resourceSharingLevel” is set to “not-shared”, SO will create new NSI and NSSI instances without asking any suggestion from OOF.

## Slide 15: 5G Slice – OOF message flows
SO sends a select NST request to OOF.
OOF returns the NST model information back to SO.
SO sends request to OOF to suggest a NSI, if the slice creation request being handled can share existing NSI.
OOF respond back with valid NSI ID if exist. Otherwise a empty string.
If no suitable NSI is suggested by OOF, SO create the NSI by itself and again request OOF to suggest NSSI which can be shared.
OOF
SO
AAI
SO receives slice creation request
Selectnst(serviceProfile)
(modelUuId, InvariantUuid)
Selectnsi(serviceProfile,
nstInfo)
(nsiId, UuId, InvariantUuid)
Selectnssi(sliceProfile,
nsstInfo)
(nssiId, UuId, InvariantUuid)
GET models
(modelUuId, InvariantUuid)
(nsiId, UuId, InvariantUuid)
(nssiId, UuId, InvariantUuid)
GET serviceinstances
GET serviceinstances

## Slide 16: Logic
To create a slice the user would send the below shown request to CSMF along with the user requirements which is highighted.
When “resourceSharingLevel” is set to shared, NSMF of SO will send a
CSMF request payload looks like shown below:
The “resourceSharingLevel” attribute in the request body indicates whether a existing slice can be shared or new slice needs to be created.
CSMF receives the request and ask OOF to get the Network Slice Template which can be used to create the slice satisfying the user requirement. (selectnst REST API will be used)
CSMF gets the NST information from OOF and request NSMF to create Network Slice sending the NST information.

## Slide 17: Request Response Structure : selectnst
URL: {{oofurl}}/api/oof/v1/selectnst
Method : POST
Request to OOF { "requestInfo":{ "transactionId":"234-675-4328", "requestId":"123-456-7890", "sourceId":"SO", "timeout":600 }, "serviceProfile":{ "latency":20, "areaTrafficCapDL":300, "areaTrafficCapUL":300, "maxNumberofUEs":300 } }
Response: { "transactionId":"234-675-4328", "requestId":"123-456-7890", "requestStatus":"accepted", "statusMessage":"", "NSTInfo":{ "invariantUUID":"23edd22b-a0b2-449f-be87-d094159b9269", "UUID":"46da8cf8-0878-48ac-bea3-f2200959411a", "NSTName":"eMBB service" } }

## Slide 18: Request Response Structure : selectnsi
URL: {{oofurl}}/api/oof/v1/selectnsi
Method : POST
Request to OOF { "requestInfo":{ "transactionId":"234-675-4328", "requestId":"123-456-7890", "sourceId":"SO", "timeout":600 }, "NSTInfo":{ "invariantUUID":"23edd22b-a0b2-449f-be87-d094159b9269", "UUID":"46da8cf8-0878-48ac-bea3-f2200959411a" }, "serviceProfile":{ "latency":100, "areaTrafficCapDL":"100", "areaTrafficCapUL":100, "maxNumberofUEs":300, "areas":" area1|area2", "expDataRateDL":10, "expDataRateUL":30, "uEMobilityLevel":"stationary", "resourceSharingLevel":"shared" } }
Response: { "transactionId":"234-675-4328", "requestId":"123-456-7890", "requestStatus":"accepted", "statusMessage":"", "NSIInfo":{ "invariantUUID":"23edd22b-a0b2-449f-be87-d094159b9269", "UUID":"46da8cf8-0878-48ac-bea3-f2200959411a", "NSIID":"61c4aa7c-9ca6-46cd-b3f8-009769db8641", "NSIName":"eMBB service" } }

## Slide 19: Request Response Structure : selectnssi
URL: {{oofurl}}/api/oof/v1/selectnssi
Method : POST
Request to OOF { "requestInfo":{ "transactionId":"234-675-4328", "requestId":"123-456-7890", "sourceId":"SO", "timeout":600 }, "NSSTInfo":{ "invariantUUID":"23edd22b-a0b2-449f-be87-d094159b9269", "UUID":"46da8cf8-0878-48ac-bea3-f2200959411a" }, "sliceProfile":{ "latency":20, "areaTrafficCapDL":300, "areaTrafficCapUL":300, "maxNumberofUEs":300 } }
Response: { "transactionId":"234-675-4328", "requestId":"123-456-7890", "requestStatus":"accepted", "statusMessage":"", "NSSIInfo":{ "invariantUUID":"23edd22b-a0b2-449f-be87-d094159b9269", "UUID":"46da8cf8-0878-48ac-bea3-f2200959411a", "NSSIID":"61c4aa7c-9ca6-46cd-b3f8-009769db8641", "NSSIName":"eMBB cn service" } }

## Slide 20: REST to Service Instance from AAI
Method: GET
URL: {{aaiurl}}/aai/v13/service-design-and-creation/models/model/{model-invariant-id}/model-vers/model-ver/{model-version-id}
Response: { "model-version-id":"54836196-c411-4690-af98-900c1c3aadd7", "model-name":"nst model", "model-version":"1.0", "resource-version":"1573183038378" }
Method: GET
URL: {{aaiurl}}/aai/v14/business/customers/customer/5GCustomer/service-subscriptions/service-subscription/5G/service-instances/service-instance/{service-instance-id}
Response: { "service-instance-id":"32cd906f-ee7a-4ecf-b1c3-2fce4d59f8c1", "service-instance-name":"eMBB_Slice_E2ESlice", "service-type":"eMBB", "service-role":"e2eslice-service", "environment-context":"01-010101", "description":"", "model-invariant-id":"21886a96-0664-47a3-beae-766952f2059f", "model-version-id":"54836196-c411-4690-af98-900c1c3aadd7", "service-instance-location-id":"300-01|300-02", "resource-version":"1574128556655", "orchestration-status":"activated", "relationship-list":{ "relationship":[ { "related-to":"service-instance", "relationship-label":"org.onap.relationships.inventory.ComposedOf", "related-link":"/aai/v14/business/customers/customer/5GCustomer/service-subscriptions/service-subscription/5G/service-instances/service-instance/32cd906f-ee7a-4ecf-b1c3-2fce4d59f8c0", "relationship-data":[ ] } ] } }

## Slide 21: Model Information of AAI
NSI and NSSI are realized using the service instance model in AAI. Slice profile is a new model added for slice requirement.
NSI:
URL: {{aaiurl}}/aai/v14/business/customers/customer/5GCustomer/service-subscriptions/service-subscription/5G/service-instances?service-role=nsi
Sample response:
{ "service-instances": { "service-instance-id":"32cd906f-ee7a-4ecf-b1c3-2fce4d59f8c0", "service-instance-name":"eMBB_Slice_E2ESlice", "service-type":"embb", "service-role":"nsi", "environment-context":"01-010101", "model-invariant-id":"21886a96-0664-47a3-beae-766952f2059f", "model-version-id":"54836196-c411-4690-af98-900c1c3aadd7", "service-instance-location-id":"300-01|300-02", "orchestration-status":"activated", "resource-version":"1573184593376"
} }
Mapping of nsi service terminology and AAI service attributes:
NSI | service-instance
id | service-instance-id
name | service-instance-name
sST | service-type service-role=“e2eslice-service”
status | orchestration-status
PLMNIdList | service-instance-location-id
snssai | environment-context

## Slide 22: Model Information of AAI
NSSI:
URL: {{aaiurl}}/aai/v14/business/customers/customer/5GCustomer/service-subscriptions/service-subscription/5G/service-instances?service-role=nssi
Sample response:
{ "service-instances": { "service-instance-id":"32cd906f-ee7a-4ecf-b1c3-2fce4d59f8c0", "service-instance-name":"eMBB_Slice_E2ESlice", "service-type":"embb", "service-role":"nssi", "environment-context":"cn", "model-invariant-id":"21886a96-0664-47a3-beae-766952f2059f", "model-version-id":"54836196-c411-4690-af98-900c1c3aadd7", "service-instance-location-id":"300-01|300-02", "orchestration-status":"activated", "resource-version":"1573184593376" } }
Mapping of nssi service terminology and AAI service attributes:
NSI | service-instance
id | service-instance-id
name | service-instance-name
sST | service-type service-role=“nssi”
status | orchestration-status
PLMNIdList | service-instace-location-id
domainType | Environment-context

## Slide 23: Model Information of AAI
Slice Profile:
URL: {{aaiurl}}/aai/v14/business/customers/customer/5GCustomer/service-subscriptions/service-subscription/5G/service-instances?service-role=nssi
Sample response:
{
"slice-profile":{
"profile-id":"e151059a-d924-4629-845f-264db19e50b4",
"latency":50,
"maxNumberOfUEs":500,
"coverageAreaTAList ":"area1|area2",
"ueMobilityLevel":"stationary",
"resourceSharingLevel":"YES",
"expDataRateUL":10,
"expDataRateDL":30,
"areaTrafficCapUL":100,
"areaTrafficCapDL":100,
"activityFactor":80,
"e2eLatency":10,
"jitter":10,
"survivalTime":30,
"csAvailability":95.5,
"reliability":99.9,
"expDataRate":80,
"payloadSize":50,
" trafficDensity":100,
"connDensity":80,
"serviceAreaDimension":"xxxxx“
}
}

## Slide 24: Questions
.

## Slide 25: Dependencies on OOF
NA