## Slide 2
Presenters: N.K. Shankaranayaranan (AT&T), Swaminathan S (Wipro)
OOF-SON: 5G Self-Organizing Network (SON) using ONAP Optimization Framework (OOF) – Honolulu Requirements Overview
October 14, 2020
Acknowledgements: Feedback and support from participants in ONAP OOF-SON team calls
Collaborators: AT&T, Wipro, IBM, highstreet technologies, Tech Mahindra, Nokia, Reliance Jio, Rutgers Winlab, Ericsson, Verizon

## Slide 3
SON use case: Roadmap
CM-Notify handling
Control Loop Co-ordination (CLC) first steps
Introduced Adaptive SON functionality
Checked in RAN-Sim into ONAP repo
R6 Frankfurt
ML-based SON – first steps (training done offline), additional input from ML-model for PCI optimization (based on PM data)
Preparation work for 3GPP/ORAN yang model
O-RAN alignment (O1 for configuration and CM notification)
C&PS - RAN config data base (first steps), cell models, initial alignment with 3GPP NRM
SON coordination (preparation/initial steps)
CLC interaction (stretch)
O-RAN alignment (FM/PM over O1)
C&PS – Full-fledged RAN data base, full alignment with 3GPP NRM
Control Loop Co-ordination, SON function co-ordination
New SON use cases & interaction with Network Slicing
SON in context of LCM, SON function deployment
R7 Guilin
R8 Honolulu
R9 Istanbul & beyond

## Slide 4
Honolulu Requirement Summary
Category | Requirement | Content | Priority
Interoperability | O-RAN alignment (VES, O1 interface) | Receive Configuration Management (CM) notifications over VES Align with relevant aspects of O-RAN O1 interface (netconf configuration, PM and FM notifications) | HIGH
Functional | RAN Database (C&PS DB), including new RAN models | Data models/DB schema & APIs to be generated from yang models Details of cells to be stored with PNF reference in AAI Modeling of RAN functions and objects (align with NRM) | HIGH
Platform | Control Loop Coordination (CLC) extensions | Collaborate on CLC extensions (queueing, priority, …) (stretch goal) | HIGH
Functional | SON co-ordination | Co-ordination across SON functions – initial steps | MEDIUM
Functional | SON function to evolve ONAP platform | (New) SON use case based on data/KPI analysis Machine Learning (ML) SON aspects in DCAE (extension) Interaction with Network Slicing (stretch goal) CLC interaction (stretch goal) | MEDIUM
Functional | SON in the context of LCM | Role of SO (e.g., new cell discovery/addition) (beyond H-release) | LOW
Platform | SON function deployment | SDC & CLAMP (for SON service/feature deployment) (beyond H-release) | LOW
Interoperability | Real gNB interaction | Interaction with real gNodeB in lab (over O1 interface) | LOW

## Slide 5
Rel 8 OOF-SON dependency on
ONAP C&PS and ORAN
5
OOF-SON use case created ConfigDB in Rel 5/Rel6/Rel7 which was the seed for C&PS
OOF-SON has a strong dependency on, and is an early adopter of, working instance of C&PS
REQ: Identify/support RAN yang model aligned with ORAN/3GPP – can be a very small sub-graph for Rel.8. SON use case with cellid, pci, neighbor cell relation
REQ: Support database API similar to existing Rel.7 ConfigDB API
  For “quick POC” solution, limit impact on existing modules which are using the Rel 7 API for ConfigDB
Dependency | Mitigation
Availability of ORAN yang models. | Use 3GPP TS 28.541 NRM based attribute definitions and yang from https://forge.etsi.org/rep/3GPP/SA5/data-models/tree/master/yang-models.
Availability of CM_Notify VES Spec, and confirmation that VES Collector will be updated to receive this. | Continue to use custom-defined CM_Notify, however, there will be no additional value for Guilin release.
Support of VES message (CM_Notify) processing by C&PS. | SDN-C (R) will process the VES CM_Notify message and update C&PS. Action: Clarify by M1 on C&PS functionality.

## Slide 6
For Rel 5/6/7, OOF-SON used a sub-tree from Broadband Forum RAN model based on 3GPP
  We have been preparing for, and advocating for, a common ORAN/3GPP network model
For Rel 8 of OOF-SON, we need to identify a suitable sub-tree of a standard 5G RAN yang model and include the minimal set below (O-RAN if available, else from 3GPP TS 28.541 Rel. 16):
Basic ids for GNB and cell: gNBDUId, nCI etc
PCI property: nRPCI
Neighbor Relations – for PCI and ANR functions
Note: The initial yang models based on 3GPP TS 28.541 NRM have already been defined for Network Slicing use case. These should be aligned and enhanced suitably for SON use case in Rel.8.
Yang model needed for OOF-SON R8

## Slide 7
Thank You

## Slide 8
ONAP-based SON
8
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SDN-R)
5G/4G Radio Network
OOF-PCI Casablanca
  First ONAP SON PCI use case
  PoC Demo in Dec 2018
OOF-SON Dublin
  Added SON function: ANR
  More SON data flows: FM, PM
  New SON-Handler MS in DCAE
Config status
Data, FM, PM
SON  Control Loop (CL)
ONAP: Open-source platform, with basic open-source code
Companies can use framework to add proprietary SON solutions, including optimization algorithms, etc.

## Slide 9
RIC (non-RT)
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SDN-R)
OOF-SON use case has built a foundation for ONAP/ORAN integration
Radio network uses common netconf/yang model
Data flows:
SDN-R to RAN: netconf-based configuration
RAN to DCAE: VES format for FM alarms, PM KPI, CM Notifn
RAN to SDN-R: Netconf ack
Config ack
Data, FM, PM
A-1/O-1
A-1/O-1
RIC (near RT)
ORAN Radio Network
Config notify
ONAP-based SON & ORAN interfaces

## Slide 10
DMaaP
Config Change
11b
VES Collector
1e
3a
12
ORAN O1 CM
interface
10
C&PS DB
CM Notification
ORAN O1 interface
4e
4a
Simulated RAN
~2000 Cells
Nbrlist, PCI
Cells/GNBs
RIC
Yang model
O1 - Netconf interface
O1 - VES
outputs
Network
Yang
Model
Netconf
Configuration
Database
Schema
API
DB-Update
Read network
configuration
1f
“PCI” value: (ORAN or 3GPP Yang model) NRCellDU/nRPCI
“PCI” value: ONAP Rel 8 implementation NRCellDU/nRPCI
4b
“Data model” used at interfaces:
C&PS DB
RAN
SON-H MS
OOF
7
SDN-R (SDN-C)
1d
11a
Model Mapping
4c
Network yang models & ONAP DB
models/API – Rel 8 (proposed)