## Slide 1
5G Self-Organizing Network (SON) using ONAP Optimization Framework (OOF):Guilin Demo & Roadmap
Collaborators : AT&T, Wipro, IBM, highstreet technologies, Tech Mahindra, Ericsson, Nokia, Reliance Jio, Rutgers Winlab, Verizon
Presenters: N.K. Shankaranayaranan, Swaminathan S, Krishna Moorthy
Demo: Niranjana Y

## Slide 2: Introduction to ONAP-based SON
2
RIC (non-RT)
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SDN-R)
OOF-SON use case has built a foundation for ONAP/O-RAN integration
Radio network uses common netconf/yang model
Data flows
SDN-R to RAN: netconf-based configuration
RAN to DCAE: VES format for FM alarms, PM KPI, CM Notification
RAN to SDN-R: Netconf ack
Config ack
Data, FM, PM
A-1/O-1
A-1/O-1
RIC (near RT)
O-RAN Radio Network
Config notify
SON  Control Loop (CL)
ONAP: Open-source platform, with basic open-source code
Companies can use framework to add proprietary SON solutions, including optimization algorithms, etc.

## Slide 3: Release Roadmap
3
CM-Notify handling
Control Loop Co-ordination (CLC) first steps
Introduced Adaptive SON functionality
Checked in RAN-Sim into ONAP repo
R6 Frankfurt
ML-based SON – first steps (training done offline), additional input from ML-model for PCI optimization (based on PM data)
Preparation work for 3GPP/O-RAN yang model
O-RAN alignment (O1 for configuration and CM notification)
CPS - RAN config data base (first steps), cell models, initial alignment with 3GPP NRM
SON coordination (preparation/initial steps)
CLC interaction (stretch)
O-RAN alignment (FM/PM over O1)
CPS – Full-fledged RAN data base, full alignment with 3GPP NRM
Control Loop Co-ordination, SON function co-ordination
New SON use cases & interaction with Network Slicing
SON in context of LCM, SON function deployment
R7 Guilin
R8 Honolulu
R9 Istanbul & beyond

## Slide 4
Guilin recap

## Slide 5: ONAP SON aligning with O-RAN: Release 7 POC
DCAE
DMaaP
SON Handler MS
OOF
SDN-R (SDN-C)
Policy
2
1b
1c
Config Change
9
1d
1a
8
11b
FM/PM KPIs
VES Collector
FM/PM DB
1e
4f
FM/PM Collector and Database
3d
[3a] 4a
12
O-RAN O1
interface
9
10
12
4a
ConfigDB
1f
CM
n
10
13
13
O-RAN O1 interface
5
7a
4c
4d
4b
4c
4e
4d
Simulated RAN
~2000 Cells
Nbrlist, PCI
Cells/GNBs
RIC
Yang model
O1 - Netconf interface
O1 - VES
outputs
Note: DES MS is a new MS introduced in Release 7.
Network yang model update based on 3GPP/O-RAN (to prepare for Rel. 8)
Config DB (RCDB) Rel 6
REST API
DMaaP Control Loop messages
CM-FM-PM messages from RAN
Config updated to RAN (netconf)
Interface enhancements
6
DES MS
7b
Offline-training
for ML-based SON function
ML-based
m
New interface
11a
Key enhancements done in Guilin release
DCAE

## Slide 6: ML-based SON: Approach
6
ML training should be done outside ONAP – use “offline training”, and then onboard the ML models on to ONAP.
  Future enhancement can include updating the model after it is onboarded to ONAP (interface, mechanism, etc. to be worked out)
SON function applying an ML model can be incorporated in OOF or DCAE. Since it is a SON use case, possible scenarios include:
  ML providing additional ‘inputs’ to the SON optimization algorithm in OOF
  ML techniques can be employed for the optimization, and consider Policy-based decision to pick from multiple ML models
  Detection of need for optimization (e.g., hidden neighbors)
  Multi-step optimization, with one or more steps involving ML
  Etc.
  So, we considered it is more appropriate to have an offline-trained SON model hosted in OOF.
Approach chosen in Guilin

## Slide 7: Remarks
7
ML model will get invoked when OOF is invoked for PCI optimization by SON-Handler.
ML sub-component will invoke DES APIs to fetch last ‘n’ PM samples (HO).
It is assumed that the historical PM samples are stored in the MongoDB by DL Feeder.
In Guilin, the ML model will be very simple (just illustrative).
Beyond Guilin, we will also consider aspects such as the following:
  A way to “update” the model later?
  Should we consider training/re-training also to happen inside ONAP?
  ML used in detection of hidden neighbors, PCI collision, etc.
  ML-based optimization
  Other SON use cases
  …

## Slide 8: OOF Architecture: Guilin
8
Container/POD
Policy
Placement Solver
Policy Models
Container/POD
Mini zinc
Mini Zinc
Generic Solver API
CRUD(mzn)
solve
(model-id, data-json)
InvokeSolver
(model, data, solver_params, timeout)
Container/POD
OSDF lib base
PCI APP
Data transform
placementAPI(json)
Container/POD
APP-X APP
Data Transform
OSDF lib SDK
Provides App users direct access to model repo:
No development needed for model changes that do not change data i/f
Tighter access control to model DB – better security
Triggers for validation when models get inserted into DB
Version control for models
Layered container images:
Allows use of base image from ONAP
  Push common data interfaces/transforms into common base
Build secret sauce as
  Models going into model repo
  API/data enhancements built on top of base image
Container/POD
APP-Y APP
Data transform
OSDF lib base
Container/POD
Placement API
OSDF lib base
CRUD(mzn)
App user
Compile time (API/Data) separated from the runtime (Gen-solver):
Enables common interface to generic & custom solvers
Allows Generic solver to scale independently (vs for each optimization)
Allows user to on-board models during runtime (provided data APIs remain same)
Platform component
App user
Container/POD
CM APP
Data transform
OSDF lib base
Allows interfacing with custom optimizers
App component
App data plugins
Platform Data APIs
data APIs
PCI heuristic Solver
pciAPI(json)
OSDF lib base
ML model (SON)
Model repos
Enhancement in Guilin
data APIs
data APIs
data APIs
data APIs

## Slide 9: ML-based SON: Flows
DCAE
9
OOF
OSDF
Minizinc
SON-Handler MS
VES Collector
DL-Feeder
Mongo DB
DES
SDN-R
Simulated RAN
Policy
Config DB
1
2
PM data over O1
FM data over O1
4
7
11
3
12
13
14
Existing CL flow
New CL flow/action
New flow for use case, but
Implemented in ONAP
PM data flow (collection)
a
b
c
PG
Offline Trained SON ML model
5
8
10
9
a
b
c
Cells/GNBs
RIC
Yang model
O1 - Netconf interface
O1 – VES outputs
6
REST API
DMaaP Control Loop messages
FM-PM messages from RAN
Config updated to RAN (netconf)
DB R/W

## Slide 10: Flow details
10
Step | Description
1 | PCI collision/confusion alarm from RAN to VES collector
2 | PCI collision/confusion alarm posted on DMaaP by VES Collector
3 | SON-Handler triggers OOF for PCI optimization
4 | OOF (OSDF) queries ConfigDB to obtain cells, PCI and neighbor details
5 | OSDF invokes the ML function for any additional inputs to the optimization
6 | ML function queries DES for PM data samples from MongoDB
7 | DES fetches PM data samples from MongoDB
8 | DES provides the PM data samples to ML function
9 | ML function provides updated ‘fixed PCI cell’ list based on the ML model
10 | Optimizer is invoked along with additional inputs from ML model
11 | OOF returns PCI optimization result to SON-Handler MS
12 | SON-Handler MS triggers a Control Loop towards Policy
13 | Policy invokes SDN-R as the actor of the CL to update PCI values
14 | SDN-R sends updated PCI values to the RAN
Blue – New step
Notes
DES can provide last ‘n’ samples of PM data. No additional functional impact in DES or its APIs.
The ML model will be hosted in OOF. In Guilin release, it will be quite simple.
Format of PM data reported by RAN – no changes are foreseen in G-release.
DL-feeder configuration to be considered.
ML model working
Based on HO PM data reported from the RAN, and by looking at the trend (last ‘n’ samples), ML model shall provide a list of cells whose PCI values shall not be changed during PCI optimization (FixedPCI cells). This shall be considered by Minizinc during PCI optimization.

## Slide 11: WINLAB at Rutgers University
WINLAB Tech Center Facility
WINLAB founded in 1989 as a collaborative
industry-university research center with
specialized focus on wireless networking
~25 faculty/staff, most from the ECE and CS departments at Rutgers
~40-50 grad students (80% PhD, 20% MS)
Low Power IoT Device
ORBIT Radio Grid Testbed
CloudLab Rack
SDN
Massive MIMO
SDR
GENI Rack
Center’s research portfolio spans information theory, radio technology, wireless systems, mobile networks and computing
Extensive experimental research infrastructure including ORBIT & GENI testbeds, SDR, SDN, …
Selected as an ONAP integration and testing laboratory for North America

## Slide 12
Guilin demo

## Slide 13: PCI Optimization: Pre-Guilin
DCAE
13
OOF
OSDF
Minizinc
SON-Handler MS
VES Collector
DL-Feeder
Mongo DB
DES
SDN-R
Simulated RAN
Policy
Config DB
1
2
PM data over O1
FM data over O1
4
6
3
7
8
9
PM data flow (collection)
a
PG
5
a
Cells/GNBs
RIC
Yang model
O1 - Netconf interface
O1 – VES outputs
REST API
DMaaP Control Loop messages
FM-PM messages from RAN
Config updated to RAN (netconf)
DB R/W
Step 2
Step 1
Step 3
Step 4
Steps illustrated in demo
Step 5

## Slide 14: Demo Sequence: Pre-Guilin
Show OOF response (PCI optimization result)
Show Policy triggering SDN-R (Actor)
Show SON-Handler MS triggering OOF
Show that the PCI optimization has solved the problem
Trigger PCI alarm (collision/confusion) from RAN-SIM UI
Step 3: Logs
Step 4: Logs
Step 5: UI
Step 2: Logs
Step 1: UI

## Slide 15: Step 1: Modify Neighbors (Chn0005)
Modify neighbors for Chn0005

## Slide 16: Step 1: Modify neighbors for Chn0005
Original neighbors for Chn0005
After addition of 3 neighbors

## Slide 17: Step 2: SON-Handler MS -> OOF trigger
No “fixedPCI cells”

## Slide 18: Step 3: Optimization Result
PCI of Chn0012 is changed

## Slide 19: Step 4: Policy -> SDN-R (Actor)

## Slide 20: Step 5: PCI optimization completed
Before optimization
After optimization

## Slide 21: ML-based PCI Optimization: Guilin Demo
DCAE
21
OOF
OSDF
Minizinc
SON-Handler MS
VES Collector
DL-Feeder
Mongo DB
DES
SDN-R
Simulated RAN
Policy
Config DB
1
2
PM data over O1
FM data over O1
4
7
11
3
12
13
14
Existing CL flow
New CL flow/action
New flow for use case, but
Implemented in ONAP
PM data flow (collection)
a
b
c
PG
Offline Trained SON ML model
5
8
10
9
a
b
c
Cells/GNBs
RIC
Yang model
O1 - Netconf interface
O1 – VES outputs
6
REST API
DMaaP Control Loop messages
FM-PM messages from RAN
Config updated to RAN (netconf)
DB R/W
Step 1
Step 3
Step 2
Step 4
Step 5
Step 6
Step 7
Step 8
Steps illustrated in demo

## Slide 22: Demo Sequence: Guilin
Show OOF response (PCI optimization result)
Show Policy triggering SDN-R (Actor)
Show SON-Handler MS triggering OOF
Show that the PCI optimization has solved the problem
PM data (with high HO for 1 cell) stored in Data Lake
Trigger PM data reporting (with high HO for some cells)
Trigger PCI alarm (collision/confusion) from RAN-SIM UI
OOF<->DES interaction for fetching HO data
Step 5: Logs
Step 6: Logs
Step 8: UI
Step 4: Logs
Step 1: UI
Step 2: Logs
Step 3: UI
Step 7: Logs
Guilin enhancement
While keeping PCI unchanged for a cell with high HO

## Slide 23: Step 1: Generate PM data
This is to initiate PM data generation from RAN-Sim.
In RAN-Sim, we pre-configure that the handovers for Chn0012 is very high.

## Slide 24: Step 2: High Handovers for Chn0012
Handovers for Chn0012 is very high (compared to other cells)

## Slide 25: Step 3: Modify Neighbors (Chn0005)
Modify neighbors for Chn0005

## Slide 26: Step 3: Modify neighbors for Chn0005
Original neighbors for Chn0005
After addition of 3 neighbors

## Slide 27: Step 4: SON-Handler MS -> OOF trigger
No “fixedPCI cells”

## Slide 28: Step 5: OOF<->DES interaction for HO data

## Slide 29: Step 6: Optimization Result
PCI of Chn0012 is not changed (fixed), but PCI of Chn0001 is changed to solve the confusion.

## Slide 30: Step 7: Policy -> SDN-R (Actor)

## Slide 31: Step 8: PCI optimization completed
Before optimization
After optimization

## Slide 32: Recap
Solution without ML-SON
Solution with ML-SON
ML-based SON takes additional inputs (cells whose PCI values should remain unchanged) from ML models during PCI optimization and then performs the optimization

## Slide 33
Honolulu release & future roadmap

## Slide 34: Release Roadmap
34
CM-Notify handling
Control Loop Co-ordination (CLC) first steps
Introduced Adaptive SON functionality
Checked in RAN-Sim into ONAP repo
R6 Frankfurt
ML-based SON – first steps (training done offline), additional input from ML-model for PCI optimization (based on PM data)
Preparation work for 3GPP/O-RAN yang model
O-RAN alignment (O1 for configuration and CM notification)
CPS - RAN config data base (first steps), cell models, initial alignment with 3GPP NRM
SON coordination (preparation/initial steps)
CLC interaction (stretch)
O-RAN alignment (FM/PM over O1)
CPS – Full-fledged RAN data base, full alignment with 3GPP NRM
Control Loop Co-ordination, SON function co-ordination
New SON use cases & interaction with Network Slicing
SON in context of LCM, SON function deployment
R7 Guilin
R8 Honolulu
R9 Istanbul & beyond

## Slide 35: Summary of Requirements
Category | Requirement | Content | Priority
Interoperability | O-RAN alignment (VES, O1 interface) | Receive Configuration Management (CM) notifications over VES Align with relevant aspects of O-RAN O1 interface (netconf configuration, PM and FM notifications) | HIGH
Functional | RAN Database (CPS DB), including new RAN models (stretch goal) | Data models/DB schema & APIs to be generated from yang models Details of cells to be stored with PNF reference in AAI Modeling of RAN functions and objects (align with NRM) | HIGH
Platform | Control Loop Coordination (CLC) extensions | Collaborate on CLC extensions (queueing, priority, …) (stretch goal) | HIGH
Functional | SON co-ordination | Co-ordination across SON functions – initial steps | MEDIUM
Functional | SON function to evolve ONAP platform | (New) SON use case based on data/KPI analysis Machine Learning (ML) SON aspects in DCAE (enhancements) Interaction with Network Slicing (stretch goal) CLC interaction (stretch goal) | MEDIUM
Functional | SON in the context of LCM | Role of SO (e.g., new cell discovery/addition) (beyond H-release) | LOW
Platform | SON function deployment | SDC & CLAMP (for SON service/feature deployment) (beyond H-release) | LOW
Interoperability | Real gNB interaction | Interaction with real gNodeB in lab (over O1 interface) | LOW
Blue Topics for which there is commitment in R8, other topics will be taken up based on resource availability, timelines & PTL agreement.

## Slide 36: ONAP SON aligning with O-RAN: Release 7 POC
36
DMaaP
DCAE
SON Handler MS
OOF
SDN-R (SDN-C)
Policy
2
1b
1c
Config Change
9
1d
1a
8
11b
FM/PM KPIs
VES Collector
FM/PM DB
1e
4f
FM/PM Collector and Database
CL setup
3d
[3a] 4a
12
O-RAN O1
interface
9
10
12
4a
ConfigDB
1f
CM
n
10
13
13
O-RAN O1 interface
5
7a
4c
4d
4b
4c
4e
4d
Simulated RAN
~2000 Cells
Nbrlist, PCI
Cells/GNBs
RIC
Yang model
O1 - Netconf interface
O1 - VES
outputs
Note: DES MS is a new MS introduced in Release 7.
Network yang model update based on 3GPP/O-RAN (to prepare for Rel. 8)
CM notification msg – Rel 6 “pre-standard” msg ,Config DB (RCDB) Rel 6
REST API
DMaaP Control Loop messages
CM-FM-PM messages from RAN
Config updated to RAN (netconf)
Interface enhancements
6
DES MS
7b
Offline-training
for ML-based SON function
ML-based
m
New interface
11a

## Slide 37: ONAP SON aligning with O-RAN: Release 8 target
CL setup
Policy
DMaaP
37
DCAE
SON Handler MS
OOF
SDN-R (SDN-C)
2
1b
1c
Config Change
9
1d
1a
8
11b
FM/PM KPIs
VES Collector
FM/PM DB
1e
4f
FM/PM Collector & DB
3d
3a
12
O-RAN O1
interface
9
10
12
4a
1f
CM
6
10
13
13
O-RAN O1 interface
5
7
4d
4b
4c
4e
4d
4a
Simulated RAN
~2000 Cells
Nbrlist, PCI
Cells/GNBs
RIC
Yang model
O1 - Netconf interface
O1 - VES
outputs
CM via VES collector
CPS DB model based on O-RAN network yang model
Offline-training
for ML-based SON function
ML-based
CM-FM-PM messages from RAN
Config updated to RAN (netconf)
REST API
DMaaP Control Loop messages
n
Interface enhancement
DES MS
7b
11a
5G use case for CPS, intention is to have an API mapper that maps existing APIs to appropriate Xpath queries
Functional enhancement
4c
TDMT
TDMT = Template-based Data Model Transformer
CPS

## Slide 38: Rel 8 OOF-SON dependency on ONAP CPS and O-RAN
OOF-SON use case created ConfigDB in Rel 5/Rel6/Rel7 which was the seed for CPS
OOF-SON has a strong dependency on, and is an early adopter of, working instance of CPS
REQ: Identify/support RAN yang model aligned with O-RAN/3GPP – can be a very small sub-graph for Rel.8. SON use case with cellid, pci, neighbor cell relation – (mostly DONE)
REQ: Support database API similar to existing Rel.7 ConfigDB API
  Use a mapper service (TDMT) which maps the existing APIs to Xpath queries to CPS
Dependency | Mitigation
Availability of O-RAN yang models. | Use 3GPP TS 28.541 NRM based attribute definitions and yang from https://forge.etsi.org/rep/3GPP/SA5/data-models/tree/master/yang-models.
Availability of CM_Notify VES Spec, and confirmation that VES Collector will be updated to receive this. | Continue to use custom-defined CM_Notify, however, there will be no additional value for Honolulu release.
CPS readiness | Continue to use ConfigDB APIs if CPS is not ready Use Xpath queries of CPS if the mapper service is not ready
Our understanding is this will be available for H-release.

## Slide 39: Yang model for R8
39
For Rel 5/6/7, OOF-SON used a sub-tree from Broadband Forum RAN model based on 3GPP
For Rel 8 of OOF-SON, we have identified a yang model based on the ORAN/3GPP (TS 28.541 Rel. 16) model for SON and Network Slicing
Basic ids for GNB and cell: gNBDUId, nCI etc
PCI property: nRPCI
Neighbor Relations – for PCI and ANR functions
SON use case has prior work (MS, OOF, SDNR, RAN-Sim) using Rel 6 APIs and model. Non-trivial effort to map the existing API/model to the CPS-DB based on New Yang model
Consensus is to rely on model/api mapping (TDMT)
RAN-Sim will also need to be modified to support new Yang model
Yang model update has impacts in SDN-R and RAN-Sim, and this work may take I-release to be completed.

## Slide 40: FM (alarms) support in ONAP-SON
40
RAN-SIM sends single FM alarm message, e.g., PCI-Conflict (step 3d)
DCAE Collector places FM message on DMaaP (step 4d)
SON-Handler MS processes FM message and stores in FM/PM DB – (step 4f)
Goal: Release 8/9: ONAP-SON should align with ORAN model for FM
What is appropriate scope in ONAP to handle alarms?
  What are the FM message formats / types as per ORAN
  What are the assumptions for single v. repeated alarms
  How does the SON loop determine that an alarm has been addressed?

## Slide 41: YANG Model Tree Used for Rel. 5/6/7 OOF PCI/ANR POC1
The platform ready to support any YANG Model
1 https://gerrit.onap.org/r/gitweb?p=ccsdk/features.git;a=tree;f=sdnr/northbound/oofpcipoc/model/src/main/yang;h=5b3ef2c03cf516ba716f69076a780a95e96fadc2;hb=refs/heads/dublin
RPC
RPC
Number & List of Cells
PCI and PNF-NAME for a Cell
List of Neighbors
Netconf Notification

## Slide 42: Network Resource Models (NRM): 3GPP 28.541 Rel 15
Figure 4.2.1.1-1: NRM for all deployment scenarios
Figure 4.2.1.1-3: NRM for <<IOC>>NRSectorCarrier and <<IOC>>BWP for all deployment scenarios
Figure 4.2.1.1-4: Cell Relation view for all deployment scenarios

## Slide 43: Network yang models & ONAP DB models/API – Rel 6 & 7
DMaaP
Config Change
11
VES Collector
1e
3a
12
ORAN O1 CM
interface
10
CM Notification
ORAN O1 interface
4e
4a
Simulated RAN
~2000 Cells
Nbrlist, PCI
Cells/GNBs
RIC
Yang model
O1 - Netconf interface
O1 - VES
outputs
Network
Yang
Model
Netconf
Configuration
Database
Schema
API
DB-Update
Read network
configuration
“PCI” value: BBF Yang model lte-ran-rf-g/ phy-cell-id
“PCI” value: ONAP Rel 4 implementation Cell.pciValue
4b
“Data model” used at interfaces:
ConfigDB
RAN
SON-H MS
OOF
7
4a
SDN-R (SDN-C)
Config DB
1f
1d
Model Mapping
4c

## Slide 44: Network yang model & CPS DB models/API – Rel 8/9
DMaaP
44
Config Change
11b
VES Collector
1e
3a
12
ORAN O1 CM
interface
10
TDMT
CPS-DB
CM Notification
ORAN O1 interface
4e
4a
Simulated RAN
~2000 Cells
Nbrlist, PCI
Cells/GNBs
RIC
Yang model
O1 - Netconf interface
O1 - VES
outputs
Network
Yang
Model
Netconf
Configuration
Database
Schema
Xpath API
DB-Update
1f
“PCI” value: (ORAN or 3GPP Yang model) NRCellDU/nRPCI
“PCI” value: ONAP Rel 8 implementation NRCellDU/nRPCI
4b
“Data model” used at interfaces:
CPS DB
RAN
SON-H MS
OOF
7
SDN-R (SDN-C)
1d
11a
4c
Maps DB API calls to suitable yang-based Xpath queries

## Slide 45: CPS overview
DCAE VES collector
Data/API normalization (if needed) happens in the Application space
xNF proxy is the owner and single point of entry for native xNF data
xNF proxy interacts with mediation/controllers and keeps the CPS data up-to-date
DB
CPS
<core>
xNF Proxy
SON normalizer
xNF
SDN Controller
1
2
3
SON-Handler MS
Data model/API normalization
OOF
Template-based Data Model Transformer

## Slide 46: SON co-ordination: Stretch Goal
46
CLC in Policy is currently designed to co-ordinate actions AFTER individual micro-services (components) have decided to take an action and trigger Policy.
SON co-ordination involves the impact of one SON function on another before or during the determination of action (e.g., optimization)
  For example, when a cell outage is being compensated, coverage and capacity optimization should be deferred or should take cell outage into consideration.
  SON co-ordination could be viewed as a platform enhancement => Policy and/or SO shall do the co-ordination.
Note: We will start with initial steps w.r.to SON co-ordination, actual implementation may happen beyond R8.

## Slide 47: Control Loop Co-ordination: Stretch Goal
47
Interaction between Target lock and CLC
Definition of target – PNF, VNF, cell, service, NSI, etc.
Queueing/de-queuing of CL messages by CLC logic
Separate DMaaP topic for each CL response (e.g., DCAE-CL-RSP)
We are working with Policy Team to address these enhancements. All consequent updates in SON-Handler MS and SDN-C will be handled by our SON use case team.