## Slide 1: E2E Network Slicing use case: Guilin status and outlook for Honolulu
Participants: CMCC, Wipro, Huawei, AT&T, IBM, LTTS, DT, TIM, QCT, Amdocs, Tech Mahindra, Reliance Jio, Tencent, China Telecom
Authors: Lin Meng (CMCC), Swaminathan S (Wipro), Henry Yu (Huawei), Shankar P N (AT&T), Lu Kai (CMCC), Yaoguang Wang (Huawei), Milind Jalwadi (Tech Mahindra)
November 12, 2020
Reporters: Lin Meng (CMCC), Swaminathan S (Wipro)

## Slide 2: Overall concept

## Slide 3: 3GPP Slice Management Functions (3GPP-defined)
Management Function | Key tasks
Communication Service Management Function (CSMF) | Responsible for translating the communication service related requirement to network slice related requirements. Communicate with Network Slice Management Function (NSMF).
Network Slice Management Function (NSMF) | Responsible for management and orchestration of NSI. Derive network slice subnet related requirements from network slice related requirements. Communicate with the Network Slice Subnet Management Function (NSSMF) and Communication Service Management Function.
Network Slice Sub-net Management Function (NSSMF) | Responsible for management and orchestration of NSSI. Communicate with the NSMF.

## Slide 4: ONAP-based Slice Management Overall Architecture Choices
NSMF (ONAP)
CSMF (ONAP)
Standard APIs
NSSMF(s)1
(ONAP)
xNFs
NSMF (ONAP)
CSMF
NSSMF(s)1
(ONAP)
xNFs
NSMF (ONAP)
CSMF
NSSMF(s)1
xNFs
NSMF (ONAP)
CSMF (ONAP)
NSSMF(s)1
xNFs
NSMF
CSMF
NSSMF(s)1
(ONAP)
xNFs
3rd party component
2
3
4
5
Standard APIs
Standard APIs
Standard APIs
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
Standard APIs
Standard APIs
Standard APIs
1 Top-most NSSMF/domain-specific NSSMF – under discussion
1

## Slide 5: Status & Roadmap
NSMF (ONAP)
CSMF (ONAP)
Standard APIs
NSSMF(s)
(ONAP)
xNFs
NSMF (ONAP)
CSMF
NSSMF(s)
(ONAP)
xNFs
NSMF (ONAP)
CSMF
NSSMF(s)
xNFs
NSMF (ONAP)
CSMF (ONAP)
TMF APIs
NSSMF(s)
xNFs
NSMF
CSMF
NSSMF(s)
(ONAP)
xNFs
3rd party component
1
2
3
4
5
3GPP APIs
3GPP APIs
Standard APIs
Standard APIs
Internal call
Internal call
Internal call
Internal call
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
Standard APIs
In H-release, we will mainly continue with enhancements for Scenario 1, and address a few gaps in Scenario 4.
Achieved so far for Core & RAN subnets
Started in Guilin for all 3 subnets

## Slide 6: Use Case Objective - NSI Life Cycle view
Ref.: 3GPP TS 28.530 (Rel 16)
Design and pre-provision: Creation of necessary slice/slice sub-net templates.
Instantiation/Configuration & Activation/Deactivation of NSIs (including instantiation/mapping of its constituent slice sub-nets)
Objective: Demonstrate the modeling, orchestration and assurance of an E2E network slice , including RAN, TRANS, CORE slice subnet, aligned with relevant standards (3GPP, IETF, TMF, O-RAN, etc.)

## Slide 7: Use Case Objective - NSI Life Cycle view
Ref.: 3GPP TS 28.530 (Rel 16)
Design and pre-provision: Creation of necessary slice/slice sub-net templates.
Instantiation/Configuration & Activation/Deactivation of NSIs (including instantiation/mapping of its constituent slice sub-nets)
Objective: Demonstrate the modeling, orchestration and assurance of an E2E network slice , including RAN, TRANS, CORE slice subnet, aligned with relevant standards (3GPP, IETF, TMF, O-RAN, etc.)
Enhancements in Guilin
Focus area for Honolulu for new functionality

## Slide 8: Guilin release recap & Honolulu proposal

## Slide 9: Guilin requirement summary
Topic | What is done in Guilin
Implement RAN NSSMF, TN NSSMF CN NSSMF within ONAP | Basic logic of all 3 NSSMFs to support NSSI allocation, activation, deactivation, deletion, modification
Enhancements in NSMF | Service Profile decomposition; NSI selection enhancements; e2e slice creation
Enable NSMF interaction with RAN NSSMF, TN NSSMF, CN NSSMF | Generic NSSMF Adaptor for three domain NSSMFs; Alignment with standard interfaces: 3GPP, IETF; connection to external RAN NSSMF
Design of RAN NSST, TN NSST, CN NSST, and Slice Profiles, TN info models | Basic E2E Slicing model was provided, all the related templates designed from SDC, TN related info models
RAN and CN NFs set up and initial configurations | CN NF Simulators were developed: AMF, SMF, UPF; Configuration of S-NSSAI RAN NF Simulator was enhanced for PM data reporting, CU and Near-RT RIC configuration
KPI Monitoring function | KPI computation logic in PM Mapper is partially done DES MS to extract data from DL is implemented
Closed loop and intelligent slicing | Closed loops in RAN domain by reconfiguring the RAN config parameters per slice (Near RT RIC level and cell level) based on PM data analysis Offline trained ML model onboarded as an MS in DCAE for demo

## Slide 10: Components impacted in Guilin: Status
CSMF Portal
NSMF Portal
SDC
U-UI
NST
CSMF
NSMF
Slice Profile determination
NST Selection
NSI Selection
CSMF Policy
NSMF Policy
SO
OOF
Policy
Service instance
Service Profile
NSI
NST
NSSI
NSST
Slice Profile
A&AI
ONAP
EXT-API
CN NSSMF (3rd party)
NSSI Selection
NSST
CST
NSSMF (RAN, Transport, Core)
KPI Computation in PM Mapper
Analysis MS
AI/ML MS
RAN-specific config
Transport specific config
SDN-C
Cell Configurations
RAN slice related configurations
Config
DB
NSSMF Policy
KPI Policies
CL Policies
DCAE
Core NFs configuration
CDS
RAN NSSMF (3rd party)
Res. determination
RAN-Simulator
Core NFs simulator
Data Lake DES
Service LCM APIs
KPI Monitoring APIs
Done
Partially done
Not implemented

## Slide 11: Guilin recap: Frankfurt improvements
Complete UUI Integration with ExtAPI for Network Slice instantiation
Extend NB interface based on TMF 641 to cover service (de)activation, termination.
Implement NSI termination (and also cover NSSI termination trigger)
Implement improvements in OOF and SO  OOF interactions, for example:
  Implement call back API in SO for NST and NSI/NSSI selection
  NSI/NSSI selection improvements
  Slice Profiles generation

## Slide 12: Guilin recap: E2E Slicing solution involving Core, RAN & Transport
NSMF functionality to invoke RAN/Core/Transport NSSMFs for respective NSSI allocation, activation, modification, deactivation and termination
NSSMF adaptor to enable abstraction of interface between NSMF and internal/external NSSMFs (RAN & Core)
  Modeling enhancements – Service Profile, Slice Profiles, NSST/NST updates, endpoints, support of both options for RAN & Transport Slicing, etc.
  Service termination resulting in NSI/NSSI termination also
  Support of new/enhanced APIs for NSSI allocation, modification, deallocation, etc.
  Support for providing sub-net capabilities for Slice Profiles generation

## Slide 13: Honolulu proposal for E2E Slicing solution involving Core, RAN & Transport
REQ-1a: Enhancements in the E2E Slice allocation & stitching together all subnets
Enhancements in CSMF and NSMF (Guilin non-critical bugs and carryover items)
UUI (NSMF portal) showing end-point info also for manual intervention, RAN and Core endpoints to be provided to TN NSSMF
3GPP API alignment and model enhancements related impacts
NSMF and NSSMF interactions for capacity and resource levels
UUI (NSSMF portal) for manual intervention (stretch goal) (will have major impacts in SO, UUI)
REQ-1b: Slice selection taking into account capacity, resource occupancy levels, etc.
Capacity definition for various sub-nets
NSI selection and NSSI selection based on capacity, resource occupancy levels
NSMF to support monitoring and update of resource levels at NSI level
NSSMF to support monitoring and update of resource levels at NSSI level (dynamic capabilities is a stretch goal)
Coverage area to TA list mapping (and considering it for RAN NSSI selection)
REQ-1c: TMF 641 API support for slice LCM operations (stretch goal)
TMF 641 APIs to be supported by UUI towards ExtAPI for service creation, (de)activation, termination

## Slide 14: RAN & Transport Slicing overview
Core Slice Subnet
Cross Domain Links, Domain NSSMF do not know both ends. It is managed by NSMF.
RU
DU
CU
Core
Front Haul
Mid Haul
Back Haul
TN
TN
TN
NSMF
RAN NSSMF
TN NSSMF
Transport Slice Subnet 1
Transport Slice Subnet 2
Transport Slice Subnet 3
ONAP
Transport Network Configurations
Align with IETF TSCi
Align with 3GPP/O-RAN
Core NSSMF
Align with 3GPP (Note)
Note: Enables interface with external NSSMF.
Options for NSSMFs in Guilin |  | Involved Companies
RAN Slice Subnet | RAN NSSMF within ONAP | CMCC, Wipro, AT&T, Amdocs, QCT, Verizon, Reliance Jio, Tencent, China Telecom
 | 3rd Party RAN NSSMF | Huawei, CMCC, Wipro
Transport Slice Subnet | TN NSSMF within ONAP | Huawei, CMCC, Fujitsu, Wipro
3rd Party
RAN NSSMF
Configure RU, DU, CU
RAN Slice Subnet
CSMF

## Slide 15: RAN & Transport Slicing: Scenario 1
CSMF
NSMF
RAN NSSMF
Transport NSSMF
Core NSSMF
Fronthaul subnet
Mid haul subnet
Backhaul subnet
RAN NFs Subnet
Core subnet
1a
3
1
2
1b-i
1b-ii
1b-iii
3a
2a
TS_1 is backhaul transport slice; TS_3, fronthaul; TS_4, midhaul.
TN MD (T-NSSMF) receives TS_1 from NSMF (step 3), and TS_3 and TS_4 from RAN NSSMF (step 1b-i).
TN MD then configures backhaul (3a), fronthaul (1b-ii), and midhaul (1b-iii), respectively.
TS_1
TS_3
TS_4
RAN NSSMF shall be responsible for determination of Slice Profile of FH, MH and RAN NFs.
RAN NSSMF shall be responsible for entire RAN subnet comprising FH and MH (stitching together, CL actions, etc.)
Preferred option by O-RAN
& ONAP internal RAN NSSMF

## Slide 16: RAN & Transport Slicing: Scenario 2
CSMF
NSMF
RAN NSSMF
Transport NSSMF
Core NSSMF
Fronthaul subnet
Mid haul subnet
Backhaul subnet
RAN NFs Subnet
Core subnet
1a
3
1
2
3a-ii
3a-iii
3a-i
2a
TS_1 is backhaul transport slice; TS_3, fronthaul; TS_4, midhaul.
TN MD (T-NSSMF) receives TS_1, TS_3 and TS_4 from NSMF (step 3).
TN MD then configures backhaul (3a-i), fronthaul (3a-ii), and midhaul (3a-iii), respectively.
TS_1
TS_3
TS_4
NSMF shall be responsible for determination of Slice Profile of FH, MH and RAN NFs.
NSMF shall be responsible for stitching together e2e slice including FH and MH.
Preferred option for external
RAN-NSSMF, E2E Slicing

## Slide 17: Guilin recap: RAN Slicing
Select RAN NSSI, determine RAN slice sub-net resources and then configure the RAN slice sub-net including allocation of ‘resources’ for a slice sub-net instance and configuration of RAN for a slice sub-net instance (including cell configuration)
Interaction with TN NSSMF for FH and BH NSSI allocation, modification, (de)activation & termination.
Determination of RAN NF, FH and MH Slice profiles; whether RAN NSSI and its constituents should be terminated upon NSI termination
Consume necessary PM/FM info from RAN, for simple Closed Loop Actions/Intelligent Slicing
Re-configure/re-allocate RAN resources
Assumptions
All RAN xNFs are created and pre-configured
Config DB is assumed to contain cell details including PNF mapping, etc.
Southbound interface from SDN-C (R) will be netconf for CM, and VES for FM/PM. For FM/PM we are aligned with O-RAN/3GPP.
ONAP
RAN
CUs
DUs
O1 for config update
Note: The config updates should actually have been sent over A1, however this will be taken up in Honolulu.
RAN slice inventory
List of cells, DUs, CUs with details of active slices
Capacity & Capability of RAN subnet
RUs
Near RT-RIC
O1

## Slide 18: Honolulu proposal for RAN Slicing
REQ-2a: P2 Instantiate RAN NFs, RAN “service” and perform initial configuration (O2 is a stretch goal) as part of slice allocation actions
REQ-2b: P2 Support end-point related enhancements for E2E Slicing and RAN<->TN interactions
REQ-2c: P1 Map RAN Slice Profile to each Near-RT RIC-level configuration
REQ-2d: P1 Support A1 interface for Closed Loop and AI/ML based config update guidance
REQ-2e: P2 Consume necessary PM/FM info from RAN, for Closed Loop Actions/Intelligent Slicing
REQ-2f: P2 Appropriately configure/re-configure RAN resources (dependency on O-RAN models)
REQ-2g: P3 Appropriate RAN resource determination is a stretch goal
ONAP
RAN
CUs
DUs
A1
Notes
O2 interface is considered as a stretch goal for RAN Slicing
Alignment with O-RAN information models to be considered in scope.
Only a part of the CPS impacts may be considered in this release.
TA <-> Cell mapping inventory to reside in C&PS/Config DB
RAN slice inventory
List of cells, DUs, Cus, Near-RT RIC with details of active slices
Capacity & capability of RAN subnet
RUs
Near RT-RIC
O1
O2 (Stretch goal)

## Slide 19: Guilin recap: Core Slicing (new Core NSSI creation)
Slice Lifecycle Flows (Existing)
NSSMF – NFVO Flow (New)
UUI
ExtAPI
Core NSSMF Workflow
NSMF
CSMF
SO
CDS
Multi-cloud
serviceOrder API
with slicing
parameters
Call E2ESericeInstance
API with serviceType=CST
1
E2E Workflow
8
OOF
AAI
Macro Workflow
Call service Instance API
2
3
4
5
6
9
K8s Plug-in
K8s Cluster
7
10
11
NSSMF->NFVO Interaction
NFVO Orchestration Flow
Solution based on ONAP Frankfurt release features

## Slide 20: Core Slicing: Reuse existing Core NSSI
Slice Lifecycle Flows (Existing)
NSSMF – NFVO Flow (New)
UUI
ExtAPI
Core NSSMF Workflow
NSMF
CSMF
SO
CDS
Multi-cloud
serviceOrder API
with slicing
parameters
Call E2ESericeInstance
API with serviceType=CST
1
E2E workflow
7
OOF
AAI
Macro workflow
2
3
4
5
6
8
K8s Plug-in
K8s Cluster
9
10
NSSMF->NFVO Interaction
NF Configuration Flow
(Day 1/n configuration)
The Slicing requirements would require in some cases to re-use the existing NSSI. In such cases the NFVO would need to configure specific NFs.
Solution based on ONAP Frankfurt release features

## Slide 21: Guilin recap: Core Slicing: Core NS design & configuration
SDC Service
  VF Level property: S-NSSAI
  Instantiation Type: Macro
  Controller Actor: CDS
SO Workflows
  ControllerExecutionBB
CDS Workflows
  resource-assignment
  config-deploy
  config-deploy-day-2
Configurations
  Day 0: S-NSSAI assigned during the NS instantiation
  Day 1: The configuration templates created in k8s plug-in as preparations for day 2 config
  Day 2: The S-NSSAI updated list is configured in CNFs
Detailed steps documented at - https://wiki.onap.org/display/DW/5GC+Instantiation+and+Modify+Config+flow+through+CDS

## Slide 22: Honolulu proposal for Core Slicing
REQ-3a: Enhance the configuration of the Core NFs beyond basic aspects such as S-NSSAI.
Exact details and NFs are still under discussion.
REQ-3b: Determine placement of Core NFs during Core NSSI instantiation (stretch goal)
Details are being discussed, including the role of Core NSSMF.

## Slide 23: Guilin recap: Transport Slicing
23
NSMF
TN NSSMF
ONAP
CSMF
Optical Domain Controller
SO
TN NSSMF Work Flow
NSMF Work Flow
Internal APIs (TSCi)
AAI
TS definition model (based on TSCi info model)
SDNC
ACTN MPI Adaptor (SBI)
Optical domain controller
ONAP
OOF
Policy
TS implementation models (e.g., te-topology, te-tunnel, etc.)
UUI
TN NSSMF Adaptor
Generic-resource-API
TSC NBI-to-SBI Mapping
SDC
TS: Transport Slice
TSC: Transport Slice Controller
TSCi: Transport Slice Connectivity Interface
NBI: Northbound interfaces
SBI: Southbound interfaces
ACTN: Abstract & Control of TE Network
MDSC: Multi-Domain Service Coordinator
PNC: Physical Network Controller
ACTN MPI: ACTN MDSC to PNC Interface
New ONAP code for TN NSSMF Functionality
AAI: Active and Available Inventory
OOF: ONAP Optimization Framework
SO: Service Orchestrator
SDNC: SDN Controller
SDC: Service Design and Creation
UUI: Usecase User Interface
EXT-API: External API
Existing ONAP code with modifications

## Slide 24: Guilin Transport Slicing: Status
Defined Transport Slice definition model as TN NSSMF NBI
  Model-driven, technology agnostic, intent-like interface
  Aligned with ETSI ZSM Framework
  Based on IETF draft (draft-rokui-5g-transport-slice-00)
Supported the following TN NSSI operations
  Allocate
  Deallocate
  Activate
  Deactivate
  Modify
Supported the following connection types between endpoints:
  P2P
  MP2MP

## Slide 25: Honolulu proposal for Transport Slicing
REQ-4a: Continue collaboration with SDOs (e.g., 3GPP, IETF, ZSM)
  Align service profile and slice profile model with latest 3GPP NRM
  Update IETF TSCi draft and enhance its model based on the inputs from ONAP community
  Align the design with ETSI ZSM
REQ-4b: Support resource occupancy levels of TN NSSIs
  Used by NSMF to determine if an existing NSI can be reused, and by NSSMF if an existing TN NSSI can be reused. (Or similarly, for denying requests to reuse existing TN NSSIs)
  TN NSSI model enhancement
REQ-4c: Support reuse and modification of existing TN NSSIs
  Selection of an existing TN NSSI for reuse/sharing (TN NSSMF provides model/interface for OOF)
  Modify TN NSSI SLA
  Modify endpoints (add or delete endpoints from TN NSSI), and endpoint connections
REQ-4d: Support MP2MP connections between endpoints (stretch goal, we may do only a part of this)

## Slide 26: Roadmap: Transport Slicing with Closed Loop Automation
Optical network
Optical network
ONAP
On-line Plan
Auto Deploy
Topo & Service
Performance & Alarm
Maintain & Optimize
Intelligent
Analysis
Self-service provisioning
Network design & deploy
Network Assurance
2
1
3
4
PNC
Service provisioning and activation:
  Days  Minutes
Network planning and deployment:
  Weeks  Days
Network troubleshooting and restoration:
  Hours  Minutes
Traffic prediction based auto network planning:
  Months  weeks
Four Types of Closed-loop Automation
2018：L2 service
2019：L1 service
2020：Transport Slicing
2021：New CPE online and deployment (and auto service activation)
2022+：Network performance prediction based service disruption prevention
CPE
CPE

## Slide 27: Guilin recap: Slice KPI monitoring
Design Time
Run Time
NSMF Portal
(Management Portal)
DCAE
Policy
Config Policy
SDC
UUI/Portal
CSMF Portal
(Tenant Portal)
NST Model
(Including KPI Monitoring )
NSST Model
NSST Model
Onboard
5G PM Data Collector
(VES / REST )
Tenant
Service Provider
Mongo DB (historic & current KPI)
PM Mapper
2.1
2.2
2.3
3.1
3.2
3.1
3.2
1 SDC distributes KPI template to Compute MS in DCAE
2.1 NSSMF reports PM data to ONAP via collector
2.2 KPI Compute MS analyses template and processes data
2.3 Data is stored in DCAE DB
3.1 Tenant /Operator monitors PM KPI
3.2 & 3,3 Operator fetches PM KPI from DCAE DB (historic data can also be visualized in DB) via DES MS
1
3rd Party CN NSSMF
ONAP
Impacts
DCAE – KPI Compute MS/PM mapper, DB
SDC – Slice template enhancements
Policy – Config policies
EXT-API – TMF 628 (stretch goal)
UUI – Input & Visualization
Enhancement
New for this use case
EXT-API
DES
3.3











Done
Partially done

Not done


## Slide 28: Honolulu proposal for Slice KPI monitoring
REQ-5a: Complete the missing parts of Guilin implementation, and re-assess if KPI computation should be done in PM-Mapper or in a separate MS within DCAE.
REQ-5b: ONAP as NSMF/NSSMF shall monitor certain KPIs for Closed Loop or Intelligent Slicing (list of KPIs to be policy driven).
REQ-5c: Support retrieval of historic PM and KPI data for presentation to UUI upon request (enhancements to Guilin functionality)
Assumption for H-release: Data from all instances of an NF is aggregated. In other words, ONAP shall NOT do aggregation of same PM data (e.g., throughput) coming from different instances of same NF, and shall also NOT check and/or wait for all NF instances to report the PM data before computing KPIs.
2 additional inputs on what KPIs to be monitored:
  Operator/tenant through KPI monitoring facility in UUI
  Operator/slice consumer through service profile (Stretch goal)

## Slide 29: Closed Loops for Network Slicing: Overview
29
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SO)
5G Network
Leverage the SON  Control Loop (CL) framework in ONAP
Based on PM/FM data, analyze NSI/NSSI traffic patterns, KPI adherence, and resource occupancy in NSI/NSSI
Based on analysis, trigger OOF for NSI resource optimization/re-allocation to guarantee KPI adherence and optimal use of resources
Perform necessary resource adjustments via SO and Domain Controllers (modify NSI/NSSI/S-NSSAI mapping/etc.)
FM, PM data
5G network
DCAE
Domain
Controllers

## Slide 30: Guilin recap: Closed Loop
Slice Analysis MS
PM Mapper
Policy
SO (RAN NSSMF)
SDN-R
Config DB
Near RT-RICs
CUs
DUs
The PM data collected from RAN in Step 1 is DL/UL PRB used for data traffic.
The configuration update determined by Slice Analysis MS and triggering Policy in Step 4 is slice specific throughput guidance for Near-RT coverage area (i.e., at Near-RT RIC level).
Notes
DFC and VES Collector are not shown in the flow but are used.
Step 8 is over O1, it will eventually be over A1.
Config DB which contains RAN config info is not an official ONAP component. This will be implemented as part of C&PS in H-release and beyond.
1
2
3
4
5
6
7
8
DCAE
O1
O1

## Slide 31: Guilin recap: Intelligent Slicing
31
Slice Analysis MS
ML MS (offline trained)
Policy
SO (RAN NSSMF)
SDN-R
Config DB
Near RT-RICs
CUs
DUs
1
3
4
5
6
7
8
9
DCAE
PM Mapper
2
The PM data collected from RAN in Step 1 is PDU sessions requested, setup successfully & failures.
The configuration update determined by ML MS and triggering Slice Analysis MS in Step 3 is slice specific maxNumberofConns for each cell (i.e., cell level for each S-NSSAI).
Notes
DFC and VES Collector are not shown in the flow but are used.
Step 8 is over O1, it will eventually be over A1.
ML MS is onboarded to DCAE, but not an official ONAP component. Later we will onboard using Acumos DCAE adaptor.
Config DB which contains RAN config info is not an official ONAP component. This will be implemented as part of C&PS in H-release and beyond.
O1
O1

## Slide 32: Honolulu proposal for Closed Loop & Intelligent Slicing
REQ-6a: Based on RAN and Core PM and KPI data, initiate Closed Loop actions for resource optimization.
RAN and Core NSSMF determining the changes to be done at NSSI level
NSMF determining changes to be done at NSI level is a stretch goal.
REQ-6b: Based on RAN and Core PM and KPI data, based on ML models, determine necessary actions to ensure KPI adherence.
RAN and Core NSSMF determining the changes to be done at NSSI level
NSMF determining changes to be done at NSI level is a stretch goal.
Details of exact scenarios are being worked out within the use case team, considering also CNF orchestration work progress, as well as collaboration with O-RAN.A

## Slide 33: Honolulu requirements summary
Requirement | Content
Provide a full E2E Slicing solution involving Core, RAN & Transport NSSMF | Enhancements in the E2E Slice allocation & stitching together all subnets Slice selection taking into account capacity, resource occupancy levels, etc. TMF 641 API support for slice LCM operations (stretch goal)
RAN Slicing enhancements | Instantiation of RAN NFs and initial configuration (RAN service) (O2 – stretch goal) Enhancements in interactions with NSMF (endpoints, slice profile) and TN NSSMF Mapping Slice Profile to each Near-RT RIC Use of A1 interface for Closed Loop and AI/ML RAN (re) configuration enhancements
Core Slicing enhancements | Configurations of Core Slice Subnet Placement of Core NFs (stretch goal)
Transport Slicing enhancements | Enable reuse of existing TN NSSI (consider also endpoints) Resource occupancy levels of TN NSSI Standard interfaces and info model enhancements Support MP2MP connectivity (stretch goal)
Modeling (indicated as a separate track but many aspects are linked with other tracks) | Service and Slice Profile, endpoints related enhancements RAN slice sub-net modeling enhancements (including front-haul and mid-haul) NST not containing NSST list, but only sub-net list (stretch goal)
KPI Monitoring, Closed Loop and use of AI/ML | PM data collection and KPI computation (Guilin carry-over) Closed Loop and AI/ML at e2e slice and slice subnet level for RAN & Core TMF 628 for PM data collection – first steps (stretch goal)
Bold – Priority 1

## Slide 34: Additional considerations
Alignment/collaboration with CPS for RAN configuration
Alignment with O-RAN for RAN Slicing
Alignment with IETF evolution for Transport Slicing
First steps towards TMF 628-based PM/KPI monitoring
Alignment with CNF orchestration
Interaction with Core NFs – NSSF, NWDAF (beyond H-release)

## Slide 35: Demo Scenarios
E2E Slice Service Creation resulting in:
(a) Creation of a new e2e slice with new RAN, Core, Transport slice subnets
(b) Creation of a new e2e slice with new RAN, but reuse Transport & Core slice subnets
(c) Reuse an existing e2e slice
E2E Slice Service activation
E2E Slice Service deactivation
E2E Slice Service termination, resulting in:
Removal of mapping of service to the e2e slice
Removal of NSI, and its associated configuration in constituent NSSIs
Removal of NSI, deallocation of constituent NSSIs
KPI monitoring via portal
Closed Loop Control scenario for slice resource optimization
Intelligent Slicing scenario for SLA guarantee
Stretch goal: (Simulated) traffic flow demo through NSI constituting of RAN, Core and Transport slice subnets created by ONAP.

## Slide 36: Links
Main use case page for Guilin
  https://wiki.onap.org/display/DW/E2E+Network+Slicing+Use+Case+in+R7+Guilin
Flows (see child-pages)
  https://wiki.onap.org/display/DW/Use+case+flows
Guilin release assumptions
  https://wiki.onap.org/display/DW/Assumptions+for+Guilin+release
Main use case page for Honolulu
  https://wiki.onap.org/display/DW/R8+E2E+Network+Slicing+use+case

## Slide 37
Thank You!