## Slide 1
E2E Network Slicing use case : Overview, Roadmap & Guilin Demo
Participants: CMCC, Wipro, Huawei, AT&T, IBM, LTTS, DT, TIM, QCT, Amdocs, Tech Mahindra, Reliance Jio, Tencent, China Telecom, highstreet technologies
Presenters: Lin Meng (CMCC), Swaminathan S (Wipro),
Henry Yu (Huawei), Milind Jalwadi (Tech Mahindra)

## Slide 2: Slice Management Functions (3GPP-defined)
Ref.: 3GPP 28 series
Management Function | Key tasks
Communication Service Management Function (CSMF) | Responsible for translating the communication service related requirement to network slice related requirements. Communicate with Network Slice Management Function (NSMF).
Network Slice Management Function (NSMF) | Responsible for management and orchestration of NSI. Derive network slice subnet related requirements from network slice related requirements. Communicate with the Network Slice Subnet Management Function (NSSMF) and Communication Service Management Function.
Network Slice Sub-net Management Function (NSSMF) | Responsible for management and orchestration of NSSI. Communicate with the NSMF.

## Slide 3: Network Slicing: 3GPP Context
3GPP TS 28.530 v15.2.0
This has some implications w.r.to realization of NSSMF functionality and is not considered IN ONAP, as there is no clarity yet on the real purpose and background.
3GPP TS 28.530 v15.1.0


## Slide 4: ONAP-based Slice Management: Overall Architecture Choices
NSMF (ONAP)
CSMF (ONAP)
TMF APIs
NSSMF(s)
(ONAP)
xNFs
NSMF (ONAP)
CSMF
NSSMF(s)
(ONAP)
xNFs
NSMF (ONAP)
CSMF
NSSMF(s)
xNFs
NSMF (ONAP)
CSMF (ONAP)
TMF APIs
NSSMF(s)
xNFs
NSMF
CSMF
NSSMF(s)
(ONAP)
xNFs
3rd party component
1
2
3
4
5
3GPP APIs
3GPP APIs
Standard APIs
Standard APIs
Internal call
Internal call
Internal call
Internal call
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
Standard APIs
In H-release, we will continue with enhancements for Scenario 1, & address a few gaps in Scenario 4.
Achieved so far for Core & RAN subnets
Started in Guilin for all 3 subnets

## Slide 5: ONAP-based Slice Management: NSI Life Cycle view
Frankfurt/Guilin scope
Ref.: 3GPP TS 28.530
Design and pre-provision: Creation of necessary slice/slice sub-net templates.
Instantiation/Configuration, Activation/Deactivation and deallocation/termination of NSIs, including its constituent NSSIs (RAN, Core and Transport).
Objective: Demonstrate e2e slice design, instantiation and operation, including RAN, core and transport slice sub-nets.
Focus area for Honolulu for new functionality

## Slide 6: E2E Network Slicing: Architecture & Interfaces
Core Slice Subnet
RU
DU
CU
Core
Front Haul
Mid Haul
Back Haul
TN
TN
TN
NSMF
RAN NSSMF
TN NSSMF
Transport Slice Subnet 1
Transport Slice Subnet 2
Transport Slice Subnet 3
ONAP
Transport Network Configurations
Align with TSCi (IETF) (Note 2)
Align with 3GPP/O-RAN
Core NSSMF
Align with 3GPP
3rd Party
RAN NSSMF
RAN Slice Subnet
CSMF
3rd Party
Core NSSMF
Align with 3GPP (Note 1)
Align with TMF
OSS/NB System
Notes:
This interface is needed only for deployment scenario 1 (see later slides).
Several aspects are also aligned to ETSI ZSM.
Not yet implemented
Align with 3GPP
Align with 3GPP (Note 3)
Near-RT RIC

## Slide 7: RAN & Transport Slicing: Scenario 1
7
CSMF
NSMF
RAN NSSMF
Transport NSSMF
Core NSSMF
Fronthaul subnet
Mid haul subnet
Backhaul subnet
RAN NFs Subnet
Core subnet
1a
3
1
2
1b-i
1b-ii
1b-iii
3a
2a
TS_1 is backhaul transport slice; TS_3, fronthaul; TS_4, midhaul.
TN MD (T-NSSMF) receives TS_1 from NSMF (step 3), and TS_3 and TS_4 from RAN NSSMF (step 1b-i).
TN MD then configures backhaul (3a), fronthaul (1b-ii), and midhaul (1b-iii), respectively.
TS_1
TS_3
TS_4
RAN NSSMF shall be responsible for determination of Slice Profile of FH, MH and RAN NFs.
RAN NSSMF shall be responsible for entire RAN subnet comprising FH and MH (stitching together, CL actions, etc.)
Preferred option by O-RAN
& ONAP internal RAN NSSMF
In H-release, we will continue to enhance this option (including RAN <-> TN NSSMF interactions)

## Slide 8: RAN & Transport Slicing: Scenario 2
CSMF
NSMF
RAN NSSMF
Transport NSSMF
Core NSSMF
Fronthaul subnet
Mid haul subnet
Backhaul subnet
RAN NFs Subnet
Core subnet
1a
3
1
2
3a-ii
3a-iii
3a-i
2a
TS_1 is backhaul transport slice; TS_3, fronthaul; TS_4, midhaul.
TN MD (T-NSSMF) receives TS_1, TS_3 and TS_4 from NSMF (step 3).
TN MD then configures backhaul (3a-i), fronthaul (3a-ii), and midhaul (3a-iii), respectively.
TS_1
TS_3
TS_4
NSMF shall be responsible for determination of Slice Profile of FH, MH and RAN NFs.
NSMF shall be responsible for stitching together e2e slice including FH and MH.
Preferred option for external
RAN-NSSMF, E2E Slicing
In H-release, we will start implementing this option in ONAP’s RAN NSSMF
(stretch goal)

## Slide 9: Honolulu proposal for E2E Slicing solution involving Core, RAN & Transport
REQ-1a: Enhancements in the E2E Slice allocation & stitching together all subnets
Enhancements in CSMF and NSMF (Guilin non-critical bugs and carryover items)
Endpoint enhancement : TN NSSI selection and connection link selection to be made by NSMF
3GPP API alignment and model enhancements related impacts
Enhancements in Service profile decomposition to Slice Profile: mapping rules for each attribute
REQ-1b: Slice selection taking into account capacity, resource occupancy levels, etc.
Capacity definition for various sub-nets
NSI selection and NSSI selection based on capacity, resource occupancy levels (partly stretch goal)
NSMF to support monitoring and update of resource levels at NSI level
Coverage area to TA list mapping (and considering it for RAN NSSI selection)

## Slide 10: E2E Network Slicing: Impacts for CSMF/NSMF enhancements
NSMF Portal
SDC
U-UI
NST
NSMF
Slice Profile determination
NST Selection
NSI Selection
NSMF Policy
SO
OOF
Policy
Service instance
Service Profile
NSI
NST
A&AI
ONAP
EXT-API
NSSMF (RAN, Transport, Core)
KPI Computation MS
Analysis MS
RAN Configurations
CPS
DCAE
Service Profile Template
Slice Profile Template
Data Exposure Service
NSSMF Adaptor
TMF 641 APIs
Enhanced interface
New interface
New/enhanced interface, stretch goal
Stretch goal
CSMF Portal
Stretch goal

## Slide 11: Honolulu proposal for RAN Slicing
11
REQ-2a: Instantiate RAN NFs, RAN “service” and perform initial configuration as part of slice allocation actions (Modeling is in scope, full functionality is a stretch goal)
REQ-2b: Support end-point related enhancements for E2E Slicing and RAN<->TN interactions
REQ-2c: Map RAN Slice Profile to each Near-RT RIC-level configuration
REQ-2d: Support A1 interface for Closed Loop and AI/ML based config update guidance from Non-RT RIC to Near RT-RIC
REQ-2e: Consume necessary PM/FM info from RAN, for Closed Loop Actions/Intelligent Slicing
REQ-2f: Appropriately configure/re-configure RAN resources (dependency on O-RAN models)
REQ-2g: Appropriate RAN resource determination
ONAP
RAN
CUs
DUs
A1
Notes
O2 interface is considered as a stretch goal for RAN Slicing
Alignment with O-RAN information models to be considered in scope.
The goal is to have an MVP of the CPS for this use case to be realized in this release.
TA <-> Cell mapping inventory to reside in CPS
RAN slice inventory
List of cells, DUs, Cus, Near-RT RIC with details of active slices
Capacity & capability of RAN subnet
RUs
Near RT-RIC
O1
O2 (Stretch goal)

## Slide 12: RAN Slicing: Impact overview
SDC
SO
OOF
Policy
NSSI
NSST
Slice Profile
A&AI
ONAP
NSSI Selection
NSST
NSSMF (RAN)
KPI Computation MS
Analysis MS
AI/ML MS
RAN-specific config
CCSDK/SDN-C
RAN Configurations
RAN slice related configurations
CPS
NSSMF Policy
DCAE
RAN (Simulator)
Slice Profile Template
Data Exposure Service
NSSMF Adaptor
NSSMF (TN)
Enhanced interface
New interface
New/enhanced interface, under discussion
Stretch goal
Endpoints
O1, A1

## Slide 13: Honolulu proposal for Core Slicing
REQ-3a: Enhance the configuration of the Core NFs beyond basic aspects such as S-NSSAI.
Exact details and NFs are still under discussion.
REQ-3b: Determine placement of Core NFs during Core NSSI instantiation (stretch goal)
Details are being discussed, including the role of Core NSSMF.

## Slide 14: Core Slicing: Impact overview
SDC
SO
OOF
Policy
NSSI
NSST
Slice Profile
A&AI
ONAP
NSSI Selection
NSST
KPI Computation MS
Analysis MS
AI/ML MS
NSSMF Policy
DCAE
Core NFs (Simulator)
Slice Profile Template
Data Exposure Service
NSSMF Adaptor
NSSMF (Core)
Core NF placement
Enhanced interface
New interface
New/enhanced interface, under discussion
Stretch goal
Stretch goal
Core NFs configuration
CDS
Endpoints

## Slide 15: Honolulu proposal for Transport Slicing
Category | Requirement |  | Notes
Architectural and Functional requirements | AR1 | none | Honolulu release will use the same architecture as that in Guilin release.
 | FR1 | Support reuse and modification of existing TN NSSIs | Selection of an existing TN NSSI for reuse/sharing (TN NSSMF provides model/interface for OOF) Modify TN NSSI SLA Modify endpoints (add or delete endpoints from TN NSSI), and endpoint connections
Modeling | MR1 | Minor fixes and updates in TS definition models and implementation models | Align service profile and slice profile model with latest 3GPP NRM
Transport Slicing enhancements is being covered as part of REQ-456 along with CCVPN use case. The architecture for Transport Slicing, its interfaces and TN NSSMF design principles shall align with the E2E Network Slicing use case. While the next few slides provide an overview of Transport Slicing enhancements in Honolulu release, refer to REQ-456 for more details about the Transport Slicing aspects.

## Slide 16: FR1: Modify/reuse existing TN NSSI: Four scenarios
Modify (increase or decrease) max-bandwidth of existing connection-links
Add new (or remove existing) connection-links
Increase max-bw
EP1
Max-banwidth 20G
EP2
Transport Slice
RAN slice
CORE slice
EP1
Max-banwidth 30G
EP2
Transport Slice
RAN slice
CORE slice
EP X
EP Y
EP X
EP Y
Add connection link
EP1
Max-banwidth 20G
EP2
Transport Slice
RAN slice
CORE slice
EP1
Max-banwidth 20G
EP2
Transport Slice
RAN slice
CORE slice
EP X
EP Y
EP X
EP Y
Max-banwidth 20G
decrease max-bw
Delete connection link
1
2
3
4

## Slide 17: TN NSSI modification: Call flow from CCVPN perspective
SO
TN NSSMF Work Flow
NSMF Work Flow
Internal APIs (TSCi)
AAI
TS definition model (based on TSCi info model)
SDNC
ACTN MPI Adaptor (SBI)
Optical domain controller
ONAP
OOF
Policy
TS implementation models (e.g., te-topology, te-tunnel, etc.)
UUI
TN NSSMF Adaptor
Generic-resource-API
TSC NBI-to-SBI Mapping
SDC
New ONAP code for TN NSSMF Functionality added in Guilin
Existing ONAP code with modifications
1
3
2
4
5
7
6
8
9
10
Upon allocate TN NSSI invocation, TN NSSMF adaptor calls OOF for making TN NSSI selection decision.
OOF makes TN NSSI selection and returns to TN NSSMF adaptor.
TN NSSMF adaptor calls TN NSSMF’s modify TN NSSI API – a new API in H release.
TN NSSMF work flow processes the request
TN NSSMF updates the TN NSSI with new parameters
After AAI is updated, TN NSSMF calls SDNC’s modify TN NSSI API – a new API in H release.
SDNC TSC NBI-to-SBI mapping DGs compare the parameters in the new TN NSSI definition with the ones in the TS implementation models (e.g., running network configurations), and identify the differences.
SDNC TSC NBI-to-SBI mapping DGs updates the TS implementation models with new network configurations.
SDNC ACTN MPI adaptor (SBI) DGs convert the new network configurations into ACTN MPI payloads.
ACTN MPI adaptor calls the external optical domain controller via ACTN MPI interfaces.
Note: Refer also to REQ-456.

## Slide 18: TN NSSI modification: A model driven approach
Network service models
Network resource models
TS definition model managed by SO. The model is intent-like, technology agnostic, and is the TN NSSMF NBI.
TS implementation models managed by SDNC. They are technology specific network configurations, and are encapsulated from the TN NSSMF’s consumer.
TN NSSMF NBI-to-SBI mapping function managed by SDNC. After SO modifies TS definition model, the mapping function will find the diff and apply the changes to the implementation models (i.e., network configs).

## Slide 19: Transport Slicing: Impact overview
SDC
SO
OOF
Policy
NSSI
NSST
Slice Profile
A&AI
ONAP
NSSI Selection
NSST
NSSMF (TN)
KPI Computation MS
Analysis MS
AI/ML MS
Transport specific config
CCSDK/SDN-C
NSSMF Policy
DCAE
TN SDN controller
Slice Profile Template
Data Exposure Service
NSSMF Adaptor
Slice Profile decomposition (RAN, RAN NF)
Enhanced interface
New interface
Stretch goal
Endpoints
TN related enhancements
New/enhanced interface, under discussion

## Slide 20: Transport Slicing future roadmap: Closed-loop Automation
Optical network
Optical network
ONAP
On-line Plan
Auto Deploy
Topo & Service
Performance & Alarm
Maintain & Optimize
Intelligent
Analysis
Self-service provisioning
Network design & deploy
Network Assurance
2
1
3
4
Phy. network controllers
Service provisioning and activation:
  Days  Minutes
Network planning and deployment:
  Weeks  Days
Network troubleshooting and restoration:
  Hours  Minutes
Traffic prediction based auto network planning:
  Months  weeks
Four Types of Closed-loop Automation
2018：L2 service
2019：L1 service
2020：Transport Slicing
2021：New CPE online and deployment (and auto service activation)
2022+：Network performance prediction based service disruption prevention
CPE
CPE
Looking beyond Guilin release, we are looking for further collaboration with ZSM on closed-loop automation.
NEs

## Slide 21: KPI Monitoring: Guilin implementation & Honolulu proposal
Design Time
Run Time
NSMF Portal
(Management Portal)
DCAE
Policy
KPI Config Policy
SDC
UUI/Portal
CSMF Portal
(Tenant Portal)
NST Model
(Including KPI Monitoring )
NSST Model
Onboard
5G PM Data Collector
(VES / REST )
Tenant
Service Provider
Mongo DB (historic & current KPI)
KPI Computation MS
2.1
2.2
2.3
3.1
3.2
3.1
3.2
1
3rd Party CN NSSMF
ONAP
New in Honolulu
New in Guilin
EXT-API (TMF 628 APIs)
DES
3.3











Done
Partially done

Not done

Implement KPI Computation as a new generic MS in DCAE.
Support retrieval of historic PM and KPI data for presentation to UUI upon request (same as Guilin functionality).
Start with TMF 628 API support if feasible (stretch goal)
Assumption: Data from NFs is already aggregated and then presented to ONAP.
Stretch Goal in Honolulu
New in Honolulu
Out of scope in Honolulu

## Slide 22: Closed Loop: Overview
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SO)
5G Network
Leverage the SON  Control Loop (CL) framework in ONAP
Based on PM/FM data, analyze NSI/NSSI traffic patterns, KPI adherence, and resource occupancy in NSI/NSSI
Based on analysis, trigger OOF for NSI resource optimization/re-allocation to guarantee KPI adherence and optimal use of resources
Perform necessary resource adjustments via SO and Domain Controllers (modify NSI/NSSI/S-NSSAI mapping/etc.)
FM, PM data
5G network
DCAE
Domain
Controllers

## Slide 23: Closed Loop: Roadmap
Use data (e.g., QoE data, network data, etc. ) from various sources as input and do analysis based on AI algorithms to obtain network capabilities that can match the SLA of tenants, and then dynamically adjust the service capabilities of network slices while using optimal resources. It mainly consists of the following three scenarios:
Commissioning-Initial resource Assignment
Determine the initial resource assignment and configuration for a new slice by intelligent analysis based on SLA requirement. For e.g.:
Determine the resources in each domain especially for RAN
Guarantee the existed slices SLA when creating a new slice
Runtime-monitoring
Evaluate the SLA fulfillment and real time monitor QoE based on the QoE model trained by ML algorithms.
The QoE model is used to describe the relationship between the QoE collected from AFs and the KPIs produced by ONAP or network data from Core & RAN NFs.
The QoE model is mainly used in measuring and predicting QoE.
Closed-loop Update
Considering the limited resource and changing condition like the Signal to Noise Ratio and users on the slice, the initial resource configuration may not be able to satisfy the slice SLA during the lifecycle of the slice. ONAP can adjust or update the resource configuration of the slice in a close loop way triggered by the analysis of SLA fulfillment.
SLA fulfillment is evaluated based on the analysis of QoE info and KPIs.
1
2
3
KPI Monitoring for Honolulu
QoE Monitoring is beyond Honolulu
Not for Honolulu
Closed loop control triggered by RAN KPI monitoring for Honolulu

## Slide 24: Closed Loop: Guilin scope and proposal for Honolulu
Slice Analysis MS
PM Mapper
Policy
SO (RAN NSSMF)
CCSDK/SDN-C (SDN-R)
CPS
Near RT-RICs
CUs
DUs
The PM data collected from RAN in Step 1 is DL/UL PRB used for data traffic.
The configuration update determined by Slice Analysis MS and triggering Policy in Step 4 is slice specific throughput guidance for Near-RT coverage area (i.e., at Near-RT RIC level).
Step 8 is over O1 in Guilin, it will be over A1 in Honolulu (using A1 adaptor).
Additional PM data to be used is under discussion.
Notes:
DFC and VES Collector are not shown in the flow but are used.
Initial configuration may also be over A1 (based on Slice Profile decomposition) – this is under discussion with O-RAN.
1
2
3
4
5
6
7
8
DCAE
O1
O1 A1
ONAP
RAN (Simulator)
RUs
Enhancements for Honolulu
New interface for Honolulu

## Slide 25: Intelligent Slicing: Guilin Scope & proposal for Honolulu
Slice Analysis MS
ML MS (offline trained)
Policy
SO (RAN NSSMF)
CCSDK/SDN-C (SDN-R)
CPS
Near RT-RICs
CUs
DUs
1
4
5
6
7
8
9
10
DCAE
PM Mapper
2
The PM data collected from RAN in Step 1 is PDU sessions requested, setup successfully & failures.
The configuration update determined by ML MS and triggering Slice Analysis MS in Step 3 is slice specific maxNumberof Conns for each cell (i.e., cell level for each S-NSSAI).
Step 10 is over O1 now, it will continue to be in O1 based on latest discussions with O-RAN community.
Notes
DFC and VES Collector are not shown in the flow but are used.
ML MS is onboarded to DCAE, but not an official ONAP component. Later we will consider onboarding via Acumos DCAE adaptor.
Initial configuration may also be over A1 (based on Slice Profile decomposition) – this is under discussion with O-RAN.
O1
O1
ONAP
RAN (Simulator)
RUs
Enhancements for Honolulu
New interface for Honolulu
3

## Slide 26: Modeling aspects
Endpoints
Enhancements to Service Profile, Slice Profile (and their mapping)
RAN Service modeling
Generic modeling to support both options of RAN and Transport Slicing

## Slide 27: E2E Network Slicing: Impact Summary
CSMF Portal
NSMF Portal
SDC
U-UI
NST
CSMF
NSMF
NST Selection
NSI Selection
Slice Profile determination
CSMF Policy
NSMF Policy
SO
OOF
Policy
Service instance
Service Profile
NSI
NST
NSSI
NSST
Slice Profile
A&AI
ONAP
EXT-API
NSSI Selection
NSST
CST
NSSMF (RAN, Transport, Core)
KPI Computation in PM Mapper
Analysis MS
AI/ML MS
RAN-specific config
Transport specific config
CCSDK/SDN-C
Cell Configurations
RAN slice related configurations
CPS
NSSMF Policy
KPI Policies
CL Policies
DCAE
Core NFs configuration
CDS
RAN NSSMF (3rd party)
Slice profile decomposition
RAN-Simulator
Service LCM APIs
Service Profile Template
Slice Profile Template
Data Exposure Service
NSSMF Adaptor
Endpoints
TMF 628 APIs (PM)
Core NF Simulator
Core NSSMF (3rd party)
O1
A1
Enhanced interface
New interface
Under discussion
Stretch Goal

## Slide 28: E2E Network Slicing Alignment with SDOs
Standards Body | Alignment Reference(s)
3GPP (Rel. 16) | TS 28.530 (Concepts, requirements) TS 28.531 (Slice and Slice sub-net LCM) TS 28.541 (Network Resource Models) TS 23.501 (Procedures in Control Plane) TS 28.552 and TS 28.554 (PM and KPIs)
TMF | TMF 641 (Service Order – CSMF NB) TMF 628 (PM and KPI monitoring – just started)
ETSI | ZSM 002 ZSM Framework ZSM 003 E2E Network Slicing Architecture ZSM 009 Closed-loop Automation
IETF | draft-rokui-5g-ietf-network-slice-00 draft-ietf-teas-actn-vn-yang RFC 8795: YANG models for TE topologies
O-RAN | O1 (RAN Configuration, notifications, PM data) – in progress O2 (not started yet) A1 – just started RAN architecture and functional split (Non-RT RIC, Near-RT RIC, SMO) – in progress

## Slide 29: Additional aspects to be considered
PM data aggregation – within ONAP or outside ONAP?
  No impact to Honolulu content, however, it has to be clarified in general from an ONAP architecture perspective.
Alignment/collaboration with CPS for RAN configuration
  Already started, will take it forward in Honolulu
First steps towards (modernized) TMF 628-based PM/KPI monitoring
  Indicated as a stretch goal for Honolulu, will also depend on API being finalized in time.
Alignment with CNF orchestration
  To be discussed further, may be taken up beyond Honolulu
Interaction with Core NFs – NSSF, NWDAF
  To be taken up beyond Honolulu