## Slide 1
Intelligent Slicing Requirements and Roadmap
Participants: CMCC, Wipro, Huawei, AT&T, Deutsche Telecom, TIM, QCT, Amdocs, Tech Mahindra, Reliance Jio, Tencent, China Telecom, Fujitsu, highstreet technologies
Presenters: Lin Meng (CMCC), ), Swaminathan S (Wipro)

## Slide 2: Intelligent Slicing Roadmap and Status
life cycle management of a Slice Service/ NSI / NSSI
Design
Creation
Activation
Deactivation
Termination
Modification
Modification Operations for NSI/NSSIs
Modification during the time of slice allocation (TBA)
Close Loop Modification Triggered by Supervision (WIP)
Modification due to Service requirement change (TBA)
Reporting
PM Data Collection and Configuration (WIP)
FM Data Collection and Configuration(TBA)
Reporting from the lower level XMF to the upper level XMF (eg: from NSSMF NSMF network capability discovery) (WIP)
Supervision
Intelligent Slicing
Done in Frankfurt and Guilin,
Enhance in Honolulu and beyond
Start in Guilin,
Enhance in Honolulu and beyond
Start in Guilin,
Enhance in Honolulu and beyond
Start in Guilin,
Enhance in Honolulu and beyond
ML-based Modification Triggered by Supervision (WIP)

## Slide 3: Autonomous Network Slicing
Intent-based network slice instantiation & life cycle management
Closed Loop Automation: ML-based prediction, root cause identification and self-adaptation
Instantiation/reuse of appropriate slice (sub-net) based on self-learning
Autonomous Network Slicing (end-to-end and in RAN/Core/Transport sub-nets) based on intent(s) – self-instantiation; dynamic adaptation (re-configuration, scaling); self-prediction, root-cause identification and self-healing; self-optimization of network resources; proactive notification to inventory on capacity exhaustion.

## Slide 4: E2E Network Slicing Use Case Internal Collaborations
“E2E Network Slicing” Use Case
”Support for Vertical Industry” Use Case
“Support for Intent based Network” Use Case
“CCVPN” Use Case
5G Domain Use case
“SON” Use Case
Provide centralized O&M capabilities for both vertical industry networks and traditional mobile networks. Network capabilities of slices can be exposed to vertical industries.
Provide general framework for intent translation, intent decision and intent execution. It could trigger Slice LCM operation and support slice SLA guarantee scenarios at different intent levels.
Provide cross domain and cross layer(L1,L2,L3) VPN services from E2E perspective. Many existing CCVPN features can be reused to service L1 and L2 service slicing which belongs to transport slicing
Provide general framework within ONAP to perform close loop control, a whole process of which includes data collection, optimization, coordination and decision, action. By leveraging SON framework, we could realize slice resource optimization and allocation, furthermore, to support SLA guarantee.
Network resource related use case: PNF Plug and Play, 5G NRM, PNF Onboarding
Standard alignment use case: 3GPP/O-RAN Alignement; ETSI NFV Support
PM/FM releated use case: Bulk PM/PM data control

## Slide 5: Potential collaboration scenarios with IBN
Intent Decision and Execution
Intent Translation
Scenario 1:
NSI/NSSI allocation triggered by customer’s intent/ sub level intent
Scenario 2:
NSI/NSSI modification triggered by customer’s intent / sub level intent
Scenario 3:
Customer Intent translation into SLA parameters
Scenario 4:
KPI data as input assisting intent decision
Scenario 5:
Slice analysis result as input assisting intent decision
……….
……..
Intent Database
IBN Framework
Scenario 6:
Closed Loop feedback to improve intent mapping

## Slide 6: Closed Loop Control/Intelligent Network Slicing
Use data (e.g., QoE data, network data, etc. ) from various sources as input, analysis such slice related data and make prediction by using AI algorithms, generate optimal decision and execute in a closed loop way.
3 cases for ONAP E2E Network Slicing implementation by introducing new SON functions:
(Cross) Slice Resource Optimization
KPI Adherence Optimization（KPI Guarantee）
The goal of maximizing KPI adherence is to maximize/improve KPI adherence by NSIs to the supported services. This action will be triggered when the performance needs to be improved. By monitoring the KPI adherence, and analyzing the trends and correlating it with resource usage data, etc. (using ML models), perform necessary modifications to the NSI/NSSI to maximize KPI adherence.
Service Experience Optimization (SLA Guarantee)
Considering the limited resource and changing condition like the Signal to Noise Ratio and users on the slice, the initial resource configuration may not be able to satisfy the slice SLA during the lifecycle of the slice. ONAP can update the resource configuration of the slice in a closed loop way triggered by the analysis of SLA fulfillment.
SLA fulfillment is evaluated based on the analysis of QoE info and KPIs.
1
2
3
Simple control loop with ML model: started in Guilin, complete in Honolulu
Simple Control Loop for single slice scenario: Guilin & Honolulu
Beyond Honolulu
The goal of resource optimization is to optimize the resource allocation within the total available physical and virtual resources, while adhering to the KPI levels.
So the trigger for resource optimization determination would be the changes in the network resources usage, and traffic patterns.
Later, ‘over-fulfillment of KPIs’ could also lead to resource optimization.

## Slide 7: Slice KPI Monitoring
Run Time
NSMF Portal
(Management Portal)
DCAE
Policy
Config Policies
UUI/Portal
CSMF Portal
(Tenant Portal)
Tenant
Service Provider
KPI Computation MS
ONAP
EXT-API
5G NFs
FM/PM data collection
1. Tenant/Operator to monitor the KPI via the UI portal
2. Slice management system internal KPI supervision & analysis
NST model incl. KPI
SDC
Impacts
DCAE – New KPI Computation MS, Data Lake Data Exposure Service (DES)
SDC – Slice template enhancements
Policy – Config policies
EXT-API – External interface
UUI – KPI monitoring inputs, and display
VES Collector
DFC
DataLake-DES
DataLake
Feeder
Big Data
DataBase
PM-Mapper
PMSH
Slice Analysis MS

## Slide 8: (Generic) Computation MS
Periodic KPI computation based on VES inputs
Slice Analysis MS
AI/ML MS
New Service/Slice profile (Note)
DMaaP
Compute request
PM data (VES)
1
3
6
Computation result
Slice Analysis MS
AI/ML MS
Data Lake Feeder
7
Policy
KPI config policies – formula, data source, etc.
Computation MS
DES (fetch data from DL)
AAI
Step | Description | Step | Description
1 (Note) | Trigger to compute a KPI, attribute, etc. | 4b | (Optional) Fetch required data from DL
2 | Fetch config policies for data source(s), formula, KPI list (Note) | 5a | Data received from all sources? If yes go to next step
3 | PM mapper posts PM data over VES | 5b | Compute KPI or other attribute based on formula
4a | Fetch inventory details (to know data from which NFs to use) | 6,7 | Post computation result on DMaaP, which is consumed by requestor and Data Lake Feeder
2
5a
4b
5b
4a
Future extension to enable more flexibility and greater reusability
Note

## Slide 9: Intelligent analysis assists Slice KPI/SLA Guarantee
Config Data
PM/FM Data
KPI Data
(NSI/NSSI/S-NSSAI level)
Network Data
(5GC NF level)
E.g.: QoS flow data, UE location, etc.
KPI/SLA Fulfillment Monitoring
(limited functionality in Guilin)
OAM Data
Non OAM Data
Application Data
QoE Data
(AF level)
Closed loop control
Determine changes, & Update Slice Resources and Configuration
(Limited updates till now)
Data Collection
Data Analysis
Input
Input
Input
Input
Input
Input
refers to G/H-release
scope




AI/ML Model:
KPI/SLA prediction
(Beyond Guilin: QoE prediction)


Trigger


## Slide 10: Closed Loop Control for NSI resource optimization
10
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SO)
5G Network
Leverage the SON  Control Loop (CL) framework in ONAP
Based on PM/FM data, analyze NSI/NSSI traffic patterns and resource occupancy in NSI/NSSI resources
Based on analysis, trigger OOF for NSI resource optimization/re-allocation
Perform necessary resource adjustments via SO and Domain Controllers (modify NSI/NSSI)
FM, PM data
5G network
SO
SO
Domain
Controllers

## Slide 11: Closed Loop: Guilin scope and proposal for Honolulu
Slice Analysis MS
PM Mapper
Policy
SO (RAN NSSMF)
CCSDK/SDN-C (SDN-R)
CPS
Near RT-RICs
CUs
DUs
The PM data collected from RAN in Step 1 is DL/UL PRB used for data traffic.
The configuration update determined by Slice Analysis MS and triggering Policy in Step 4 is slice specific throughput guidance for Near-RT coverage area (i.e., at Near-RT RIC level).
Step 8 is over O1 in Guilin, it will be over A1 in Honolulu (using A1 adaptor).
Additional PM data to be used is under discussion.
Notes:
DFC and VES Collector are not shown in the flow but are used.
Initial configuration may also be over A1 (based on Slice Profile decomposition) – this is under discussion with O-RAN.
1
2
3
4
5
6
7
8
DCAE
O1
O1 A1
ONAP
RAN (Simulator)
RUs
Enhancements for Honolulu
New interface for Honolulu
Trigger OOF for determining optimal re-configuration later

## Slide 12: Intelligent Slicing: Guilin Scope & proposal for Honolulu
Slice Analysis MS
ML MS (offline trained)
Policy
SO (RAN NSSMF)
CCSDK/SDN-C (SDN-R)
CPS
Near RT-RICs
CUs
DUs
1
4
5
6
7
8
9
10
DCAE
PM Mapper
2
The PM data collected from RAN in Step 1 is PDU sessions requested, setup successfully & failures.
The configuration update determined by ML MS and triggering Slice Analysis MS in Step 3 is slice specific maxNumberof Conns for each cell (i.e., cell level for each S-NSSAI).
Step 10 is over O1 now, it will continue to be in O1 based on latest discussions with O-RAN community.
Notes
DFC and VES Collector are not shown in the flow but are used.
ML MS is onboarded to DCAE, but not an official ONAP component. Later we will consider onboarding via Acumos DCAE adaptor.
Initial configuration may also be over A1 (based on Slice Profile decomposition) – this is under discussion with O-RAN.
O1
O1
ONAP
RAN (Simulator)
RUs
Enhancements for Honolulu
New interface for Honolulu
3
Consider onboarding via Acumos-DCAE Adaptor later