## Slide 1
PNF Pre-Onboarding / Onboarding & Modeling to Support 5G RAN
ONAP Modeling
PNF Onboarding
Mar 18, 2019 version 6 / 3:45PM Pythagore, Nozay, France
Benjamin Cheung, PhD
Michela Bevilacqua
Zu Qiang

## Slide 2
Onboarding and Design Time
WHO
WHEN
WHAT
Onboarding Package
Platform ONAP Model
SDC CSAR Artifacts
NF Instance
Package Delivery
Onboarding
Design Time
Run Time
Vendor
Technology Specialist
Asset Manager
Service Designer
Operations Specialist
Operations Specialist
SOL 004 Package
-
-
-
Platform Information Model
Platform Data Model
PNF Descriptor Model
Onboarding Descriptor
Pre-Onboarding
Technology Specialist
Asset Manager
SOL 001 PNFD
-
CSAR (VSP, VF, Service)
PNF Package Artifacts (CSAR)
NF Discovery, Instantiation
Run time Catalog

## Slide 3
Onboarding and Design Time
WHO
WHEN
WHAT
xNF Package
Resource Creation
Service Creation
Service Instantiation
Package Delivery
Onboarding
Design Time
Run Time
Vendor
Technology Specialist
Asset Manager
Service Designer
Operations Specialist
Operations Specialist
SOL 004 Package
SOL 001 xNFD
-
-
-
Platform Information Model
Platform Data Model
Validating xNF Package
Validation
Pre-Onboarding
Technology Specialist
Asset Manager
SOL 004 Package
Service CSAR
(VSP, VF, Service)
xNF Package Artifacts (CSAR)
xNF Descriptor Model
NF Discovery, Instantiation
Run time Catalog

## Slide 4
Pre-onboarding/Onboarding in Design Time
KEY INFO
WHEN
WHAT
xNF Package
Resource Creation
Service Creation
Service Instantiation
Package Delivery
Onboarding
Design Time
Run Time
Onboarding Package
Resource CSAR
Service CSAR Creation
Service Instantiation
SOL 004 Package
SOL 001 xNFD
AID Model
-
Platform Information Model
Platform Data Model
Validating xNF Package
Validation
Pre-Onboarding
VNF-SDK Validation
SOL 001 PNFD
TOSCA/AID model
Service CSAR
(VSP, VF, Service)
xNF Package Artifacts (CSAR)
PNF Descriptor Model
NF Discovery, Instantiation
Run time Catalog

## Slide 5
Pre-onboarding/Onboarding in Design Time
KEY INFO
WHEN
WHAT
xNF Package
Resource Creation
Service Creation
Service Instantiation
Package Delivery
Onboarding
Design Time
Run Time
Onboarding Package
Resource CSAR
Service CSAR Creation
Service Instantiation
-
AID Model
-
Platform Information Model
Platform Data Model
Validating VNF Package
Validation
Pre-Onboarding
VNF-SDK Validation
-
TOSCA/AID model
Service CSAR
(VSP, VF, Service)
VNF Package Artifacts (CSAR)
VNF Descriptor Model
NF Discovery, Instantiation
Run time Catalog

## Slide 6
Vendor
Asset Manager
Service Designer
Operations
Onboarding and Design Time
Onboarding Package
NF Descriptor
Platform Model
NF Instance
Pre/Onboarding
Pre/Onboarding
Design Time
Run Time
NF
Descriptor
NF
Registration
PM Dictionary
PM Schema
Informational
Artifacts
Configuration
Files
Communication
Files
PNF
Onboarding
Package
Service
TOSCA
Root
Node
Network
Function
Virtual
Link
PNF
Device
Connect
Point
NF
Comp
Complex
Ports / NICs
Connectivity
N
1
1
1
N
1
SDC
Catalog
A&AI
PNF
Instance
Current Platform Data Model
Vs. Target Platform Data Model

## Slide 7
PNF PRE-ONBOARDING/ONBOARDING U/C OVERVIEW
PNF
Descriptor
NF
Registration
Informational
Artifacts
Configuration
Files
Communication
Files
SDC
Catalog
Onboarding
PNF
Onboarding
Package
+Vendor Meta-data
VF Model Information
SDC
Pre
Onboarding
VNF
SDK
Distribute
SO, AAI,
DCAE etc.
SDC Service
CSAR Package
Dublin Priority
Dublin Priority
Package Delivery
Onboarding
Design Time
Run Time
Onboarding Package
NF Descriptor
Platform Model
NF Instance
1. PNF Package Delivery: Vendor creates & delivers PNF Package with PNF artifacts
1
3. PNF Onboarding: PNF Package is loaded
3
2. PNF Pre-Onboarding (optional): VNF-SDK ( ) can create or validate PNF Onboarding Package
2
4 Design Time Activities: NF Onboard Package > SDC catalog
5. ONAP RT Components:
Ingest and use CSAR package
4
5
PM Dictionary
Schema (YAML)
VF Model
SDC Internal CSAR Package
(derived from the Vendor PNF Onboarding Package)

## Slide 8
DUBLIN DEVELOPMENT STATUS
COMPONENT | IMPACTS DESCRIPTION | JIRA TICKETS
SDC | PNF PACKAGE FORMAT Identify current VNF package format constraints in SDC Propose a PNF Package format Evaluate VNF and PNF package alignment PACKAGE MAPPING - Onboarding PNF package to internal PNF package mapping PNFD MAPPING - Onboarding PNFD to internal PNFD mapping A new flow to map ETSI SOL001 PNFD in SDC AID model. ARTIFACT MANAGEMENT Design-time catalog update to associate artifacts to a PNF Run-time catalog update to associate artifacts to a PNF | SDC-1970, SDC-1973, SDC-1974, SDC-1975, SDC-1976, SDC-1977, SDC-1978, SDC-1979, SDC-1980
VNF SDK | PACKAGE VERIFICATION - PNF package format verification PNF PACKAGE FORMAT PACKAGE USAGE - Package for PNF Onboarding Package for use in VNF SDK | VNFSDK-337, VNFSDK-338, VNFSDK-339, VNFSDK-340, VNFSDK-341, VNFSDK-342, VNFSDK-343
Modelling | PNFD MAPPING – Mapping Onboarded PNFD to platform PNFD mapping SDC SW task but PNFD mapping & part of ONAP Resource Data Model. | 
VNF Requirements | PACKAGE, DESCRIPTOR, ARTIFACTS - VNF requirements to cover PNF package contents and directory structures and mandatory elements. PNF DESCRIPTOR - Requirements for the PNF Descriptor ARTIFACTS - Requirements for Artifacts of PNF and PNF Package | VNFRQTS-506, VNFRQTS-496, VNFRQTS-497, VNFRQTS-498, VNFRQTS-499, VNFRQTS-505, VNFRQTS-507, VNFRQTS-508
RT Comp | Grant backward compatibility use cases on ONAP RT Components | 

## Slide 10
PNF PACKAGE CREATION & DELIVERY
Vendor
Onboarding Package
Onboarding

## Slide 11
PNF ONBOARDING PACKAGE
NF
Descriptor
NF
Registration
PM
Dictionary
Informational
Artifacts
Configuration
Files
VES Event
Registration
PNF-D
PM Dictionary
PM Schema
Manuals, Help files
Customer Doc Products
Test files
Licensing agreement
Resource
Configuration Info
Communication
Files
Ansible Playbooks
Netconf Yang model
Chef Cookbooks
PNF Onboarding Package
Manifest
File
TOSCA
Metadata
(SDC)
SDC Added Files
TOSCA
Metadata
PNF Package Artifacts
Definition Files
Vendor Provided
SDC Service
CSAR
Package
SDC
Design
Time
TOSCA
Descriptor
(SDC)
X License
Model Files
Additional
Artifacts
UUID Metadata

## Slide 12
Controller Blueprint Archive file (manually in R4 only manual, or incorporated into a package? [FUTURE])
Jinja (Python-based dynamic content) Template
Velocity Template
Schema vendor specific/agnostic
Generic or Per PNF type (customized)

## Slide 13
VNF (TOSCA format) ONBOARDING PACKAGE
NF
Descriptor
NF
Registration
PM
Dictionary
Informational
Artifacts
Configuration
Files
VES Event
Registration
VNF-D
PM Dictionary
PM Schema
Manuals, Help files
Customer Doc Products
Test files
Licensing agreement
Resource
Configuration Info
Communication
Files
Ansible Playbooks
Netconf Yang model
Chef Cookbooks
VNF Onboarding Package
Manifest
File
TOSCA
Metadata
(SDC)
SDC Added Files
TOSCA
Metadata
VNF Package Artifacts (not SOL004 based)
Definition Files
Vendor Provided
SDC Service
CSAR
Package
SDC
Design
Time
TOSCA
Descriptor
(SDC)
X License
Model Files
Additional
Artifacts
UUID Metadata

## Slide 14
VNF (HEAT Template) ONBOARDING PACKAGE
Heat
Template
NF
Registration
PM
Dictionary
Informational
Artifacts
Configuration
Files
VES Event
Registration
PM Dictionary
PM Schema
Manuals, Help files
Customer Doc Products
Test files
Licensing agreement
Resource
Configuration Info
Communication
Files
Ansible Playbooks
Netconf Yang model
Chef Cookbooks
VNF Onboarding Package
Proprietary
Manifest
File
AID
Model
(SDC)
SDC Added Files
PNF Package Artifacts
Definition Files
Vendor Provided
SDC Service
CSAR
Package
SDC
Design
Time
X License
Model Files
Additional
Artifacts
UUID Metadata
#x HEAT
Template
Environment
file

## Slide 15
SDC INTERNAL PACKAGE
SDC Internal Package
TOSCA
Metadata
(SDC)
SDC Added Files
SDC Internal PNF Package Artifacts
SDC Additions
SDC Service
CSAR
Package
SDC
Design
Time
TOSCA
Descriptor
(SDC)
X License
Model Files
Additional
Artifacts
UUID Metadata

## Slide 16
R4: Modelling VES Events

## Slide 17
SDK VALIDATION - PNF ONBOARDING PACKAGE
NF
Descriptor
NF
Registration
PM
Dictionary
Informational
Artifacts
Configuration
VES Event
Registration
PNF-D
PM Dictionary
PM Schema
Manuals, Help files
Customer Docs
Test files, Licensing
Configuration Info
Communication
Ansible Playbooks
Netconf Yang model
Manifest
File
TOSCA
Metadata
PNF Package Artifacts
Definition Files
Vendor Provided – PNF Onboarding Package
TOSCA Meta
Manifest File
VNF SDK to check the PNF keywords in the MainServiceTemplate.mf (manifest) New tags are pnf_product_name and pnf_provider_id, pnf_package_version, pnf_release_date_time and non_mano_artifact_sets.
ETSI SOL004 Validation for Meta-Data file (TOSCA.meta) in PNF Package. New checks for "Entry definition, Entry-manifest, Entry-change-log, Entry-tests, Entry-certificates" is VNF SDK development work.
5
4
VNF-SDK Checks that files defined in the Manifest file (specify files & directory locations) actually exist where they have been specified in the Manifest File.
1
License
Certificate
License File Check
This is a license term file
2
Certificate File Check
3

## Slide 18
SDK VALIDATION - PNF ONBOARDING PACKAGE
NF
Descriptor
NF
Registration
PM
Dictionary
Informational
Artifacts
Configuration
VES Event
Registration
PNF-D
PM Dictionary
PM Schema
Manuals, Help files
Customer Docs
Test files, Licensing
Configuration Info
Communication
Ansible Playbooks
Netconf Yang model
Manifest
File
TOSCA
Metadata
PNF Package Artifacts
Definition Files
Vendor Provided – PNF Onboarding Package
TOSCA Meta
Manifest File
VNF SDK checks PNF keywords in the MainServiceTemplate.mf (manifest) Tags: pnf_product_name, and pnf_provider_id, pnf_package_version, pnf_release_date_time, and non_mano_artifact_sets.
ETSI SOL004 Validation for Meta-Data file (TOSCA.meta) in PNF Package. VNF-SDK checks for Entry definition, Entry-manifest, Entry-change-log, Entry-tests, and Entry-certificates
6
5
VNF-SDK checks files & directory locations defined in the Manifest file actually exist.
4
License
Certificate
License File Check
This is a license term file
2
Certificate File Check
3

## Slide 19
VNF
SDK
PNF CSAR Package
(Vendor onboarded)
VSP [vendor s/w product]
SDC
Design Studio
SDC Internal CSAR
PNF Package
SDC
Catalog
NF
Registration
PM
Dictionary
Deployment Section
To Attach Artifacts
SDC Service
CSAR Package
PNF PACKAGES
Deployment
Studio
SDC
Catalog
VNF 1. TOSCA / 2. AID Model

## Slide 20
VNF
SDK
PNF Package
(Vendor onboarded)
VSP [vendor s/w product]
SDC
Design Studio
SDC Internal CSAR
PNF Package
SDC
Catalog
SDC Service
CSAR Package
PNF PACKAGES
Deployment
Studio
SDC
Catalog

## Slide 21
PNF Onboarding Package (CSAR)
Scripts
ChangeLog.txt
Tests
MainServiceTemplate.cert
Images
PNF
Onboarding
(CSAR file)
ROOT
MainServiceTemplate.mf
MainServiceTemplate.yaml
TOSCA-Metadata
Definitions
TOSCA.meta
Artifacts
…
Configuration
Deployment
Yang_module
Measurements
Events
ves-dictionary.yaml
yang-module.yang
pm-dictionary.yaml
Install.csh
NF descriptor
License_term.txt
metadata:
pnf_product_name: gNB
pnf_provider_id: Ericsson
pnf_package_version:1.0
pnf_release_date_time:2018-12-03T08:44:00-05:00
non_mano_artifact_sets:
Events:
source: Artifacts/Deployment/Events/VES_registration.yaml
Note:
Package Example
Not all files are listed.
Folder / file name in blue is requested by SOL004.
Folder / file name in black is example only.
…
TOSCA-Meta-Version: 1.0
CSAR-Version: 1.1
Created-By: Ericsson (Zu Qiang 2018-12-03)
Entry-Definitions: Definitions/MainServiceTemplate.yaml
Entry-Manifest: MainServiceTemplate.mf
Entry-Change-Log: Artifacts/ChangLog.txt
Entry-Tests: Artifacts/Tests
Entry-Certificate: Artifacts/License_term.txt
Not supported by ONAP Casablanca
Not used
yet

## Slide 22
R4: Modelling VES Events
SOL004 required PNF manifest file
metadata: ######################### New key Name to be supported by SDC
pnf_product_name: gNB
pnf_provider_id: Ericsson
pnf_package_version:1.0
pnf_release_date_time:2018-12-03T08:44:00-05:00
######################### non mano artifact sets to be supported by SDC
non_mano_artifact_sets:
Events:
source: Artifacts/Deployment/Events/VES_registration.yaml
Measurements:
source: Artifacts/Deployment/Measurements/PM_Dictionary.yaml
Yang_module:
Source: Artifacts/Deployment/Yang_module/Yang_module.yaml
Others:
Source: Artifacts/Informational/scripts/install.sh
Source: Artifacts/Informational/user_guide.txt
Source: Artifacts/Other/installation_guide.txt
Source: Artifacts/Other/review_log.txt
PNF ONBOARDING FILES – Manifest file Example

## Slide 23
R4: Modelling VES Events
VNFSDK #4 Manifest file: new PNF tags
metadata:
pnf_product_name: gNB
pnf_provider_id: CompanyXYZ
pnf_package_version: 1.0
pnf_release_date_time: 2019-02-11T09:10:00-05:00
non_mano_artifact_sets:
Events:
source: Artifacts/Deployment/Events/VES_registration.yaml
Measurements:
source: Artifacts/Deployment/Measurements/PM_Dictionary.yaml
Yang_module:
Source: Artifacts/Deployment/Yang_module/Yang_module.yaml
Others:
Source: Artifacts/Informational/scripts/install.sh
Source: Artifacts/Informational/user_guide.txt
Source: Artifacts/Other/installation_guide.txt
Source: Artifacts/Other/review_log.txt
PNF ONBOARDING FILES – Main Service Template manifest (.mf) file
VNF SDK to check the PNF keywords in the MainServiceTemplate.mf New tags are pnf_product_name and pnf_provider_id, pnf_package_version, pnf_release_date_time and non_mano_artifact_sets.

## Slide 24
R4: Modelling VES Events
SOL004 required TOSCA.meta file
TOSCA-Meta-File-Version: 1.0
CSAR-Version: 1.1
Created-By: Ericsson
Entry-Definitions: Definitions/resource-Ericssongnodeb-template.yml
Entry-Manifest: resource-Ericssongnodeb-template.mf
Entry-Certificate: Artifacts/resource-Ericssongnodeb-template.cert
Entry-Tests: Artifacts/Tests
Entry-Licenses: Artifacts/Licenses/license_term.txt
Entry-Change-Log: Artifacts/ChangeLog.txt
PNF ONBOARDING FILES – Tosca Metadata File

## Slide 25
R4: Modelling VES Events
VNFSDK Task #5 TOSCA Meta file checks
TOSCA-Meta-Version: 1.0
CSAR-Version: 1.1
Created-By: CompanyXYZ (User123 2019-02-11)
Entry-Definitions: Definitions/MainServiceTemplate.yaml
Entry-Manifest: MainServiceTemplate.mf
Entry-Change-Log: Artifacts/ChangLog.txt
Entry-Tests: Artifacts/Tests
Entry-Certificate: Artifacts/License_term.txt
PNF ONBOARDING FILES – TOSCA Meta File Checks
ETSI SOL004 Validation for Meta-Data file & Manufacturer file (TOSCA.meta file) in PNF Package. New checks for "Entry definition, Entry-manifest, Entry-change-log, Entry-tests, Entry-certificates" would be new VNF SDK development work.
"TOSCA-Meta-Version" and "CSAR-Version" and "Created by" checks are already supported.

## Slide 26
SDC Service CSAR Package
Informational
ChangeLog.txt
Tests
MainServiceTemplate.cert
Images
CSAR file
ROOT
MainServiceTemplate.mf
MainServiceTemplate.yaml
TOSCA-Metadata
Definitions
TOSCA.meta
Artifacts
Deployment
Not supported by ONAP Casablanca
NF descriptor
created by SDC
MainServiceTemplate.yaml
Copy of NF descriptor
HEAT
HEAT_VOL
HEAT_NET
HEAT_ENV
HEAT_ARTIFACT
HEAT_NESTED
YANG_XML
VNF_CATALOG
MODEL_INVENTORY_PROFILE
VNF_LICENSE
VENDOR_LICENSE
APPC_CONFIG
VF_MODULES_METADATA
DCAE_TOSCA
DCAE_JSON
PLAN
GUIDE
…
Install.csh
Other
VFC[name]
Any unrecognized artifacts
VFC[name]/Deployment
VFC[name]/Information
(can we move it in Deployment dir ?)
Not supported by ONAP Casablanca
Directoriy list under review
NF_ONBOARDED_PACKAGE
Directoriy list under review
VSP CSAR File
VF/Resource CSAR file
PNF/Resource CSAR file
SDC Service CSAR file >1 Resource file

## Slide 27
SDC
Catalog
Resource CSAR File (PNF) onboarded
PNF Package Version 2019-1.1
SDC adds files
SDC add vendor meta-data
Internal CSAR file
Structure change
Information missing
Metadata file changed (generated by SDC) not have info on left side
Manufactured metafile is lost
Certain artifacts is lost.
CSAR.meta (added by SDC) … what is it for?
Definition File (define policies) added by SDC
Resource UUID
WHAT WOULD BE A PROBLEM
WHAT DOES THE VENDOR NEEDS TO PROVIDE
WHAT DOES SDC need
Today in PNF descriptor more than 3 properties
In SDC PNF CSAR only 3 properties NF function, NF role, NF type, SWVersions
PNF onboarding package from SOL001 MANY properties
ARTIFACTS SOL004 MANY artifacts add
In Current PNF CSAR file no place to hold it.
Vendor provided
SDC
Heat File
OPENO TOSCA

## Slide 28
Resource CSAR File (VF) generated from VSP
Resource CSAR File (PNF) onboarded (SDC)
Resource CSAR File (PNF) onboarded (SDC)
Resource CSAR File (VF) generated from VSP
SDC Service CSAR File
(SDC distributes to other ONAP RT components)
Resource CSAR File (PNF) onboarded (SDC)
NF Descriptor
Descriptor (Interface connections)
Artifacts (incl. Onboarded Package)
SDC doesn’t recognized SOL001 Modeling vs Platform Data Model
SOL004 artifacts some artifacts dropped by SDC
name NF (naming policy)
TOSCA API to ingest CSAR package > same APIs to have clients ingest PNFs > onboarding of PNF packages.
NETWORK ASSIGNMENTS VLAN tag assignment,, IP assignments > Plug & play
PNF Package Version 2019-1.1
SDC PNF Package Version 2.6
SDC Service Package Version 1.5
SDC
Catalog

## Slide 29
Onboarded Package to SDC Internal Mapping
MainServiceTemplate.mf *
ROOT
PNF Onboarding Package (Vendor CSAR)
SDC Service CSAR
TOSCA.meta
MainServiceTemplate.mf
ROOT
Vendor Manifest File
Manifest File
(SDC created)
TOSCA-Metadata
TOSCA.meta
TOSCA-Metadata
TOSCA Meta-data file
TOSCA Meta-data file
(SDC created)
pm-dictionary.yaml
Artifacts/Deployment
Measurements
Performance Measure
Dictionary & Schema
Performance Measure
PM Dictionary & Schema
(Vendor Provided)
pm-dictionary.yaml
Artifacts
NF_ONBOARDED_PACKAGE
Artifacts/Deployment
Measurements
Performance Measure
PM Dictionary & Schema
(SDC Internal)
pm-dictionary.yaml
Artifacts
Deployment
ves-dictionary.yaml
Artifacts/Deployment
Events
VES Dictionary
(YAML)
ves-dictionary.yaml
Artifacts
Events
ves-dictionary.yaml
Artifacts
NF_ONBOARDED_PACKAGE
Artifacts/Deployment
Events
PNF Registration File
VES Event definitions
(Vendor Provided)
PNF Registration File
VES Event definitions
* Paths defined by manifest file

## Slide 30
PRE-ONBOARDING PROCESSES
Asset Manager
Platform Model
Onboarding
Asset Manager
NF Descriptor
Pre Onboarding
ONBOARDING PROCESSES

## Slide 31
PRE-ONBOARDING: VNF SDK DEVELOPMENT
PNF
Onboarding
Package
NF
Descriptor
NF
Registration
Informational
Artifacts
Configuration
Files
VES Event
Registration
Specification
PNF-D
Manuals, Help files
CustDoc Products
Test files
Licensing agreement
Configuration Info
Package
creation
VNF
SDK
WinZIP
Validating Content
Communication
Files
Ansible Playbooks
Netconf Yang model
Chef Cookbooks
Dublin Priority
Dublin Priority
PM Dictionary
PM Schema
PM Dictionary
PM Schema
2. PNF Pre-Onboarding (optional): VNF-SDK ( ) can create or validate PNF Onboarding Package
2

## Slide 32
PNF ONBOARDING: SDC Catalog
SDC
Catalog
Onboarding
PNF
Onboarding
Package
+VENDOR
META DATA
NF
Descriptor
NF
Registration
Informational
Artifacts
Configuration
Files
SDC
VES Event
Registration
Specification
PNF-D
Manuals, Help files
CustDoc Products
Test files
Licensing agreement
Configuration Info
Package
creation
xNF
SDK
WinZIP
Validating Content
Communication
Files
Dublin Priority
Dublin Priority
PM Dictionary
PM Schema
PM Dictionary
PM Schema
3. PNF Onboarding: PNF Package is loaded
3
Ansible Playbooks
Netconf Yang model
Chef Cookbooks

## Slide 33
VNFD ETSI SOL001 based
Heat template
VOLTE workflow
vCPE CreateVcpeWorkflow
Pre-onboarding
Onboarding
Design Time
VNF
SOL001
Vendor VNF CSAR
VNF heat template
vCPE Create&ActivateWorkflow
PNF defined by UI
AI
AID
xNF ONBOARDING Dependencies R3
TOSCA AID VNF
TOSCA AID PNF
SDC
SO
SDNC/APPC
Multi-VIM
VFC
VNF SDK

## Slide 34
VNFD, PNFD ETSI SOL001
Heat template
VOLTE workflow
vCPE CreateVcpeWorkflow
Pre-onboarding
Onboarding
Design Time
VNF
SOL001
TOSCA AID VNF
Vendor VNF CSAR
VNF heat template
vCPE Create&ActivateWorkflow
TOSCA AID PNF
PNF defined by UI
AI
AID
xNF ONBOARDING Dependencies R4
Vendor PNF CSAR
PNF SOL001
SDC
SO
SDNC/APPC
Multi-VIM
VFC
VNF SDK

## Slide 35
DESIGN TIME & SDC
Service Designer
SDC CSAR Pkg
Design Time

## Slide 36: NFV Release 2: stage 2 and stage 3 specification summary
NFV-IFA 005
NFV-IFA 006
NFV-IFA 007
NFV-IFA 008
NFV-IFA 013
NFV-IFA 004
(Acceleration)
NFV-IFA 011
(VNF Pkg)
NFV-IFA 014
(NS templates)
NFV-IFA 010
(NFV-MANO Functional Reqs)
NFV-IFA 015
(NFV Information Model Report)
+
NFV-IFA 016 (Papyrus Guidelines),
NFV-IFA 017 (UML Modeling Guidelines),
NFV-IFA 024 (NFV Information Model External Touchpoints)
NFV-IFA 002
(Acceleration)
NFV-IFA 003
(Acceleration)
NFV-TST 008
(NFVI metrics)
NFV-SOL 003
NFV-SOL 002
NFV-SOL 001
NFV-SOL 006
(VNF and NS
Descriptors)
NFV-SOL005
(*) Release 2 Stage 3 work items in “green”
SOL004
(VNF Packaging)
NFV-SOL007 (NSD file structure)
Published!
Status as of Apr. 2018
PNF package impacts
PNF Descriptor impacts

## Slide 37
NF Registration (YAML) Onboarding
PNF Descriptor (ETSI SOL 001)
PNF
Properties:
NODE
DependsOn
PnfExtCp
NODE
VirtualLinkable
Capabilities
Requirements
LEGEND:
PNFD Service Template
NsVirtualLink
VirtualLinkable
Application (NF)
Infrastructure (H/W)
PNFD
Abstract
VirtualLinkable
Substituted by

## Slide 38
NF Registration (YAML) Onboarding
DsnTm: PNFD > ONAP Platform Model
PNF
Properties:
NODE
DependsOn
PnfExtCp
NODE
VirtualLinkable
Capabilities
Requirements
LEGEND:
PNFD DESCRIPTOR
Ns Virtual
Link
VirtualLinkable
Service
TOSCA Root
Node
Network
Function
Virtual
Link
PNF
Device
Connection
Point
NF
Component
Complex
Ports / NICs
Connectivity
N
1
1
1
N
1
PLATFORM MODEL (INTERNAL MODEL)
4 Design Time Activities: NF Onboard Package > SDC catalog
4

## Slide 39
SDC AID (Architecture Integration Document) Internal Model
PNF
Properties:
NODE
DependsOn
PnfExtCp
NODE
VirtualLinkable
Capabilities
Requirements
LEGEND:
PNFD DESCRIPTOR
Ns Virtual
Link
VirtualLinkable
NF Registration (YAML) Onboarding
4 Design Time Activities: NF Onboard Package > SDC catalog
4
DsnTm: PNFD > SDC AID

## Slide 40
Design-Time Process
Service
Designer
SDC
Catalog
Onboarding
Policy
Designer
Workflow
Studio
CLAMP
Designer
Add
Policies
Add
Workflows
Define
Services
Add Control
Loops
A&AI
DCAE
SO
Controller
ONAP
RUN-TIME
DESIGN-TIME (SDC)
NF
Onboarding Package
Vendor MetaData
Policy
Database
DCAE
Design Studio
Define
Templates
SDC
Distribute
CSAR
Analytics
Service Orchestration
APP-C, SDN-C
Inventory, Listener
CSAR
Package
DCAE Inventory
P
Descriptor
NF Registration
Certification
Studio
Deployment
Studio

## Slide 41
Defining a Service
Virtual
Link
Connection
Point
HEAT
Templates
Informational
Artifacts
Deployment
Artifacts
Blueprints
Policies
Configuration
Files
Templates
SERVICE
VNF
PNF
ANF
(Allotted)
Resources
User Designed
Vendor Provided
Foundational
P
4 Design Time Activities: Designing a Service
4
SDC Service CSAR
Package
Distribute

## Slide 42
R4: 5G Base Station (gNodeB)
DU
CU
(VNF)
DU
RAU
CU
N
1
UPF
(VNF)
AMF
(VNF)
RAN Network Elements
Core Network Elements
N
1
1
N
VNF/CU #1
Conn Pt #1
Conn Pt #3
Conn Pt #n
PNF/DU #n
PNF/DU #1
Virtual Link
5G SERVICE
Resources
…
User Plane Connection

## Slide 43
VNF Requirements
Asset Manager
NF Descriptor
Onboarding

## Slide 44
VNF Requirement extension for PNF
VNFRQTS-506: Supporting PNF package onboarding
  VNFRQTS-507: Project scope to include PNF
  VNFRQTS-508: Add PNFD requirements
  Section 5.1.6:
    VNFRQTS-499: PNF onboarding CSAR package structure based SOL004
    VNFRQTS-497: Adding package security requirements
  Section 7.2:
    Clarifications on the documentation requirements
    VNFRQTS-505: PNF onboarding package artifacts
    VNFRQTS-498: Add VES Event Registration requirement to PNF package
    Clarifications on artifacts structure requirements
    VNFRQTS-496: supporting Ansible protocol in PNF

## Slide 45
ONAP VNF Descriptor (5.1.9) Requirements
R number | Description | Comments
R-35854 | The VNF Descriptor (VNFD) provided by VNF vendor MUST comply with TOSCA/YAML based Service template for VNF descriptor specified in ETSI NFV-SOL001. | Shall applicable to PNFD
R-65486 | The VNFD MUST comply with ETSI GS NFV-SOL001 document endorsing the above mentioned NFV Profile and maintaining the gaps with the requirements specified in ETSI GS NFV-IFA011 standard. | Shall applicable to PNFD
R-17852 | The VNFD MAY include TOSCA/YAML definitions that are not part of NFV Profile. If provided, these definitions MUST comply with TOSCA Simple Profile in YAML v.1.2. | Shall applicable to PND
R-46527 | A VNFD is a deployment template which describes a VNF in terms of deployment and operational behavior requirements. … including topology, deployment aspect, and VNF lifecycle management (LCM) operations | PNF LCM is not defined yet
R-15837 | The major TOSCA Types specified in ETSI NFV-SOL001 standard draft | 
R-54356 R-54876 | VNF Data Types | CpProtocolData AddressData L2AddressData L3AddressData LocationInformation CivicAddressElement
R-67895 | VNF Capability Types | VirtualLinkable
R-95321 | VNF Relationship Types | VirtualLinksTo
R-32155 | VNF Interface Types | 
 |  | PNF Node Types: PNF, PnfExtCp, Cp
 |  | PBF Policy Types

## Slide 46
ONAP VNF CSAR Package (5.1.6) Requirements
R number | Description | Comments
R-51347 | The VNF package MUST be arranged as a CSAR archive as specified in TOSCA Simple Profile in YAML 1.2. | Shall applicable to PNF package
R-87234 | The VNF package provided by a VNF vendor MAY be either with TOSCA-Metadata directory (CSAR Option 1) or without TOSCA-Metadata directory (CSAR Option 2) as specified in ETSI GS NFV-SOL004. On-boarding entity (ONAP SDC) must support both options. Note: SDC supports only the CSAR Option 1 in Casablanca. The Option 2 will be considered in future ONAP releases, | Shall applicable to PNF package
R-10087 | The VNF package MUST contain all standard artifacts as specified in ETSI GS NFV-SOL004 including Manifest file, VNFD (or Main TOSCA/YAML based Service Template) and other optional artifacts. CSAR Manifest file as per SOL004 - for example ROOT\ MainServiceTemplate.mf | Shall applicable to PNF package
R-01123 | The VNF package Manifest file MUST contain: VNF package meta-data, a list of all artifacts (both internal and external) entry’s including their respected URI’s, an algorithm to calculate a digest and a digest result calculated on the content of each artifacts, as specified in ETSI GS NFV-SOL004. The VNF Package MUST include VNF Identification Data to uniquely identify the resource for a given VNF provider. The identification data must include: an identifier for the VNF, the name of the VNF as was given by the VNF provider, VNF description, VNF provider, and version. | Shall applicable to PNF package With new valid names/values pnf_provider_id pnf_product_name pnf_release_date_time pnf_package_version
R-21322 | The VNF provider MUST provide their testing scripts to support testing as specified in ETSI NFV-SOL004 - Testing directory in CSAR | Should applicable to PNF package
R-26885 | The VNF provider MUST provide the binaries and images needed to instantiate the VNF (VNF and VNFC images) either as: Local artifact in CSAR: ROOT\Artifacts\ VNF_Image.bin externally referred (by URI) artifact in Manifest file (also may be referred by VNF Descriptor) Note: Currently, ONAP doesn’t have the capability of Image management, we upload the image into VIM/VNFM manually. | May applicable to PNF package Not supported with current release
R-40820 | The VNF provider MUST enumerate all of the open source licenses their VNF(s) incorporate. CSAR License directory as per ETSI SOL004. for example ROOT\Licenses\ License_term.txt | May applicable to PNF package
R-xxxxx | VNF Package Authenticity | May applicable to PNF package

## Slide 47
PNF on-boarding requirements (7.2)
R number | Description | Comments
R-77707 | The xNF provider MUST include a Manifest File that contains a list of all the components in the xNF package | OK. Overlapped with R-10087 in section 5.1.6.3
R-66070 | The xNF Package MUST include xNF Identification Data to uniquely identify the resource for a given xNF provider. The identification data must include: an identifier for the xNF, the name of the xNF as was given by the xNF provider, xNF description, xNF provider, and version. | Part of the descriptor
R-98617 | The xNF provider MUST provide information regarding any dependency (e.g., affinity, anti-affinity) with other xNFs and resources. | Part of the descriptor
R-22346 | The VNF package MUST provide VES Event Registration for all VES events provided by that xNF. | VES event Registration Should be applicable to PNF
R-89571 | The xNF MUST support and provide artifacts for configuration management using at least one of the following technologies; a) Netconf/YANG, b) Chef, or c) Ansible. | 
R-30278 | The xNF provider MUST provide a Resource/Device YANG model as a foundation for creating the YANG model for configuration. This will include xNF attributes/parameters and valid values/attributes configurable by policy. | 
R-27711 | The xNF provider MUST provide an XML file that contains a list of xNF error codes, descriptions of the error, and possible causes/corrective action | Not the proposed FM dictionary
R-74763 | The xNF provider MUST provide an artifact per xNF that contains all of the xNF Event Records supported. The artifact should include reference to the specific release of the xNF Event Stream Common Event Data Model document it is based on. (e.g., VES Event Listener) | VES event Listener
R-35851 | The xNF Package MUST include xNF topology that describes basic network and application connectivity internal and external to the xNF including Link type, KPIs, Bandwidth, latency, jitter, QoS (if applicable) for each interface. | Part of the descriptor?
R-26881 | The xNF provider MUST provide the binaries and images needed to instantiate the xNF (xNF and VNFC images). | Not supported by Casablanca
R-96634 | The xNF provider MUST describe scaling capabilities to manage scaling characteristics of the xNF. | Not supported by PNF
R-04298 | The xNF provider MUST provide their testing scripts to support testing. | Testing Requirements.
R-58775 | The xNF provider MUST provide software components that can be packaged with/near the xNF, if needed, to simulate any functions or systems that connect to the xNF system under test. This component is necessary only if the existing testing environment does not have the necessary simulators. | 
R-85653 | The xNF MUST provide metrics (e.g., number of sessions, number of subscribers, number of seats, etc.) to ONAP for tracking every license. | Only if Licensing is needed
R-40827 | The xNF provider MUST enumerate all of the open source licenses their xNF(s) incorporate. | 
R-85991 | The xNF provider MUST provide a universal license key per xNF to be used as needed by services (i.e., not tied to a VM instance) as the recommended solution. The xNF provider may provide pools of Unique xNF License Keys, where there is a unique key for each xNF instance as an alternate solution. Licensing issues should be resolved without interrupting in-service xNFs. | 
R-47849 | The xNF provider MUST support the metadata about licenses (and their applicable entitlements) as defined in this document for xNF software, and any license keys required to authorize use of the xNF software. This metadata will be used to facilitate onboarding the xNF into the ONAP environment and automating processes for putting the licenses into use and managing the full lifecycle of the licenses. | 

## Slide 48
Q&A

## Slide 49
REFERENCES / APPENDIX / BACKUP SLIDES
Benjamin Cheung, PhD

## Slide 50
NF ONBOARDING ARTIFACTS
DEPLOYMENT ARTIFACT

## Slide 51
INFORMATIONAL ARTIFACTS
INFORMATION
ARTIFACT
(SDC Design Studio)
Cloud Questionnaire
Features
Vendor Test Scripts
Resource Security Template
HEAT Template (Vendor)
Capacity Descriptive
Other Informational Artifacts

## Slide 52
VNF SDK Updates
Benjamin Cheung, PhD
Asset Manager
NF Descriptor
Onboarding

## Slide 53
SDK ENHANCEMENTS

## Slide 54
SDK ENHANCEMENTS

## Slide 55
VNF SDK Impacts
VNFSDK-337: Supporting PNF package onboarding
  VNFSDK-338: Project scope to include PNF
  VNFSDK-339: PNF CSAR structure based SOL004
  VNFSDK-340: PNF manifest file
  VNFSDK-341: PNFD validation based on SOL001
  VNFSDK-342: Support packaging security
  VNFSDK-343: Enhancement of the test on PNF package

## Slide 56
PLATFORM MODEL / MODELING A SERVICE
Benjamin Cheung, PhD
Service Designer
Platform Model
Design Time

## Slide 57
Platform Data Model
Service
TOSCA Root
Node
VNF
Virtual
Link
PNF
Connection
Point
NF
Component
Complex
Ports / NICs
Connectivity
N
1
1
1
N
1
Design time view of a service
Internal representation of a model
Onboarding Model > SDC produces
Compute Host

## Slide 58
PNF
VNF
NF
Capabilities
Requirement
Capabilities
Requirement
Platform (Internal) Information Model
ANF
Assign [connections pts]
Create
Configure
Create “PNF”
Assign (registers)/connpts
Configure

## Slide 59
NF Registration (YAML) Onboarding
PNF Descriptor > ONAP Platform Model
PNF
Properties:
NODE
DependsOn
PnfExtCp
NODE
VirtualLinkable
Capabilities
Requirements
LEGEND:
PNFD DESCRIPTOR
Ns Virtual
Link
VirtualLinkable
PLATFORM MODEL (INTERNAL MODEL)
PNF
VNF
NF
ANF

## Slide 60
Policy Example
SDC
Catalog
Onboarding
Policy
Designer
Add
Policies
DCAE
Service Change
Handler
DCAE
(Run Time)
DESIGN-TIME (SDC)
PNF
Onboarding Package
Policy
Database
SDC
Distribute
CSAR
CSAR
Package
CLAMP
Designer
Add Control
Loops
DCAE
Design Studio
Define
Templates
DCAE
Controller
DCAE
Inventory
PNF
VNF
VES
Event
DCAE
Collector
Micro
Service
P
P
P
P
Policy
Engine
P
Controller
P
Ticketing
P
DMaaP
P
DMaaP
Descriptor
NF Registration
A&AI
Fault Domain

## Slide 61
Onboarding and Design Time

## Slide 62
5G RAN Wireless Systems
Benjamin Cheung, PhD

## Slide 63
3GPP Release 15, IMT-2020 = 5G
Virtual and Augmented Reality
Smart City
Geographically spread devices
Smart Automated Vehicle Control
Remote Surgery and Examination
Factory Automation
Industry 4.0
Remote Device Control
Internet of Things (IoT)
M2M communications
Smart Infrastructure
Broadband Experience Everywhere Anytime
Media Anywhere
eMBB (enhanced Mobile Broadband)
URLLC (Ultra Reliable Low Latency Communications)
mMTC (massive Machine Type Communications)
Smart
Connected
Collaborate
Access
Interactive
Aware

## Slide 64
5G Key Technology Components
New Spectrum (Rel 15, 52.6 GHz/39 GHz, Rel 16 > 52.6 GHz)
Advanced
Beamforming
Multi-Connectivity (NSA, SA, Option 3, 4, 7)
Network Slicing
Edge Computing
Software Defined Networking (SDN)
Network Functions Virtualization (NFV)
Fog Computing (FC)
Mobile Edge Computing (MEC)

## Slide 65
5G RAN Wireless Systems & ONAP
Benjamin Cheung, PhD

## Slide 66
5G RAN Wireless Network
5G
Application
Ecosystem
UE
RU
DU
CU
Internet
Edge
Cloud
Antenna
DU
RAU
External Content
RU – Remote Radio Unit
DU – Distributed Unit (5G Base Unit)
CU – Centralized Unit
CPRI
Mid Haul
Back Haul
Centralized
Cloud
Disaggregated Core
UPF
SMF
UDM
AUSF
UPF – User Plane Function
SMF – Session Management Function
UDM – Unified Data Management Function
AUSF – Authentication Service Function
RAN Network Elements
Core Network Elements
ONAP Run Time Management
SO
SDN-C
DCAE
A&AI
OSS
BSS
APP-C
SO – Service Orchestrator
SDN-C – Service Design Network Controller
DCA&E – Data Collection Analytics & Events
A&AI – Available & Active Inventory
APP-C – Application Control
CU-CP (ONAP)
CU-UP
RAP
RF
AMF

## Slide 67
R4: Modeling a 5G Service
Virtual
Link
Connection
Point
HEAT
Templates
Informational
Artifacts
Deployment
Artifacts
Blueprints
Policies
Configuration
Files
Templates
5G SERVICE
Network
Function (VNF)
Network
Function PNF
Resources
User Designed
Vendor Provided
Foundational
PNF
Device
P

## Slide 68
R4: 5G Base Station (gNodeB)
DU
CU
(VNF)
DU
RAU
CU
N
1
UPF
(VNF)
AMF
(VNF)
RAN Network Elements
Core Network Elements
N
1
1
N
NF/CU #1
Conn Pt #1
Conn Pt #3
Conn Pt #n
PNF/DU #n
PNF/DU #1
Virtual Link
5G SERVICE
Resources
…
ANF

## Slide 69
Configurations
Benjamin Cheung, PhD

## Slide 70
MODELING WITHIN A PNF (DU)
5G DU
(PNF)
Sub-Component #1
Sub-Component #2
Sub-Component #n
SFP #1 = Port #1
SFP #n = Port #n
PNF
Device
Connection
Point
Ports / NICs
NF
Component
Network
Function
Software Function of a DU
“Hardware Aspects of a PNF”
Sub-components within PNF
The hardware Ports
(e.g. SFP/Backhaul Ports)
FUTURE
NF PNF – “Application” S/W does 5G voice/data
N/F Node Type
Hardware PNF - Modem (5G DU) [Hardware]
H/W Node Type

## Slide 71
DU
5G DU
(PNF)
Version 2018-09A
Version 2018-09B
PNF
Version 2018-09A
Version 2018-09B
SUBCOMPONENTS (R4+)
DRIVE PARTITIONS
Partition1 (Active)
Partition2 (Inactive)
Sub-Component-1
Sub-Component-2
PNF
Version LTE2018-09A
Version 2018-09B
TANDEM CHASSIS CONFIGURATIONS
Sub-Frame DU#1
Sub-Frame DU#2
DU
MULTI-PNF
DAISY CHAIN CONFIG
DU
DU
DU
4G PNF
5G PNF
DU
5G PNF
Version 2018-09B
Sub-Frame DU#2
Version 2018-09A
Version 2018-09A
DU Configurations
Sub-component
(e.g. Circuit Pack)

## Slide 72
ETSI (SOL 001, SOL 004, SOL005, SOL 007)
Benjamin Cheung, PhD

## Slide 73
ETSI SOL Standards

## Slide 74
SO
Legacy NFV-O
SOL003
VNFM
SOL005
SDC
SOL004 CSAR
SOL001 VNF-D & NS-D
Onboarding
SOL001
NS-D
NFVO
VNFM
SOL003 & SOL001
VNF-D
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
App-C / GNF-C
SOL002
SOL002
SOL002
Legacy OSS
SOL 005
SOL001 NS-D
ETSI SOL Standards Alignment

## Slide 75: VNFD/PNFD/NSD properties alignment
PNFD | VNFD | NSD | Comments
descriptor_id | descriptor_id | descriptor_id | 
version | descriptor_version | descriptor_version | Proposed new name in PNFD: descriptor_version
provider | provider | provider | 
name | product_info_name | name | Better to be aligned. Proposed new name in VNFD: name
- | software_version | software_version | New in PNFD 1. Better to align with VNFD. VNFD uses software_version for only software change. descriptor_id might be changed only due to descriptor evolution itself like security adding. 2. Long-term view, it would be useful to upgrade PNF software. 3. It is also useful for service provider to get such information for OAM view like trouble-shooting, service checking, PNF packability checking and so on 4. Align with ONAP model
function_description | product_info_description | - | Proposed new name in VNFD: function_description. Add function_description into NSD
descriptor_invariant_id | product_name | invariant_id | Proposed new name in VNFD / PNFD: invariant_id
geographical_location_info | - | - | 
On-going ETSI discussion

## Slide 76: SOL004 expanded scope option
Tentative updated SOL004 title : “Network Functions Virtualisation (NFV) Release 2; Protocols and Data Models; VNF Package specification and PNF file specification”
Tentative updated scope: The present document specifies the structure and format of a VNF package file and its constituents, fulfilling the requirements specified in ETSI GS NFV-IFA 011 [1] for a VNF package and in ETSI GS NFV-IFA 014 [x] for a PNFD.
Working schedule:
Milestone name | Target date
CR approval with expanded scope of 2.6.1 | 2018/12/07
Functional CRs approved | 2018/12/13
WG approval | 2018/12/31
TB approval | 2019/01/31
On-going ETSI discussion

## Slide 80
Just in time instantiation of resources
VNFD
U/C deploy VNFC in K8S dynamically provision the platform.
NFIaaS
Inventory; order, capacity
RACK of H/W
redfishAPI, RestFUL API envelope of specification (TOSCA)
Declarative,
Physical infrastructure manager
Multicloud layer
IaaS , Service based style-guide
Aws azure
PNF Box, NF, composition API dynamically created.
Scarce res composable infrastructure multi-tenacy. Compose/resize.

## Slide 81
TOSCA
Metadata
(SDC)
TOSCA
Descriptor
(SDC)
X License
Model Files
Additional
Artifacts
UUID Metadata
SDC Internal Package